## Slide 1: Handout # 2: Course Logistics and Introduction
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
yganjali@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali
CSC 2229 – Software-Defined Networking

## Slide 2: Today
Outline
  What this course is about
Logistics
  Course structure, evaluation
  What is expected from you
  What you want to know
Overview
  Packet switching systems
  Software-Defined Networking

## Slide 3: CSC229: Software-Defined Networking
Graduate level course
  Introduction to Software-Defined Networking (SDN)
  SDN challenges and opportunities
Course components
  Lectures
  Research papers
  Research project
Theory + Practice
  Switching systems are simple enough for us to prove something about them
  Yet they are complex enough to work in practice

## Slide 4: Outline – Part I
Introduction
  Packet switch systems
  Evolution of the Internet, and Internet routers
  Basic architectural components
  Some example architectures
Software-Defined Networking
  Innovation in computer networks
  Control vs. data plane

## Slide 5: Outline – Part II
SDN Challenges and Opportunities
  Controller and switch design
  Reliability, efficiency, and scalability
  Architecture
  Programming, correctness, and debugging
  SDN security
  New abstractions, state management
  Network services
  Network function virtualization
  Network optimization

## Slide 6: Logistics
Class location: moved to BA5205 starting the 2nd week
Office hours
  Mon. 12 PM - 1 PM, BA5238
  Or by appointment
Course web page
  http://www.cs.toronto.edu/~yganjali/courses/csc2229/
  Please check regularly for announcements.
Class mailing list
  Based on e-mail address you provide in class.
  Send me an e-mail if you don’t receive a welcome message from that list by the end of today.
  Please post (course-related!) questions to this list.

## Slide 7: Logistics
Prerequisites
  Any introductory course on networking
  Algorithms
  Basic probability theory
Papers
  Will be listed on class web page
  Please read suggested papers BEFORE class

## Slide 8: Logistics
Grading
  Active participation in class and discussions: 10%
  Paper presentations: 30%
  Final project: 60%
    Proposal: 5% - 1-2 pages
    Intermediate report: 10% - 3 pages
    Presentation: 15% - Last week of classes
    Final report: 30% - 6 pages
Deadlines
  5% deduction for each day of delay, up to 4 days.
  Exception: final report deadline is hard.

## Slide 9: Logistics
Final Project
  Groups of three students
  Project topic
    Choose from the offered list; or
    Talk to me and define your own

## Slide 10: Logistics
Academic Integrity
  All submissions must present original, independent work.
  We take academic offenses very seriously.
  Please read
    “Guideline for avoiding plagiarism”
    http://www.cs.toronto.edu/~fpitt/documents/plagiarism.html
    “Advice about academic offenses”
    http://www.cs.toronto.edu/~clarke/acoffences/

## Slide 11: Logistics
Accessibility Needs
  The University of Toronto is committed to accessibility. If you require accommodations or have any accessibility concerns, please visit http://studentlife.utoronto.ca/accessibility as soon as possible.

## Slide 12: Acknowledgements
Special thanks to:
  Prof. Nick McKeown, Stanford University
  Prof. Balaji Prabhakar, Stanford University
  Prof. Jennifer Rexford, Princeton University
  Prof. Nick Feamster, University of Chicago

## Slide 13: Questions?
What else do you like to know
about this course?

## Slide 14: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 15: What is Routing?
R3
A
B
C
R1
R2
R4
D
E
F
R5
R5
F
R3
E
R3
D
Next Hop
Destination
D

## Slide 16: What is Routing?
R3
A
B
C
R1
R2
R4
D
E
F
R5
R5
F
R3
E
R3
D
Next Hop
Destination
D
16
32
4
1
Data
Options (if any)
Destination Address
Source Address
Header Checksum
Protocol
TTL
Fragment Offset
Flags
Fragment ID
Total Packet Length
T.Service
HLen
Ver
20 bytes

## Slide 17: What is Routing?
A
B
C
R1
R2
R3
R4
D
E
F
R5

## Slide 18: Points of Presence (POPs)
A
B
C
POP1
POP3
POP2
POP4
D
E
F
POP5
POP6
POP7
POP8

## Slide 19: Where High Performance Routers are Used
R10
R11
R4
R13
R9
R5
R2
R1
R6
R3
R7
R12
R16
R15
R14
R8
(2.5 Gb/s)
(2.5 Gb/s)
(2.5 Gb/s)
(2.5 Gb/s)

## Slide 20: What a Router Looks Like
Cisco CRS-X
7ft
23”
3ft
Capacity: 6.4Tb/s Power: 15.2kW
Notes: Weight ~800 Kg

## Slide 21: Basic Architectural Components of an IP Router
Control Plane
Data-path
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols

## Slide 22: Packet Switching – Simple Router Model
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”

## Slide 23: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 24: Per-packet Processing in an IP Router
1. Accept packet arriving on an incoming link.
2. Lookup packet destination address in the forwarding table, to identify outgoing port(s).
3. Manipulate packet header: e.g., decrement TTL, update header checksum.
4. Send packet to the outgoing port(s).
5. Buffer packet in the queue.
6. Transmit packet onto outgoing link.

## Slide 25: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
~1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Buffer
Memory
~1M packets
Off-chip DRAM

## Slide 26: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Data
Hdr
Data
Hdr
Data
Hdr
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr

## Slide 27: Why are Fast Routers Difficult to Make?
It’s hard to keep up with Moore’s Law:
  The bottleneck is memory speed.
  Memory speed is not keeping up with Moore’s Law.
Moore’s Law is too slow:
  Routers need to improve faster than Moore’s Law.

## Slide 28: Router Performance Exceeds Moore’s Law
Growth in capacity of commercial routers:
  Capacity 1992 ~ 2Gb/s
  Capacity 1995 ~ 10Gb/s
  Capacity 1998 ~ 40Gb/s
  Capacity 2001 ~ 160Gb/s
  Capacity 2003 ~ 640Gb/s
  Capacity 2007 ~ 4Tb/s
  Capacity 2010 ~ 16Tb/s
  Capacity 2020 ~ 1Pb/s?
Average growth rate: 2x / 18 months.

## Slide 29: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 30: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Lookup
IP Address
Address
Table
Lookup
IP Address
Address
Table
Lookup
IP Address
Address
Table

## Slide 31: IP Address Lookup
Why it’s thought to be hard:
  It’s not an exact match: it’s a longest prefix match.
  The table is large: about 850,000 entries today, and growing.
  The lookup must be fast: about 4-5ns for a 100Gb/s line.

## Slide 32: IP Lookups find Longest Prefixes
128.9.16.0/21
128.9.172.0/21
128.9.172.0/24
0
232-1
128.9.0.0/16
142.12.0.0/19
65.0.0.0/8
128.9.16.14
Routing lookup: Find the longest matching prefix (aka the most specific route) among all prefixes that match the destination address.

## Slide 33: IP Address Lookup
Why it’s thought to be hard:
  It’s not an exact match: it’s a longest prefix match.
  The table is large: about 850,000 entries today, and growing.
  The lookup must be fast: about 4-5ns for a 100Gb/s line.

## Slide 34: Address Tables are Large
Source: http://www.cidr-report.org/

## Slide 35: IP Address Lookup
Why it’s thought to be hard:
  It’s not an exact match: it’s a longest prefix match.
  The table is large: about 850,000 entries today, and growing.
  The lookup must be fast: about 4-5ns for a 100Gb/s line.

## Slide 36: Lookups Must be Fast
Line rates have been constantly growing over time.
  100Gb/s to 500Gb/s
Packet sizes have not changed
  Max: 1500 bytes (9000 jumbo packets)
  Average: around 250 bytes
  Min: 40 bytes
Time to process each packet around a few nano-seconds

## Slide 37: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 38: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory

## Slide 39: Fast Packet Buffers
Example: 40Gb/s packet buffer
Size = RTT*BW = 10Gb; 40 byte packets
Write Rate, R
1 packet
every 8 ns
Read Rate, R
1 packet
every 8 ns
Buffer
Manager
Buffer
Memory
Use SRAM?
+ fast enough random access time, but
- too low density to store 10Gb of data.
Use DRAM?
+ high density means we can store data, but
- too slow (50ns random access time).
Notes: How fast?
Get into the motivation – say OC768 line rate buffering is a goal.
- Just mention directly the amount of buffering required.
Why is it not possible today?
Why is it intersting….
Talks abut SRAM/DRAM.

## Slide 40: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 41: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N
N times line rate
N times line rate

## Slide 42: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N
Data
Hdr
Data
Hdr
Data
Hdr
Scheduler

## Slide 43: A Router with Output Queues
The best that any queueing system can achieve.

## Slide 44: A Router with Input Queues Head of Line Blocking
The best that any queueing system can achieve.

## Slide 45: Head of Line Blocking

## Slide 46: Virtual Output Queues

## Slide 47: A Router with Virtual Output Queues
The best that any queueing system can achieve.

## Slide 48: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N
N times line rate
N times line rate

## Slide 49: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 50: First Generation Routers
Route
Table
CPU
Buffer
Memory
Line
Interface
MAC
Line
Interface
MAC
Line
Interface
MAC
Typically <0.5Gb/s aggregate capacity
Shared Backplane
Line Interface
CPU
Memory

## Slide 51: Second Generation Routers
Route
Table
CPU
Line
Card
Buffer
Memory
Line
Card
MAC
Buffer
Memory
Line
Card
MAC
Buffer
Memory
Fwding
Cache
Fwding
Cache
Fwding
Cache
MAC
Buffer
Memory
Typically <5Gb/s aggregate capacity

## Slide 52: Third Generation Routers
Line
Card
MAC
Local
Buffer
Memory
CPU
Card
Line
Card
MAC
Local
Buffer
Memory
Switched Backplane
Line Interface
CPU
Memory
Fwding
Table
Routing
Table
Fwding
Table
Typically <50Gb/s aggregate capacity

## Slide 53: Fourth Generation Routers/Switches Optics inside a router for the first time
Switch Core
Linecards
Optical links
100s
of metres
0.3 - 10Tb/s routers in development

## Slide 54: Introduction to Packet Switching
Background
  What is a router?
  Router architecture
Packet processing in routers
  IP address lookup
  Packet buffering
  Switching
Router architectures
  The evolution
  Software-Defined Networking

## Slide 55: Software Defined Networks
Data Plane
Control Plane
Data Plane
Control Plane
Data Plane
Control Plane
Data Plane
Control Plane

## Slide 56: Software Defined Networks – Cont’d
Controller
OpenFlow Switch
PC
OpenFlow
Protocol
SSL
Data Plane
Data Plane
Data Plane
Data Plane

## Slide 57: Final Comments/Questions
What other line rate functionalities can you think of (other than packet forwarding)?
  Are they performance bottleneck in today’s networks?
  How would they evolve over time?
  Do they belong on data path?
Control and management complexity
  What control functionalities do we have in networks today?
  How do we manage those?
  What can we do to simplify this?