## Slide 1: Handout # 2: Course Logistics and Introduction
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
yganjali@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali
CSC 458/2209 – Computer Networks

## Slide 2: Today
Outline
  What this course is about
Logistics
  Course structure, assignments, evaluation
  What is expected from you
  What you can expect from this course
Review
  Simple example – mail vs. FTP
Foundations and basic concepts

## Slide 3: What is This Course About?
Undergrad course; can be taken by grads
Computer networks
  Basics: Layers, naming, and addressing, network (socket) programming, packet switching, routing, congestion control, …
  Advanced networking: HTTP, web, peer-to-peer, routers and switches, security, multimedia, online social networks, software-defined networking, …
Theory vs. Practice
  CSC 358: foundation and theory
  CSC 458: advanced networking and network programming

## Slide 4: Logistics – Prerequisites, Readings
Prerequisites
  Algorithms
  Basic probability theory
  Strong background in C programming and Unix environment
CSC 358 is not a prerequisite.
Readings
  Will be posted on course schedule web page
  Read before class

## Slide 5: Logistics – Textbooks
Textbook
  “Computer Networks: A Systems Approach”, (5th Edition), Peterson, Davie, 2011
Recommended books
  “UNIX Network Programming, Volume I: The Sockets Networking API”, W. Richard Stevens, Bill Fenner, and Andrew M. Rudoff, 3rd edition, 2003
  “TCP/IP Illustrated, Volume 1: The Protocols”, W. Richard Stevens, 1993

## Slide 6: Logistics – Sections
This course is offered in three sections
  L0101: Thu 1-3PM, BA1220, Y. Ganjali
  L0201: Tue. 1-3PM, ES B149, Y. Ganjali
  L5101: Tue. 6-8PM, BA1210, P. Marbach
Might have slight differences in content
  Assignments and exams are coordinated

## Slide 7: Logistics – Hours, Web, Announcements
Office hours
  L0101, and L0201:
    Tue. 3-4 PM, Thu. 3-4 PM, Bahen 5238,
    Or by appointment
  L5101
    Tue. 5-6 PM, Bahen 5224
Course web page
  http://www.cs.toronto.edu/~yganjali/courses/csc458/
Please check the class web page, and the bulletin board regularly for announcements.

## Slide 8: Logistics – Teaching Assistants
Please check class web site for the list of teaching assistants
  And which assignments they are responsible for.
Also, check class web page for office hours.

## Slide 9: Logistics – TA hours, Tutorials
Tutorials and discussion session
  L0101: Fri. 11-12PM, BA1220
  L0201: Fri. 1-2PM, ES B149
  L0501: Tue. 8-9PM, BA1210
First tutorial:
  L0101 and L0201: Friday, September 13th
  L0501: Tuesday, September 10th

## Slide 10: Logistics – Mailing List, Bulletin Board
Bulletin board
  We will use Piazza for announcements and Q&A
    Sign up link on class web site
  Post any questions related to the course.
  Check previous posts before asking a question.
  We guarantee to respond within 48 hours.
Class mailing list
  Based on e-mail address you have defined on ACORN.
  The TAs and I will use this list for announcements only.
  Do not send e-mails to this list!

## Slide 11: Logistics – Grading
Grading for undergraduate AND graduate students
  Assignments: 50%
    Problem sets: 20%
    Programming: 30%
  Midterm exam: 20% - In class
    L0101: Oct. 17th
    L0201: Oct. 22nd
    L0501: Oct. 22nd
  Final exam: 30% - TBA
Please note that grading is the same for graduate and undergraduate students this year.

## Slide 12: Logistics - Deadlines
Assignment deadlines
  One free late submission of 24 hours
    Use on assignment of your choice
    E-mail TAs before the deadline
  10% deduction for each day late
    Up to 20%
    Assignment not accepted after two days

## Slide 13: Logistics – Programming Assignments
To be completed in groups of 2-3 students.
You can submit your assignment during a 7 day period before the deadline
  And have the results of basic tests back
  You get 8 tokens for submission per day
  Your last submission before the deadline will be marked
Socket Programming
MiniNet
  Your very own virtual network!
  You will create and program your own network
  VM available on CDF machines
  More detail on this later.
This is a heavy course, but manageable!

## Slide 14: Logistics – Academic Integrity
Academic Integrity
  All submissions must present original, independent work.
  We take academic offenses very seriously.
  Please read
    Handout # 1 (course information sheet)
    “Guideline for avoiding plagiarism”
    http://www.cs.toronto.edu/~fpitt/documents/plagiarism.html
    “Advice about academic offenses”
    http://www.cs.toronto.edu/~clarke/acoffences/

## Slide 15: Logistics - Accessibility
Accessibility Needs
  The University of Toronto is committed to accessibility. If you require accommodations or have any accessibility concerns, please visit http://studentlife.utoronto.ca/accessibility as soon as possible.

## Slide 16: Acknowledgements
Special thanks to:
  Nick McKeown from Stanford University
  Jennifer Rexford from Princeton University
  David Wetherall from University of Washington
  Nick Feamster from Georgia Tech

## Slide 17: Quick Survey
Have you taken CSC358 before?
Have you taken any networking course?
Are you familiar with
  Socket programming?
  Ethernet, framing, encoding, error detection/correction?
  UDP, TCP and congestion control?
  DNS, SNMP, BGP?
  BitTorrent?
  Voice and video over IP?
  Network security?
  Software-defined networking?
  Control plane vs. data path?

## Slide 18: Questions?
What else do you want to know
about this course?

## Slide 19: Announcement
First tutorial
  L0101 and L0201, Friday, Sep. 13th
  L5101, Tuesday, Sep 10th
Covers socket programming
You’ll need this information for your first programming assignment, which will be posted next week.

## Slide 20: Let’s Begin
An introduction to the mail system
An introduction to the Internet

## Slide 21: An Introduction to the Mail System
Yashar
Nick
U of T
Stanford
Admin
Admin

## Slide 22: Characteristics of the Mail System
Each envelope is individually routed.
No time guarantee for delivery.
No guarantee of delivery in sequence.
No guarantee of delivery at all!
  Things get lost
  How can we acknowledge delivery?
  Retransmission
    How to determine when to retransmit? Timeout?
    Need local copies of contents of each envelope.
    How long to keep each copy.
    What if an acknowledgement is lost?

## Slide 23: An Introduction to the Mail System
Yashar
Nick
U of T
Stanford
Admin
Admin
Application Layer
Transport Layer
Network Layer
Link Layer

## Slide 24: An Introduction to the Internet
Yashar
Nick
cs.toronto.edu
leland.stanford.edu
Network Layer
Link Layer
Application Layer
Transport Layer
O.S.
O.S.
Header
Data
Header
Data
Datagram

## Slide 25: Characteristics of the Internet
Each packet is individually routed.
No time guarantee for delivery.
No guarantee of delivery in sequence.
No guarantee of delivery at all!
  Things get lost
  Acknowledgements
  Retransmission
    How to determine when to retransmit? Timeout?
    Need local copies of contents of each packet.
    How long to keep each copy?
    What if an acknowledgement is lost?

## Slide 26: Characteristics of the Internet – Cont’d
No guarantee of integrity of data.
Packets can be fragmented.
Packets may be duplicated.

## Slide 27: Layering in the Internet
Transport Layer
  Provides reliable, in-sequence delivery of data from end-to-end on behalf of application.
Network Layer
  Provides “best-effort”, but unreliable, delivery of datagrams.
Link Layer
  Carries data over (usually) point-to-point links between hosts and routers; or between routers and routers.

## Slide 28: An Introduction to the Mail System
Yashar
Nick
U of T
Stanford
Admin
Admin
Application Layer
Transport Layer
Network Layer
Link Layer

## Slide 29: Some Questions About the Mail System
How many sorting offices are needed and where should they be located?
How much sorting capacity is needed?
  Should we allocate for Mother’s Day?
How can we guarantee timely delivery?
  What prevents delay guarantees?
  Or delay variation guarantees?
How do we protect against fraudulent mail deliverers, or fraudulent senders?

## Slide 30: Outline – Foundations & Basic Concepts
A detailed FTP example
Layering
Packet switching and circuit switching

## Slide 31: Example: FTP over the Internet Using TCP/IP and Ethernet
App
OS
R2
R3
R4
R1
R5
Ethernet
“A” U of T
“B” Stanford
Ethernet
App
OS
1
2
3
4
6
7
20
19
18
17
5
9
10
8
12
13
11
15
16
14

## Slide 32: In the Sending Host
1. Application-Programming Interface (API)
  Application requests TCP connection with “B”
2. Transmission Control Protocol (TCP)
  Creates TCP “Connection setup” packet
  TCP requests IP packet to be sent to “B”
TCP
Data
TCP
Header
TCP Packet
Type = Connection Setup
Empty

## Slide 33: In the Sending Host – Cont’d
3. Internet Protocol (IP)
  Creates IP packet with correct addresses.
  IP requests packet to be sent to router.
IP
Data
TCP Packet
Encapsulation
IP
Header
IP Packet
Destination Address: IP “B”
Source Address: IP “A”
Protocol = TCP
TCP
Data
TCP
Header

## Slide 34: In the Sending Host – Cont’d
4. Link (“MAC” or Ethernet) Protocol
  Creates MAC frame with Frame Check Sequence (FCS).
  Wait for Access to the line.
  MAC requests PHY to send each bit of the frame.
Ethernet
Data
IP Packet
Ethernet
FCS
Ethernet
Header
Ethernet Packet
Destination Address: MAC “R1”
Source Address: MAC “A”
Protocol = IP
IP
Data
IP
Header
Encapsulation

## Slide 35: In Router R1
5. Link (“MAC” or Ethernet) Protocol
  Accept MAC frame, check address and Frame Check Sequence (FCS).
  Pass data to IP Protocol.
Ethernet
Data
IP Packet
Ethernet
FCS
Ethernet
Header
Ethernet Packet
Destination Address: MAC “R1”
Source Address: MAC “A”
Protocol = IP
IP
Data
IP
Header
Decapsulation

## Slide 36: In Router R1
6. Internet Protocol (IP)
  Use IP destination address to decide where to send packet next (“next-hop routing”).
  Request Link Protocol to transmit packet.
IP
Data
IP
Header
IP Packet
Destination Address: IP “B”
Source Address: IP “A”
Protocol = TCP

## Slide 37: In Router R1
7. Link (“MAC” or Ethernet) Protocol
  Creates MAC frame with Frame Check Sequence (FCS).
  Wait for Access to the line.
  MAC requests PHY to send each bit of the frame.
Ethernet
Data
IP Packet
Ethernet
FCS
Ethernet
Header
Ethernet Packet
Destination Address: MAC “R2”
Source Address: MAC “R1”
Protocol = IP
IP
Data
IP
Header
Encapsulation

## Slide 38: In Router R5
16. Link (“MAC” or Ethernet) Protocol
  Creates MAC frame with Frame Check Sequence (FCS).
  Wait for Access to the line.
  MAC requests PHY to send each bit of the frame.
Ethernet
Data
IP Packet
Ethernet
FCS
Ethernet
Header
Ethernet Packet
Destination Address: MAC “B”
Source Address: MAC “R5”
Protocol = IP
IP
Data
IP
Header
Encapsulation

## Slide 39: In the Receiving Host
17. Link (“MAC” or Ethernet) Protocol
  Accept MAC frame, check address and Frame Check Sequence (FCS).
  Pass data to IP Protocol.
Ethernet
Data
IP Packet
Ethernet
FCS
Ethernet
Header
Ethernet Packet
Destination Address: MAC “B”
Source Address: MAC “R5”
Protocol = IP
IP
Data
IP
Header
Decapsulation

## Slide 40: In the Receiving Host - Cont’d
18. Internet Protocol (IP)
  Verify IP address.
  Extract/decapsulate TCP packet from IP packet.
  Pass TCP packet to TCP Protocol.
IP
Data
TCP Packet
Decapsulation
IP
Header
IP Packet
Destination Address: IP “B”
Source Address: IP “A”
Protocol = TCP
TCP
Data
TCP
Header

## Slide 41: In the Receiving Host - Cont’d
19. Transmission Control Protocol (TCP)
  Accepts TCP “Connection setup” packet
  Establishes connection by sending “Ack”.
20. Application-Programming Interface (API)
  Application receives request for TCP connection with “A”.
TCP
Data
TCP
Header
TCP Packet
Type = Connection Setup
Empty

## Slide 42: Outline – Foundations & Basic Concepts
A detailed FTP example
Layering
Packet switching and circuit switching

## Slide 43: Layering – The OSI Model
Session
Network
Link
Physical
Physical
Physical
Application
Presentation
Transport
Network
Link
Link
Network
Transport
Session
Presentation
Application
Network
Link
Physical
Peer-layer communication
layer-to-layer communication
Router
Router
1
2
3
4
5
6
7
1
2
3
4
5
6
7

## Slide 44: Layering – Our FTP Example
Network
Link
Transport
Application
Presentation
Session
Transport
Network
Link
Physical
The 7-layer OSI Model
The 4-layer Internet model
Application
FTP
ASCII/Binary
IP
TCP
Ethernet

## Slide 45: Outline – Foundations & Basic Concepts
A detailed FTP example
Layering
Packet switching and circuit switching

## Slide 46: Circuit Switching
It’s the method used by the telephone network.
A call has three phases:
  Establish circuit from end-to-end (“dialing”),
  Communicate,
  Close circuit (“tear down”).
Originally, a circuit was an end-to-end physical wire.
Nowadays, a circuit is like a virtual private wire: each call has its own private, guaranteed data rate from end-to-end.
A
B
Source
Destination

## Slide 47: Circuit Switching – Telephone Network
Source
“Caller”
Central
Office
“C.O.”
Destination
“Callee”
Central
Office
“C.O.”
Trunk
Exchange
Each phone call is allocated 64kb/s. So, a 10Gb/s trunk line can carry about 156,000 calls.

## Slide 48: Packet Switching
It’s the method used by the Internet.
Each packet is individually routed packet-by-packet, using the router’s local routing table.
The routers maintain no per-flow state.
Different packets may take different paths.
Several packets may arrive for the same output link at the same time, therefore a packet switch has buffers.
A
R1
R2
R4
R3
B
Source
Destination

## Slide 49: Packet Switching – Simple Router Model
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”

## Slide 50: Statistical Multiplexing – Basic Idea
time
time
time
rate
One flow
Two flows
Average rate
Many flows
Network traffic is bursty. i.e. the rate changes frequently.
Peaks from independent flows generally occur at different times.
Conclusion: The more flows we have, the smoother the traffic.
Average rates of: 1, 2, 10, 100, 1000 flows.
rate
rate

## Slide 51: Packet Switching – Statistical Multiplexing
Link rate, R
X(t)
Dropped packets
B
Dropped packets
Queue Length
X(t)
Time
Packet buffer
Packets for one output
Data
Hdr
Data
Hdr
Data
Hdr
R
R
R
Because the buffer absorbs temporary bursts, the egress link need not operate at rate N.R.
But the buffer has finite size, B, so losses will occur.
1
2
N

## Slide 52: Statistical Multiplexing
B
A
time
time
Rate
Rate
C
C
A
C
B
C
Notes: Statistical multiplexing
  Important if traffic is bursty
Less expensive
Contention requires buffering
  Variable delay => no QoS guarantees

## Slide 53: Statistical Multiplexing Gain
A
B
R
2C
R < 2C
A+B
time
Rate
Statistical multiplexing gain = 2C/R
Other definitions of SMG: The ratio of rates that give rise to a particular queue occupancy, or particular loss probability.
Notes: Statistical multiplexing
  Important if traffic is bursty
Less expensive
Contention requires buffering
  Variable delay => no QoS guarantees

## Slide 54: Why Packet Switching in the Internet?
Efficient use of expensive links:
  The links are assumed to be expensive and scarce.
  Packet switching allows many, bursty flows to share the same link efficiently.
  “Circuit switching is rarely used for data networks, ... because of very inefficient use of the links” - Gallager
Resilience to failure of links & routers:
  “For high reliability, ... [the Internet] was to be a datagram subnet, so if some lines and [routers] were destroyed, messages could be ... rerouted” - Tanenbaum
Notes: Breaking message into packets allows parallel transmission across all links, reducing network latency.
In summary the benefits that of packet switched networks can be summarized as follows:
They use the bandwidth efficiently, meaning that a trunk link uses less resources than the sum of its tributaries, as they multiplex and conserve bandwidth
They have little state in the intermediate nodes
They are robust, some claim that they were designed to withstand a nuclear attack
They do not have a central authority from whom we need permission to run experiments

## Slide 55: Final Comments, Discussion
Is layering the best approach?
  Simplifies design
  Yet, limited and inflexible
Best effort service
  Made the rapid growth of the Internet possible
  Makes providing any guarantees very difficult
Packet switching
  Enables statistical multiplexing
  We need extremely fast routers
Routing
  How does a router know which output port to send the packet to?