## Slide 1: Handout # 4: Link Layer, Error Detection/Correction
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
yganjali@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali
CSC 458/2209 – Computer Networks

## Slide 2: Announcements
Programming assignment 1 out (Sep 17th).
To be completed in groups of 2-3 people.
Due: Oct. 11th at 5PM.
  Will have test runs during the last week.
Tutorials
  We had a tutorial on socket programming last week.
  This week the tutorial will be a review of this assignment.
Links posted on class web page:
  Socket programming
  Coding guidelines
Use Piazza if you have any questions.

## Slide 3: Announcements – Cont’d
Reading for this week:
  Chapter 1 of the textbook
Next week: Chapter 2

## Slide 4: Last Time …
Protocols, layering and reference models
Network
Link
Transport
Application
Presentation
Session
Transport
Network
Link
Physical
The 7-layer OSI Model
The 4-layer Internet model
Application
FTP
ASCII/Binary
IP
TCP
Ethernet

## Slide 5: Outline
Part 1. Physical/link layer
  Different types of media
  Encoding bits with signals
  Framing
  Model of a link
Part 2. Error detection and correction
  Hamming distance
  Parity, checksums, CRC, …

## Slide 6: Part 1 – Physical/Link Layer
Focus:
How do we send a message across a wire?
The physical / link layers:
  Different kinds of media
  Encoding bits, messages
  Model of a link
Physical
Data Link
Network
Transport
Session
Presentation
Application
0
1
1
0
0
1
1
1

## Slide 7: 1. Different Types of Media
Wire
  Twisted pair, e.g., CAT5 UTP, 10  100Mbps, 100m
  Coaxial cable, e.g, thin-net, 10  100Mbps, 200m
Fiber
  Multi-mode, e.g., 100Mbp/s, 600m
  Single-mode, e.g., 100  2400 Mbps, 40km
Wireless
  Infra-red, e.g., IRDA, ~1Mbps
  RF, e.g., 802.11 wireless LANs, Bluetooth (2.4GHz)
  Microwave, satellite, cell phones, …
Notes: UTP: Unshielded Twisted Pair
IRDA: InfraRed Data Association

## Slide 8: Wireless
Different frequencies have different properties
Signals subject to atmospheric/environmental effects
Freq (Hz)
104
106
108
1010
1012
1014
AM
Coax
Microwave
Satellite
Fiber
FM
Twisted
Pair
TV
Radio
UV
Microwave
IR
Light

## Slide 9: Fiber
Long, thin, pure strand of glass
  light propagated with total internal reflection
  enormous bandwidth available (terabits)
Multi-mode allows many different paths, limited by dispersion
Chromatic dispersion if multiple frequencies
Light source
(LED, laser)
Light detector
(photodiode)

## Slide 10: Bandwidth of a Channel
EE: bandwidth (B, in Hz) is the width of the pass-band in the frequency domain
CS: bandwidth (bps) is the information carrying capacity (C) of the channel
Shannon showed how they are related by noise
  Noise limits how many signal levels we can safely distinguish
  Geekspeak: “cannot distinguish the signal from the noise”

## Slide 11: 2. Encoding Bits with Signals
Generate analog waveform (e.g., voltage) from digital data at transmitter and sample to recover at receiver
We send/recover symbols that are mapped to bits
  Signal transition rate = baud rate, versus bit rate
This is baseband transmission …
0
1

## Slide 12: NRZ and NRZI
Simplest encoding, NRZ (Non-return to zero)
  Use high/low voltages, e.g., high = 1, low = 0
Variation, NRZI (NRZ, invert on 1)
  Use transition for 1s, no transition for 0s
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 13: Clock Recovery
Problem: How do we distinguish consecutive 0s or 1s?
If we sample at the wrong time we get garbage …
If sender and receiver have exact clocks no problem
  But in practice they drift slowly
This is the problem of clock recovery
Possible solutions:
  Send separate clock signal  expensive
  Keep messages short  limits data rate
  Embed clock signal in data signal  other codes

## Slide 14: Manchester Coding
Make transition in the middle of every bit period
  Low-to-high is 0; high-to-low is 1
  Signal rate is twice the bit rate
  Used on 10 Mbps Ethernet
Advantage: self-clocking
  clock is embedded in signal, and we re-sync with a phase-locked loop every bit
Disadvantage: 50% efficiency

## Slide 15: Coding Examples

## Slide 16: 4B/5B Codes
We want transitions *and* efficiency …
Solution: map data bits (which may lack transitions) into code bits (which are guaranteed to have them)
4B/5B code:
  0000  11110, 0001  01001, … 1111  11101
  Never more than three consecutive 0s back-to-back
  80% efficiency
This code is in LANs such as FDDI, 100Mbps Ethernet

## Slide 17: 3. Framing
Need to send message, not just bits
  Requires that we synchronize on the start of message reception at the far end of the link
  Complete Link layer messages are called frames
Common approach: Sentinels
  Look for special control code that marks start of frame
  And escape or “stuff” this code within the data region

## Slide 18: Example: Point-to-Point Protocol (PPP)
IETF standard, used for dialup and leased lines
Flag is special and indicates start/end of frame
Occurrences of flag inside payload must be “stuffed”
  Replace 0x7E with 0x7D, 0x5E
  Replace 0x7D with 0x7D, 0x5D
Flag
0x7E
(header)
Payload
(variable)
(trailer)
Flag
0x7E

## Slide 19: 4. Model of a Link
Abstract model is typically all we will need
  What goes in comes out altered by the model
Other parameters that are important:
  The kind and frequency of errors
  Whether the media is broadcast or not
Message
M bits
Rate R Mbps
Delay D seconds

## Slide 20: Message Latency
How long does it take to send a message?
Two terms:
  Propagation delay = distance / speed of light in media
    How quickly a message travels over the wire
  Transmission delay = message (bits) / rate (bps)
    How quickly you can inject the message onto the wire
Later we will see queuing delay …
Delay D, Rate R
Message M

## Slide 21: Relationships
Latency = Propagation + Transmit + Queue
Propagation Delay = Distance/SpeedOfLight
Transmit Time = MessageSize/Bandwidth

## Slide 22: One-way Latency
Dialup with a modem:
  D = 10ms, R = 56Kbps, M = 1000 bytes
  Latency = 10ms + (1000 x 8)/(56 x 1000) sec = 153ms!
Cross-country with T3 (45Mbps) line:
  D = 50ms, R = 45Mbps, M = 1000 bytes
  Latency = 50ms + (1000 x 8) / (45 x 1000000) sec = 50ms!
Either a slow link or long wire makes for large latency

## Slide 23: Latency and RTT
Latency is typically the one way delay over a link
  Arrival Time - Departure Time
The round trip time (RTT) is twice the one way delay
  Measure of how long to signal and get a response
+
RTT
Departure
Time
Arrival
Time

## Slide 24: Throughput
Measure of system’s ability to “pump out” data
  NOT the same as bandwidth
Throughput = Transfer Size / Transfer Time
  Eg, “I transferred 1000 bytes in 1 second on a 100Mb/s link”
    BW?
    Throughput?
Transfer Time = SUM OF
  Time to get started shipping the bits
  Time to ship the bits
  Time to get stopped shipping the bits

## Slide 25: Messages Occupy “Space” On the Wire
Consider a 1b/s network.
  How much space does 1 byte take?
Suppose latency is 16 seconds.
  How many bits can the network “store”
  This is the BANDWIDTH-DELAY Product
  Measure of “data in flight.”
  1b/s * 16s = 16b
Tells us how much data can be sent before a receiver sees any of it.
  Twice B.D.P. tells us how much data we could send before hearing back from the receiver something related to the first bit sent.
  Implications?

## Slide 26: A More Realistic Example
101100…11…0010101010101010101
BDP = 50ms * 100Mbps = 5Mb = 625KB

## Slide 27: Packet Switching
Host A
Host B
R1
R2
R3
A
R1
R2
R4
R3
B
TRANSP1
TRANSP2
TRANSP3
TRANSP4
PROP1
PROP2
PROP3
PROP4
Source
Destination
“Store-and-Forward” at each Router

## Slide 28: Packet Switching
Why not send the entire message in one packet?
Breaking message into packets allows parallel transmission across all links, reducing end to end latency. It also prevents a link from being “hogged” for a long time by one message.
Host A
Host B
R1
R2
R3
M/R
Host A
Host B
R1
R2
R3
M/R

## Slide 29: Packet Switching – Queueing Delay
Because the egress link is not necessarily free when a packet arrives, it may be queued in a buffer. If the network is busy, packets might have to wait a long time.
Host A
Host B
R1
R2
R3
TRANSP1
TRANSP2
TRANSP3
TRANSP4
PROP1
PROP2
PROP3
PROP4
Q2
How can we determine the queueing delay?

## Slide 30: Part 1: Key Concepts
We typically model links in terms of bandwidth and delay, from which we can calculate message latency.
Different media have different properties that affect their performance as links.
We need to encode bits into signals so that we can recover them at the other end of the channel.
Framing allows complete messages to be recovered at the far end of the link.

## Slide 31: Outline
Part 1. Physical/link layer
  Different types of media
  Encoding bits with signals
  Framing
  Model of a link
Part 2. Error detection and correction
  Hamming distance
  Parity, checksums, CRC, …

## Slide 32: Part 2 – Error Detection and Correction
Focus: How do we detect and correct messages that are garbled during transmission?
The responsibility for doing this cuts across the different layers
Physical
Data Link
Network
Transport
Session
Presentation
Application

## Slide 33: Errors and Redundancy
Noise can flip some of the bits we receive
  We must be able to detect when this occurs!
  Why?
  Who needs to detect it? (links, routers, OSs, or apps?)
Basic approach: add redundant data
  Error detection codes allow errors to be recognized
  Error correction codes allow errors to be repaired too

## Slide 34: Motivating Example
A simple error detection scheme:
  Just send two copies. Differences imply errors.
Question: Can we do any better?
  With less overhead
  Catch more kinds of errors
Answer: Yes – stronger protection with fewer bits
  But we can’t catch all inadvertent errors, nor malicious ones
We will look at basic block codes
  K bits in, N bits out is a (N, K) code
  Simple, memoryless mapping

## Slide 35: Detection vs. Correction
Two strategies to correct errors:
  Detect and retransmit, or Automatic Repeat reQuest. (ARQ)
  Error correcting codes, or Forward Error Correction (FEC)
Satellites, real-time media tend to use error correction
Retransmissions typically at higher levels (Network+)
Question: Which should we choose?

## Slide 36: Detect or Correct?
Advantages of Error Detection
  Requires smaller number of bits/overhead.
  Requires less/simpler processing.
Advantages of Error Correction
  Reduces number of retransmissions.
Most data networks today use error detection, not error correction.

## Slide 37: Retransmissions vs. FEC
The better option depends on the kind of errors and the cost of recovery
Example: Message with 1000 bits, Prob(bit error) 0.001
  Case 1: random errors
  Case 2: bursts of 1000 errors
  Case 3: real-time application (teleconference)

## Slide 38: Encoding to Detect Errors
We use codes to help us detect errors.
The set of possible messages is mapped by a function onto the set of codes.
We pick the mapping function so that it is easy to detect errors among the resulting codes.
Example: Consider the function that duplicates each bit in the message. E.g. the message 1011001 would be mapped to the code 11001111000011, and then transmitted by the sender. The receiver knows that bits always come in pairs. If the two bits in a pair are different, it declares that there was a bit error.
Of course, this code is quite inefficient…

## Slide 39: The Hamming Distance
Errors must not turn one valid codeword into another valid codeword, or we cannot detect/correct them.
Hamming distance of a code is the smallest number of bit differences that turn any one codeword into another
  e.g, code 000 for 0, 111 for 1, Hamming distance is 3
For code with distance d+1:
  d errors can be detected, e.g, 001, 010, 110, 101, 011
For code with distance 2d+1:
  d errors can be corrected, e.g., 001  000

## Slide 40: Hamming Distance
Number of bits that differ between two codes
e.g. 1 0 0 1 0 1 0 1
1 0 1 1 1 0 0 1
0 0 1 0 1 1 0 0
In our example code (replicated bits), all codes have at least two bits different from every other code. Therefore, it has a Hamming distance of 2.
HD=3

## Slide 41: Hamming Distance
To reliably detect a d-bit error: HD ≥ d+1
To reliably correct a d-bit error: HD ≥ 2d+1
HD = min (dij )
4
3
1
2
d23
Set of codes

## Slide 42: Parity
Start with n bits and add another so that the total number of 1s is even (even parity)
  e.g. 0110010  01100101
  Easy to compute as XOR of all input bits
Will detect an odd number of bit errors
  But not an even number
Does not correct any errors

## Slide 43: 2D Parity
Add parity row/column to array of bits
Detects all 1, 2, 3 bit errors, and many errors with >3 bits.
Corrects all 1 bit errors
0101001 1
1101001 0
1011110 1
0001110 1
0110100 1
1011111 0
1111011 0

## Slide 44: Checksums
Used in Internet protocols (IP, ICMP, TCP, UDP)
Basic Idea: Add up the data and send it along with sum
Algorithm:
  checksum is the 1s complement of the 1s complement sum of the data interpreted 16 bits at a time (for 16-bit TCP/UDP checksum)
1s complement: flip all bits to make number negative
  Consequence: adding requires carryout to be added back

## Slide 45: CRCs (Cyclic Redundancy Check)
Stronger protection than checksums
  Used widely in practice, e.g., Ethernet CRC-32
  Implemented in hardware (XORs and shifts)
Algorithm: Given n bits of data, generate a k bit check sequence that gives a combined n + k bits that are divisible by a chosen divisor C(x)
Based on mathematics of finite fields
  “numbers” correspond to polynomials, use modulo arithmetic
  e.g, interpret 10011010 as x7 + x4 + x3 + x1

## Slide 46: Example
Message: 10011010
Generator: 1101
Divide 10011010000 by 1101
  Remainder: 101
Message to be sent: 10011010101

## Slide 47: Reed-Solomon / BCH Codes
Developed to protect data on magnetic disks
Used for CDs and cable modems too
Property: 2t redundant bits can correct <= t errors
Mathematics somewhat more involved …

## Slide 48: Part 2: Key Concepts
Redundant bits are added to messages to protect against transmission errors.
Two recovery strategies are retransmissions (ARQ) and error correcting codes (FEC)
The Hamming distance tells us how much error can safely be tolerated.