## Slide 1: Handout # 6: Interconnecting LANs; Internet Protocol (IP)
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
yganjali@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali
CSC 458/2209 – Computer Networks

## Slide 2: Announcements
Problem Set 1 out today (Sep 24th).
  Problems from the textbook
  Due Friday Oct. 4th at 5pm.
  Remember the late submission policy.
  Remember academic integrity guidelines.
  Submit electronically on MarkUS.
    NOTE. File names must be: ps1.pdf
  You can scan and save as a pdf file.
    Not preferred, but acceptable.
This week’s tutorial: sample problems (PS1)

## Slide 3: Announcements – Cont’d
Programming assignment 1
  Have you tested MiniNet?
  Have you been able to setup your VM?
  Slides for the tutorial available on class web page
  Start early! Start early! Start early! …
Reading for next week:
  Chapter 3 of the textbook

## Slide 4: The Story
So far …
  Layers, and protocols
  Link layer
    Media type, encoding
    Framing, link model
    Error detection, correction
This time
  Interconnecting LANs
    Hubs, switches, and bridges
  The Internet Protocol
Physical
Data Link
Network
Transport
Session
Presentation
Application

## Slide 5: Ethernet
Dominant wired and wireless LAN technology
First widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s
Ethernet
sketch

## Slide 6: Ethernet Uses CSMA/CD
Carrier sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
Collision detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random access: exponential back-off
  After collision, wait a random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again

## Slide 7: Limitations on Ethernet Length
Latency depends on physical length of link
  Time to propagate a packet from one end to the other
Suppose A sends a packet at time t
  And B sees an idle line at a time just before t+d
  … so B happily starts transmitting a packet
B detects a collision, and sends jamming signal
  But A doesn’t see collision till t+2d
latency d
A
B

## Slide 8: Limitations on Ethernet Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions on Ethernet
  Maximum length of the wire: 2500 meters
  Minimum length of the packet: 512 bits (64 bytes)
latency d
A
B

## Slide 9: Ethernet Frame Structure
Addresses: source and destination MAC addresses
  Adaptor passes frame to network-level protocol
    If destination address matches the adaptor
    Or the destination address is the broadcast address
  Otherwise, adapter discards frame
Type: indicates the higher layer protocol
  Usually IP
  But also Novell IPX, AppleTalk, …
CRC: cyclic redundancy check
  Checked at receiver
  If error is detected, the frame is simply dropped

## Slide 10: Unreliable, Connectionless Service
Connectionless
  No handshaking between sending and receiving adapter.
Unreliable
  Receiving adapter doesn’t send ACKs or NACKs
  Packets passed to network layer can have gaps
  Gaps will be filled if application is using TCP
  Otherwise, the application will see the gaps

## Slide 11: Shuttling Data at Different Layers
Different devices switch different things
  Physical layer: electrical signals (repeaters and hubs)
  Link layer: frames (bridges and switches)
  Network layer: packets (routers)
Application gateway
Transport gateway
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data

## Slide 12: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals on each LAN
  Transmits an amplified copy

## Slide 13: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub

## Slide 14: Limitations of Repeaters and Hubs
One large collision domain
  Every bit is sent everywhere
  So, aggregate throughput is limited
  E.g., three departments each get 10 Mbps independently
  … and then connect via a hub and must share 10 Mbps
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  So, can’t interconnect between different rates or formats
  E.g., 10 Mbps Ethernet and 100 Mbps Ethernet
Limitations on maximum nodes and distances
  Does not circumvent the limitations of shared media
  E.g., still cannot go beyond 2500 meters on Ethernet

## Slide 15: Link Layer: Bridges
Connects two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate LAN segment
Each segment is its own collision domain
host
host
host
host
host
host
host
host
host
host
host
host
Bridge

## Slide 16: Link Layer: Switches
Typically connects individual computers
  A switch is essentially the same as a bridge
  … though typically used to connect hosts, not LANs
Like bridges, support concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D

## Slide 17: Dedicated Access and Full Duplex
Dedicated access
  Host has direct connection to the switch
  … rather than a shared LAN connection
Full duplex
  Each connection can send in both directions
  Host sending to switch, and host receiving from switch
  E.g., in 10BaseT and 100Base T
Completely avoids collisions
  Each connection is a bidirectional point-to-point link
  No need for carrier sense, collision detection, and so on

## Slide 18: Bridges/Switches: Traffic Isolation
Switch breaks subnet into LAN segments
Switch filters packets
  Frame only forwarded to the necessary segments
  Segments become separate collision domains
hub
hub
hub
switch/bridge
collision domain
collision domain
collision domain

## Slide 19: Advantages Over Hubs/Repeaters
Only forwards frames as needed
  Filters frames to avoid unnecessary load on segments
  Sends frames only to segments that need to see them
Extends the geographic span of the network
  Separate collision domains allow longer distances
Improves privacy by limiting scope of frames
  Hosts can “snoop” the traffic traversing their segment
  … but not all the rest of the traffic
Applies carrier sense and collision detection
  Does not transmit when the link is busy
  Applies exponential back-off after a collision
Joins segments using different technologies

## Slide 20: Disadvantages Over Hubs/Repeaters
Delay in forwarding frames
  Bridge/switch must receive and parse the frame
  … and perform a look-up to decide where to forward
  Storing and forwarding the packet introduces delay
  Solution: cut-through switching
Need to learn where to forward frames
  Bridge/switch needs to construct a forwarding table
  Ideally, without intervention from network administrators
  Solution: self-learning
Higher cost
  More complicated devices that cost more money

## Slide 21: Motivation For Cut-Through Switching
Buffering a frame takes time
  Suppose L is the length of the frame
  And R is the transmission rate of the links
  Then, receiving the frame takes L/R time units
Buffering delay can be a high fraction of total delay
  Propagation delay is small over short distances
  Making buffering delay a large fraction of total
  Analogy: large group walking through NYC
A
B
switches

## Slide 22: Cut-Through Switching
Start transmitting as soon as possible
  Inspect the frame header and do the look-up
  If outgoing link is idle, start forwarding the frame
Overlapping transmissions
  Transmit the head of the packet via the outgoing link
  … while still receiving the tail via the incoming link
  Analogy: different folks crossing different intersections
A
B
switches

## Slide 23: Motivation For Self Learning
Switches forward frames selectively
  Forward frames only on segments that need them
Switch table
  Maps destination MAC address to outgoing interface
  Goal: construct the switch table automatically
switch
A
B
C
D

## Slide 24: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a time-to-live field to eventually forget the mapping
A
B
C
D
Switch learns how to reach A.

## Slide 25: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often
A
B
C
D
When in doubt, shout!

## Slide 26: Switch Filtering/Forwarding
When switch receives a frame:
index switch table using MAC dest address
if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 27: Flooding Can Lead to Loops
Switches sometimes need to broadcast frames
  Upon receiving a frame with an unfamiliar destination
  Upon receiving a frame sent to the broadcast address
Broadcasting is implemented by flooding
  Transmitting frame out every interface
  … except the one where the frame arrived
Flooding can lead to forwarding loops
  E.g., if the network contains a cycle of switches
  Either accidentally, or by design for higher reliability

## Slide 28: Solution: Spanning Trees
Ensure the topology has no loops
  Avoid using some of the links when flooding
  … to avoid forming a loop
Spanning tree
  Sub-graph that covers all vertices but contains no cycles
  Links not in the spanning tree do not forward frames

## Slide 29: Constructing a Spanning Tree
Need a distributed algorithm
  Switches cooperate to build the spanning tree
  … and adapt automatically when failures occur
Key ingredients of the algorithm
  Switches need to elect a “root”
    The switch with the smallest identifier
  Each switch identifies if its interface is on the shortest path from the root
    And exclude it from the tree if not
  Messages (Y, d, X)
    From node X
    Claiming Y is the root
    And the distance is d
root
One hop
Three hops

## Slide 30: Steps in Spanning Tree Algorithm
Initially, each switch thinks it is the root
  Switch sends a message out every interface
  … identifying itself as the root with distance 0
  Example: switch X announces (X, 0, X)
Switches update their view of the root
  Upon receiving a message, check the root id
  If the new id is smaller, start viewing that switch as root
Switches compute their distance from the root
  Add 1 to the distance received from a neighbor
  Identify interfaces not on a shortest path to the root
  … and exclude them from the spanning tree

## Slide 31: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 32: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 33: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
    Need to elect a new root, with the next lowest identifier
  Failure of other switches and links
    Need to recompute the spanning tree
Root switch continues sending messages
  Periodically reannouncing itself as the root (1, 0, 1)
  Other switches continue forwarding messages
Detecting failures through timeout (soft state!)
  Switch waits to hear from others
  Eventually times out and claims to be the root
See the textbook for details and another example

## Slide 34: Switches vs. Routers
Advantages of switches over routers
  Plug-and-play
  Fast filtering and forwarding of frames
  No pronunciation ambiguity (e.g., “rooter” vs. “rowter”)
Disadvantages of switches over routers
  Topology is restricted to a spanning tree
  Large networks require large ARP tables
  Broadcast storms can cause the network to collapse

## Slide 35: Comparing Hubs, Switches, & Routers
hubs
routers
switches
traffic
isolation
no
yes
yes
plug & play
yes
no
yes
optimal
routing
no
yes
no
cut
through
yes
no
yes

## Slide 36: Part II – The Internet Protocol (IP)
IP: The Internet Protocol
  Service characteristics
  The IP Datagram format
  IP addresses
  Classless Inter-Domain Routing (CIDR)
  An aside: Turning names into addresses (DNS)

## Slide 37: The Internet Protocol (IP)
App
Transport
Network
Link
TCP / UDP
IP
Data
Hdr
Data
Hdr
TCP Segment
IP Datagram
Protocol Stack

## Slide 38: The Internet Protocol (IP)
Characteristics of IP
  CONNECTIONLESS: mis-sequencing
  UNRELIABLE: may drop packets…
  BEST EFFORT: … but only if necessary
  DATAGRAM: individually routed
A
R1
R2
R4
R3
B
Source
Destination
D
H
D
H
Transparent
Architecture
Links
Topology

## Slide 39: The IP Datagram
Flags
vers
TTL
TOS
checksum
HLen
Total Length
ID
FRAG Offset
Protocol
SRC IP Address
DST IP Address
(OPTIONS)
(PAD)
<=64 KBytes
Offset within original packet
Hop count
8
16
32
bits 0

## Slide 40: Fragmentation
A
Ethernet
MTU=1500 bytes
MTU=1500 bytes
B
Source
Destination
MTU<1500 bytes
Problem: A router may receive a packet larger than the maximum transmission unit (MTU) of the outgoing link.
R1
R2
Solution: R1 fragments the IP datagram into multiple, self-contained datagrams.
Data
HDR (ID=x)
Data
HDR (ID=x)
Data
HDR (ID=x)
Data
HDR (ID=x)
Offset>0
More Frag=0
Offset=0
More Frag=1

## Slide 41: Fragmentation
Fragments are re-assembled by the destination host; not by intermediate routers.
To avoid fragmentation, hosts commonly use path MTU discovery to find the smallest MTU along the path.
Path MTU discovery involves sending various size datagrams until they do not require fragmentation along the path.
Most links use MTU>=1500bytes today.
Try: traceroute –F www.uwaterloo.ca 1500 and traceroute –F www.uwaterloo.ca 1501
(DF=1 set in IP header; routers send “ICMP” error message, which is shown as “!F”).
Bonus: Can you find a destination for which the path MTU < 1500 bytes?

## Slide 42: IP Addresses
IP (Version 4) addresses are 32 bits long
Every interface has a unique IP address:
  A computer might have two or more IP addresses
  A router has many IP addresses
IP addresses are hierarchical
  They contain a network ID and a host ID
  E.g. Apple computers addresses start with: 17….
IP addresses are assigned statically or dynamically (e.g. DHCP)
IP (Version 6) addresses are 128 bits long

## Slide 43: IP Addresses
Originally there were 5 classes:
CLASS “A”
1
7
0
Net ID
Host-ID
CLASS “B”
10
Net ID
Host-ID
24
2
14
16
CLASS “C”
110
Net ID
Host-ID
3
21
8
CLASS “D”
1110
Multicast Group ID
4
28
CLASS “E”
11110
Reserved
5
27
A
B
C
D
0
232-1

## Slide 44: IP Addresses – Examples
Class “A” address: www.mit.edu
  18.7.22.83
  (18<128 => Class A)
Class “B” address: www.toronto.edu
  142.150.210.13
  (128<142<128+64 => Class B)

## Slide 45: IP Addressing
Problem:
Address classes were too “rigid”. For most organizations, Class C were too small and Class B too big. Led to inefficient use of address space, and a shortage of addresses.
Organizations with internal routers needed to have a separate (Class C) network ID for each link.
And then every other router in the Internet had to know about every network ID in every organization, which led to large address tables.
Small organizations wanted Class B in case they grew to more than 255 hosts. But there were only about 16,000 Class B network IDs.

## Slide 46: IP Addressing
Two solutions were introduced:
Subnetting within an organization to subdivide the organization’s network ID.
Classless Inter-Domain Routing (CIDR) in the Internet backbone was introduced in 1993 to provide more efficient and flexible use of IP address space.
CIDR is also known as “supernetting” because subnetting and CIDR are basically the same idea.

## Slide 47: Subnetting
CLASS “B”
e.g. Company
10
Net ID
Host-ID
2
14
16
10
Net ID
Host-ID
2
14
16
0000
Subnet ID (20)
Subnet
Host ID (12)
10
Net ID
Host-ID
2
14
16
1111
Subnet ID (20)
Subnet
Host ID (12)
10
Net ID
Host-ID
2
14
16
000000
Subnet ID (22)
Subnet
Host ID (10)
10
Net ID
Host-ID
2
14
16
1111011011
Subnet ID (26)
Subnet
Host ID (6)
e.g. Site
e.g. Dept

## Slide 48: Subnetting
Subnetting is a form of hierarchical routing.
Subnets are usually represented via an address plus a subnet mask or “netmask”.
E.g.
yganjali@apps0.cs.toronto.edu > ifconfig eth0
Link encap:Ethernet HWaddr 00:15:17:1C:85:30
inet addr:128.100.3.40 Bcast:128.100.3.255 Mask:ffffff00
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
Netmask ffffff00: the first 24 bits are the subnet ID, and the last 8 bits are the host ID.
Can also be represented by a “prefix + length”, e.g. 128.100.3.0/24, or just 128.100.3/24.

## Slide 49: Classless Inter-Domain Routing (CIDR) Addressing
The IP address space is broken into line segments.
Each line segment is described by a prefix.
A prefix is of the form x/y where x indicates the prefix of all addresses in the line segment, and y indicates the length of the segment.
E.g. The prefix 128.9/16 represents the line segment containing addresses in the range: 128.9.0.0 … 128.9.255.255.
0
232-1
128.9/16
128.9.0.0
216
142.12/19
65/8
128.9.16.14

## Slide 50: Classless Inter-Domain Routing (CIDR) – Addressing
0
232-1
128.9/16
128.9.16.14
128.9.16/20
128.9.176/20
128.9.19/24
128.9.25/24
Most specific route = “longest matching prefix”

## Slide 51: Classless Inter-Domain Routing (CIDR) – Addressing
Prefix aggregation:
If a service provider serves two organizations with prefixes, it can (sometimes) aggregate them to form a shorter prefix. Other routers can refer to this shorter prefix, and so reduce the size of their address table.
E.g. ISP serves 128.9.14.0/24 and 128.9.15.0/24, it can tell other routers to send it all packets belonging to the prefix 128.9.14.0/23.
ISP Choice:
In principle, an organization can keep its prefix if it changes service providers.

## Slide 52: Detour: Map Computer Names to IP addresses The Domain Naming System (DNS)
Names are hierarchical and belong to a domain:
  e.g. apps0.cs.utoronto.ca
  Common domain names: .com, .edu, .gov, .org, .net, .ca (or other country-specific domain).
  Top-level names are assigned by the Internet Corporation for Assigned Names and Numbers (ICANN).
  A unique name is assigned to each organization.
DNS Client-Server Model
  DNS maintains a hierarchical, distributed database of names.
  Servers are arranged in a hierarchy.
  Each domain has a “root” server.
  An application needing an IP address is a DNS client.

## Slide 53: Mapping Computer Names to IP addresses The Domain Naming System (DNS)
A DNS Query
  Client asks local server.
  If local server does not have address, it asks the root server of the requested domain.
  Addresses are cached in case they are requested again.
.stanford.edu
.berkeley.edu
.eecs.berkeley.edu
.edu
“What is the IP address of
www.eecs.berkeley.edu?”
e.g. gethostbyname()
Client
application
Example: On CDF machines, try “host www.eecs.berkeley.edu”

## Slide 54: An Aside – Error Reporting (ICMP) and traceroute
On CDF machines try: traceroute www.google.com
traceroute to www.google.com (74.125.159.147), 30 hops max, 40 byte packets
1 butler.syslab.sandbox (192.168.70.100) 0.103 ms 0.092 ms 0.082 ms
2 foundry0.cs.toronto.edu (128.100.5.210) 2.146 ms 4.061 ms 5.977 ms
3 sf-cs1.gw.utoronto.ca (128.100.1.253) 2.184 ms 2.175 ms 2.168 ms
4 murus-gpb.gw.utoronto.ca (128.100.96.2) 2.146 ms 2.483 ms 3.037 ms
5 skye2murus-blue.gw.utoronto.ca (128.100.200.210) 7.088 ms 7.207 ms 7.198 ms
6 murus2skye-yellow.gw.utoronto.ca (128.100.200.217) 3.310 ms 11.325 ms 12.061 ms
7 ut-hub-utoronto-if.gtanet.ca (205.211.94.129) 12.681 ms 2.541 ms 2.535 ms
8 ORION-GTANET-RNE.DIST1-TORO.IP.orion.on.ca (66.97.23.57) 3.638 ms 4.391 ms 4.384 ms
9 BRDR2-TORO-GE2-1.IP.orion.on.ca (66.97.16.121) 4.368 ms 4.729 ms 4.844 ms
10 74.125.51.233 (74.125.51.233) 12.459 ms 12.453 ms 12.808 ms
11 216.239.47.114 (216.239.47.114) 4.681 ms 4.795 ms 12.661 ms
12 209.85.250.111 (209.85.250.111) 23.666 ms 23.659 ms 13.226 ms
13 209.85.242.215 (209.85.242.215) 32.436 ms 32.431 ms 32.913 ms
14 72.14.232.213 (72.14.232.213) 33.537 ms 72.14.232.215 (72.14.232.215) 33.525 ms 72.14.232.213 (72.14.232.213) 164.315 ms
15 209.85.254.14 (209.85.254.14) 45.864 ms 209.85.254.10 (209.85.254.10) 42.232 ms 209.85.254.6 (209.85.254.6) 42.346 ms
16 yi-in-f147.google.com (74.125.159.147) 34.728 ms 34.727 ms 34.713 ms

## Slide 55: An Aside – Error Reporting (ICMP) and traceroute
Internet Control Message Protocol
  Used by a router/end-host to report some types of error:
    E.g. Destination Unreachable: packet can’t be forwarded to/towards its destination.
    E.g. Time Exceeded: TTL reached zero, or fragment didn’t arrive in time. traceroute uses this error to its advantage.
  An ICMP message is an IP datagram, and is sent back to the source of the packet that caused the error.

## Slide 56: Summary
Shuttling data from one link to another
  Bits, frames, packets, …
  Repeaters/hubs, bridges/switches, routers, …
Key ideas in switches
  Cut-through switching
  Self learning of the switch table
  Spanning trees
Internet Protocol
  Addresses, subnets, CIDR
  DNS, Traceroute, ICMP