## Slide 1: Handout # 7: The Internet Protocol, Routing and Forwarding
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
yganjali@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali
CSC 458/2209 – Computer Networks

## Slide 2: Announcements
Don’t forget the programming assignment.
  Due: Friday Oct. 11th at 5pm.
  Take advantage of tutorials, and piazza.
  Don’t leave it to the last minute.
Problem set 1 out on Sep. 24th
  Friday Oct. 4th at 5 pm
  Submit electronically on MarkUs.
  File name: ps1.pdf
This week’s tutorial
  Problem set 1

## Slide 3: Announcements – Cont’d
Reading for next week
  Chapter 4 of the textbook
Midterm exam
  Section L0101: Thu. Oct. 17th, 1-3 PM
  Section L5101: Tue. Oct. 22nd, 6-8 PM
  Section L0201: Tue. Oct. 22nd, 1-3 PM
  Same room and time as the lecture
  For undergraduate and graduate students

## Slide 4: The Story
So far …
  Layers, and protocols
  Link layer
  Interconnecting LANs
    Hubs, switches, and bridges
  The Internet Protocol
    IP datagram, fragmentation
    Naming and addressing
    CIDR, DNS
This time
  Routing and forwarding
Physical
Data Link
Network
Transport
Session
Presentation
Application

## Slide 5: Packet Routing and Forwarding
Forwarding IP datagrams
  Class-based vs. CIDR
Routing Techniques
  Naïve: Flooding
  Distance vector: Distributed Bellman Ford Algorithm
  Link state: Dijkstra’s Shortest Path First-based Algorithm

## Slide 6: Hop-by-Hop Packet Forwarding
Each router has a forwarding table
  Maps destination addresses…
  … to outgoing interfaces
Upon receiving a packet
  Inspect the destination IP address in the header
  Index into the table
  Determine the outgoing interface
  Forward the packet out that interface
Then, the next router in the path repeats
  And the packet travels along the path to the destination

## Slide 7: Inside a Router
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress

## Slide 8: Inside a Router
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Forwarding
Decision
Forwarding
Table

## Slide 9: Forwarding in an IP Router
Lookup packet DA in forwarding table.
  If known, forward to correct port.
  If unknown, drop packet.
Decrement TTL, update header Checksum.
Forward packet to outgoing interface.
Transmit packet onto link.
Question: How is the address looked up in a real router?

## Slide 10: Separate Table Entries Per Address
If a router had a forwarding entry per IP address
  Match destination address of incoming packet
  … to the forwarding-table entry
  … to determine the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
Forwarding Table

## Slide 11: Separate Entry Class-based Address
If the router had an entry per class-based prefix
  Mixture of Class A, B, and C addresses
  Depends on the first couple of bits of the destination
Identify the mask automatically from the address
  First bit of 0: class A address (/8)
  First two bits of 10: class B address (/16)
  First three bits of 110: class C address (/24)
Then, look in the forwarding table for the match
  E.g., 1.2.3.4 maps to 1.2.3.0/24
  Then, look up the entry for 1.2.3.0/24
  … to identify the outgoing interface

## Slide 12: Example – Class-based Addressing
Class A
Class B
Class C
D
212.17.9.4
Class A
Class B
Class C
212.17.9.0
Port 4
Exact
Match
Routing Table:
IP Address Space
212.17.9.0
Exact Match: There are many well-known ways to find an exact match in a table.

## Slide 13: CIDR Makes Packet Forwarding Harder
There’s no such thing as a free lunch
  CIDR allows efficient use of the limited address space
  But, CIDR makes packet forwarding much harder
Forwarding table may have many matches
  E.g., table entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 14: Longest Prefix Match Forwarding
Forwarding tables in IP routers
  Maps each IP prefix to next-hop link(s)
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups

## Slide 15: How a Router Forwards Datagrams
128.9/16
128.9.16/20
128.9.176/20
128.9.19/24
128.9.25/24
142.12/19
65/8
Prefix
Port
3
2
2
7
2
1
3
128.17.14.1
128.17.14.1
128.17.20.1
128.17.10.1
128.17.14.1
128.17.16.1
128.17.16.1
Next-hop
R1
R2
R3
R4
1
2
3
128.17.20.1
128.17.16.1
e.g. 128.9.16.14 => Port 2
Forwarding Table

## Slide 16: Simplest Algorithm is Too Slow
Scan the forwarding table one entry at a time
  See if the destination matches the entry
  If so, check the size of the mask for the prefix
  Keep track of the entry with longest-matching prefix
Overhead is linear in size of the forwarding table
  Today, that means 400,000-500,000 entries!
  And, the router may have just a few nanoseconds
  … before the next packet is arriving
Need greater efficiency to keep up with line rate
  Better algorithms
  Hardware implementations

## Slide 17: Lookup Performance Required
Line
Line Rate
Pkt­size=40B
Pkt­size=240B
T1
1.5Mbps
4.68
Kpps
0.78
Kpps
OC3
155Mbps
480
Kpps
80
Kpps
OC12
622Mbps
1.94
Mpps
323
Kpps
OC48
2.5Gbps
7.81
Mpps
1.3
Mpps
OC192
10
Gbps
31.25
Mpps
5.21
Mpps

## Slide 18: Fast Lookups
The are algorithms that are faster than linear scan
  Proportional to number of bits in the address
We can use special hardware
  Content Addressable Memories (CAMs)
  Allows look-ups on a key rather than flat address
Huge innovations in the mid-to-late 1990s
  After CIDR was introduced (in 1994)
  … and longest-prefix match was a major bottleneck

## Slide 19: Where do Forwarding Tables Come From?
Routers have forwarding tables
  Map prefix to outgoing link(s)
Entries can be statically configured
  E.g., “map 12.34.158.0/24 to Serial0/0.1”
But, this doesn’t adapt
  To failures
  To new equipment
  To the need to balance load
  …
That is where other technologies come in…
  Routing protocols, DHCP, and ARP

## Slide 20: Packet Routing and Forwarding
Forwarding IP datagrams
  Class-based vs. CIDR
Routing Techniques
  Naïve: Flooding
  Distance vector: Distributed Bellman Ford Algorithm
  Link state: Dijkstra’s Shortest Path First-based Algorithm
Routing is a very complex subject, and has many aspects.
Here, we will concentrate on the basics.

## Slide 21: The Problem
“A”
“B”
R1
R2
R3
R4
How does R1 choose a next-hop on the path towards host B?

## Slide 22: What is Routing?
A famous quotation from RFC 791
  “A name indicates what we seek. An address indicates where it is. A route indicates how we get there.” -- Jon Postel

## Slide 23: Forwarding vs. Routing
Forwarding: data plane
  Directing a data packet to an outgoing link
  Individual router using a forwarding table
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Individual router creating a forwarding table

## Slide 24: Why Does Routing Matter?
End-to-end performance
  Quality of the path affects user performance
  Propagation delay, throughput, and packet loss
Use of network resources
  Balance of the traffic over the routers and links
  Avoiding congestion by directing traffic to lightly-loaded links
Transient disruptions during changes
  Failures, maintenance, and load balancing
  Limiting packet loss and delay during changes

## Slide 25: Example Network
Objective: Determine the route from A to B that minimizes the path cost.
R7
R6
R4
R2
R1
1
1
4
2
4
2
2
3
2
3
R8
Examples of link cost:
Distance, data rate, price, congestion/delay, …
A
B
R5
R3

## Slide 26: Example Network
In this simple case, solution is clear from inspection
R7
R6
R4
R2
R1
1
1
4
2
4
2
2
3
2
3
R8
A
B
R5
R3

## Slide 27: What about this Network...!?
Learn more at
http://www.lumeta.com

## Slide 28: Technique 1: Naïve Approach
Advantages:
  Simple
  Every destination in the network is reachable.
Disadvantages:
  Some routers receive a packet multiple times.
  Packets can go round in loops forever.
  Inefficient.
Flood! -- Routers forward packets to all ports
except the ingress port.
R1

## Slide 29: Lowest Cost Routes
Objective: Find the lowest cost route from each of
(R1, …, R7) to R8.
R5
R3
R7
R6
R4
R2
R1
1
1
4
2
4
2
2
3
2
3
R8

## Slide 30: A Spanning Tree
The solution is a spanning tree with R8 as the root of the tree.
Tree: There are no loops.
Spanning: All nodes included.
We’ll see two algorithms that build spanning trees automatically:
  The distributed Bellman-Ford algorithm
  Dijkstra’s shortest path first algorithm
R3
R1
R5
R4
R8
R6
R2
R7
1
1
4
2
4
2
2
3
2
3

## Slide 31: Technique 2: Distance Vector Distributed Bellman-Ford Algorithm
Define distances at each node x
  dx(y) = cost of least-cost path from x to y
Update distances based on neighbors
  dx(y) = min {c(x,v) + dv(y)} over all neighbors v
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) = min{c(u,v) + dv(z),
c(u,w) + dw(z)}

## Slide 32: Distance Vector Algorithm
c(x,v) = cost for direct link from x to v
  Node x maintains costs of direct links c(x,v)
Dx(y) = estimate of least cost from x to y
  Node x maintains distance vector Dx = [Dx(y): y є N ]
Node x maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Each node v periodically sends Dv to its neighbors
  And neighbors update their own distance vectors
  Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Over time, the distance vector Dx converges

## Slide 33: Distance Vector Algorithm
Iterative, asynchronous: each local iteration caused by:
  Local link cost change
  Distance vector update message from neighbor
Distributed:
  Each node notifies neighbors only when its DV changes
  Neighbors then notify their neighbors if necessary
wait for (change in local link cost or message from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors
Each node:

## Slide 34: Distance Vector Example: Step 1
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C |  | –
D | 3 | D
E |  | –
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A |  | –
B |  | –
C | 0 | C
D | 1 | D
E |  | –
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A |  | –
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F |  | –
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B |  | –
C |  | –
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 6 | A
B | 1 | B
C | 1 | C
D |  | –
E | 3 | E
F | 0 | F
Optimum 1-hop paths

## Slide 35: Distance Vector Example: Step 2
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 7 | F
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 7 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 2-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 36: Distance Vector Example: Step 3
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 6 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E | 5 | C
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D | 5 | F
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 3-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 37: Bellman-Ford Algorithm
Questions:
  How long can the algorithm take to run?
  How do we know that the algorithm always converges?
  What happens when link costs change, or when routers/links fail?
Topology changes make life hard for the Bellman-Ford algorithm…

## Slide 38: A Problem with Bellman-Ford Bad news travels slowly
R4
R3
R2
R1
1
1
1
Consider the calculation of distances to R4:
…
…
…
…
5,R2
4,R3
5,R2
3
3,R2
4,R3
3,R2
2
3,R2
2,R3
3,R2
1
1, R4
2,R3
3,R2
0
R3
R2
R1
Time
“Counting to infinity”
R3 R4 fails

## Slide 39: Counting to Infinity Problem – Solutions
Set infinity = “some small integer” (e.g. 16). Stop when count = 16.
Split Horizon: Because R2 received lowest cost path from R3, it does not advertise cost to R3
Split-horizon with poison reverse: R2 advertises infinity to R3
There are many problems with (and fixes for) the Bellman-Ford algorithm.

## Slide 40: Technique 3: Link State Dijkstra’s Shortest Path First Algorithm
Routers send out update messages whenever the state of an incident link changes.
  Called “Link State Updates”
Based on all link state updates received each router calculates lowest cost path to all others, starting from itself.
  Use Dijkstra’s single-source shortest path algorithm
  Assume all updates are consistent
At each step of the algorithm, router adds the next shortest (i.e. lowest-cost) path to the tree.
Finds spanning tree rooted at the router.

## Slide 41: Dijsktra’s Algorithm
1 Initialization:
2 S = {u}
3 for all nodes v
4 if v adjacent to u {
5 D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in S with the smallest D(w)
10 add w to S
11 update D(v) for all v adjacent to w and not in S:
12 D(v) = min{D(v), D(w) + c(w,v)}
13 until all nodes in S

## Slide 42: Dijkstra’s Algorithm Example Find Routes for the Red (Leftmost) Node
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3

## Slide 43: Dijkstra’s Algorithm Example
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3

## Slide 44: Shortest-Path Tree
Shortest-path tree from u
Forwarding table at u
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)

## Slide 45: Reliable Flooding of LSP
The Link State Packet:
  The ID of the router that created the LSP
  List of directly connected neighbors, and cost
  Sequence number
  TTL
Reliable Flooding
  Resend LSP over all links other than incident link, if the sequence number is newer. Otherwise drop it.
Link State Detection:
  Link layer failure
  Loss of “hello” packets

## Slide 46: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) messages sent
DV: exchange between neighbors only
  Convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) messages
DV: convergence time varies
  May be routing loops
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  Each node’s table used by others (error propagates)