IPNL: A NAT-Extended Internet Architecture

This paper presents and analyzes IP Next Layer (IPNL), a NAT extended

Internet protocol architecture designed to scalablly solve the address

depletion problem of IPv4. In this approach only hosts and NAT boxes

are modified, and IPv4 routers and support protocols remain untouched.

Using NAT has pros and cons. The most important benefits of NAT are

expanding the IPV4 address space, and isolating a site’s address space

from the global address space. Disadvantages of NAT are inhibiting certain

kinds of peer-to-peer applications, and complicating scalable network

operation and new protocol and application design. IPNL tries to use NAT

extension instead of IPV6 as a long term architecture.

The IPNL topology is the same as today’s Internet topology: privately-

addressed realms connected to the globally-addressed Internet, and,

sometimes, to each other, by NAT boxes. To IP routers in a realm, an

nl-router appears to be just another host. To nl-routers, a realm appears

to be a multi-access nonbroadcast “link”.

IPNL utilizes Fully Qualified Domain Names (FQDNs) as an end-to-end

host identifier in packets. The FQDN header contains the source and

destination FQDNs of the packet. IPNL addresses are 10 bytes long, and

consist of three parts: a 4-byte globally unique IP address called the Middle

Realm IP address (MRIP), a 2-byte Realm Number (RN), and a 4-byte IP

address, called End Host IP (EHIP) address.

When a host initiates a connection, it only knows three addresses: its own

FQDN, its own EHIP, and the FQDN of the destination. In particular, it does

not know its own MRIP and RN. It learns the destination host MRIPs by

transmitting a message to a frontdoor asking that frontdoor to do a middle

realm DNS lookup for the destination. But it does not know the destination’s

RN and EHIP when it transmits its first packet. Instead, the source MRIP and

RN, as well as the destination RN and EHIP, are written into the packets

the packet travels from source to destination. Authors have implemented a

testbed for IPNL evaluation in Linux 2.2.16, and they have seen no degradation

in network performance after adding IPLN layer.

The approach of the paper is interesting and new. It tries to keep IPV4 infrastructure

using NATs to solve IPV4 address depletion. However, from my point of view,

replacing IPV4 by IPV6 is a better approach. The most important benefit of NAT extension over IPV6 can bet its less cost, but as we see in the paper, authors are not

sure that NAT extension is less costly than IPV6. I believe that complications that NAT imposes on the network limits innovations and new protocols. Therefore, it will be

worth to implement IPV6 even its cost is higher reasonably compared to NAT.