## Slide 1
Learning Complex Dexterous Manipulation with Deep Reinforcement Learning and Demonstrations
Aravind Rajeswaran , Vikash Kumar , Abhishek Gupta, Giulia Vezzani , John Schulman , Emanuel Todorov , Sergey Levine
Jason Rebello
UTIAS

## Slide 2
Overview
Motivation
Contributions
Methodology
Experiments
Future Work

## Slide 3
Motivation
Dextrous multi-fingered hands are extremely versatile
Control is challenging due to high dimensionality, complex contact patterns
Previous methods require reward shaping
DRL limited to simpler manipulators and simple tasks
Lack of physical systems due to sample inefficiency
Object relocation task

## Slide 4
Contributions
Manipulation with 24-DOF hand
Model Free DRL
Used in complex tasks with variety of tools
Small number of human demonstrations reduces sample complexity
Reduces learning time
Robust and natural movements
Tool use task

## Slide 5
Manipulation Task 1
Object Relocation
Move Blue ball to green position
Task complete when ball is epsilon ball away from target
Positions of ball and target are randomized
Main challenge is exploration (reach object, grab and move to target location)

## Slide 6
Manipulation Task 2
In-hand Manipulation
Reposition blue pen to match orientation of green target
Task complete when orientation is achieved
Base of hand is fixed
Large number of contacts with complex solutions
Used a well shaped reward for training an expert

## Slide 7
Manipulation Task 3
Door Opening
Undo latch and swing door open
Task complete when door touches door stopper
No information of latch explicitly provided
A lot of hidden sub-tasks
Position of door is randomized

## Slide 8
Manipulation Task 4
Tool Use
Pickup and hammer nail
Task complete when entire nail is inside the board
Use tool instead of just relocation
Multiple steps in task

## Slide 9
Experimental Setup
ADROIT hand
24-DOF hand
First, middle, ring – 4 DOF each
Little finger, thumb – 5 DOF each
Wrist – 2 DOF
Actuated with position control and has joint angle sensor
MuJoCo physics simulation with friction
25 demonstrations for each task
HAPTIX Simulator
CyberGlove 3
HTC headset

## Slide 10
Methodology (Preliminaries)
MDP definition:
Value function:
Q function:
Advantage function:
States
Actions
Rewards
Transition dynamics
Initial Probability distribution
Discount Factor
Reward for taking action a in state s
Expected reward in state s’

## Slide 11
Methodology (NPG)
Directly optimize parameters of policy to maximize objective
Vanilla Policy Gradient:
Fisher Information Matrix:
Sub-optimal
Fisher information matrix measures the curvature (sensitivity) of policy relative to model parameters
Fisher information matrix is related to the Hessian matrix

## Slide 12
Methodology (NPG)
Limit policy change based on parameter change
Fisher information matrix maps between parameter space and policy space
Generally use learning rate in optimization
Poor step size leads to poor initialization
Use Fisher information matrix to perform update
Gradient ascent update:
Steepest Ascent direction
Normalized step-size

## Slide 13
Methodology (Problems with RL)
Challenges with using NPG
  RL requires careful reward shaping
  Impractical number of samples to learn (approx. 100 hours)
  Unnatural movement
  Not as robust to environmental variations
Solution
  Combine RL with demonstrations
  Guide exploration and decrease sample complexity
  Robust and natural looking behaviour
  Demonstration Augmented Policy Gradient (DAPG)

## Slide 14
Methodology (Pretraining with BC)
Exploration in PG achieved with stochastic action distribution
Poor initialization leads to slow exploration
Behavioral Cloning (BC) guides exploration
Reduces sample complexity
Mimic actions taken in demonstrations
Does not guarantee effectiveness of policy due to distributional shift

## Slide 15
Methodology (Fine-tuning with augmented loss)
BC does not make optimal use of demonstrations
Cannot learn subtasks (reaching, grasping, hammering)
BC policy (only grasping)
Capturing all data
Weighting function
Dataset from policy
iteration
hyperparameters
Dataset from demonstrations
Behavioral cloning
Policy gradient

## Slide 16
Results 1
Reinforcement learning from scratch
Can RL cope with high dimensional manipulation tasks ?
Is it robust to variations in environment ?
Are movements safe and can they be used on real hardware ?
Compare NPG vs DDPG (Deep Deterministic Policy Gradient)
DDPG is a policy gradient actor-critic algorithm that is off-policy
Stochastic policy for exploration, estimates deterministic policy
Score based on percentage of successful trajectories (100 samples)
Sparse Reward vs Reward shaping

## Slide 17
Results 1
Reinforcement learning from scratch
NPG learns with reward shaping, DDPG fails to learn
DDPG is sample efficient but sensitive to hyper-parameters
Resulting policies have unnatural behaviors
Poor sample efficiency, cant use on hardware
Cannot generalize to unseen environment (weight and ball size change)

## Slide 18
Results 2
Reinforcement learning with demonstrations
Does incorporating demonstrations reduce learning time?
Comparison of DAPG vs DDPGfD (.. from Demonstrations)?
Does it result in human like behaviour ?
DDPGfD better version of DDPG (demonstrations in replay buffer, prioritized experience replay, n-step returns, regularization)
Only use sparse rewards

## Slide 19
Results 2
Reinforcement learning with demonstrations
DAPG outperforms DDPGfD
DAPG requires few robot hours
Can be used on real hardware
Robust and human behavior
Generalizes to unseen environment
NPG
# RL iterations to achieve 90% success

## Slide 20
Future Work
Tests on real hardware
Reduce sample complexity using novelty based exploration methods
Learn policies from raw visual inputs and tactile sensing

## Slide 21
Results

## Slide 22: Thank you & Questions ?
Questions

## Slide 23
Related Works
Model-based trajectory Optimization
  Useful when dynamics can be relaxed (computer animation)
  Cant translate to real-world systems
  Learning complex models is tough with contact dynamics
Model-free RL
  Optimize policy directly
  Don’t require to know dynamics
  Require large number of real-world samples

## Slide 24
Related Works
Imitation Learning (Behaviour Cloning)
  Demonstrations of successful behaviour
  Used to bootstrap RL
  Distribution Drift
  Cannot exceed capabilities of demonstrator
RL with demonstrations
  Sample complexity reduces
  Require large number of samples for complex tasks

## Slide 25
Contributions
Dexterous manipulation in simulation with high dimensional hand using
model free DRL
Using a small number of demonstrations to reduce sample complexity
Policies with demonstrations robust to environmental changes
Propose a set of manipulation tasks