## Slide 1: Exploiting Compressed Block Size as an Indicator of Future Reuse
Gennady Pekhimenko,
Tyler Huberty, Rui Cai,
Onur Mutlu, Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 2: Executive Summary
In a compressed cache, compressed block size is an additional dimension
Problem: How can we maximize cache performance utilizing both block reuse and compressed size?
Observations:
  Importance of the cache block depends on its compressed size
  Block size is indicative of reuse behavior in some applications
Key Idea: Use compressed block size in making cache replacement and insertion decisions
Results:
  Higher performance (9%/11% on average for 1/2-core)
  Lower energy (12% on average)

## Slide 3: Potential for Data Compression
Compression Ratio
Latency
0.5
1.5
1.0
2.0
FPC
X
C-Pack
X
BDI
X
SC2
X
Frequent Pattern
Compression (FPC)
[Alameldeen+, ISCA’04]
C-Pack [Chen+,
Trans. on VLSI’10]
Base-Delta-Immediate (BDI)
[Pekhimenko+, PACT’12]
Statictical Compression
(SC2) [Arelakis+, ISCA’14]
5 cycles
9 cycles
1-2 cycles
8-14 cycles
Can we do better?
All use LRU replacement policy
All these works showed significant performance improvements

## Slide 4: Size-Aware Cache Management
Compressed block size matters
Compressed block size varies
Compressed block size can indicate reuse

## Slide 5: #1: Compressed Block Size Matters
A
Y
B
Cache:
X
miss
hit
A
Y
hit
B
miss
C
miss
C
time
X
miss
hit
B
C
time
A
Y
miss
hit
hit
Belady’s OPT Replacement
Size-Aware Replacement
saved cycles
Size-aware policies could yield fewer misses
X A Y B C
Access stream:
large
small

## Slide 6: #2: Compressed Block Size Varies
Chart: Cache Coverage, %
 | 95747 | 74979 | 2102620 | 375881841 | 50813 | 2233065 | 12892190 | 1907038 | 5443123
 | 591 | 12817602 | 1006006 | 419865 | 5819 | 2888878 | 994569 | 745306 | 329320
 | 1286278 | 879730 | 16461026 | 14614264 | 119491 | 11576435 | 317339 | 5062854 | 15140710
 | 101237209 | 1202307 | 169424087 | 34810743 | 84860 | 1509034 | 309028 | 3195618 | 86700988
 | 438661822 | 793833 | 670753253 | 50533937 | 194054 | 97922655 | 518059 | 6346086 | 60228812
 | 1596238818 | 828881 | 281444015 | 72471798 | 191533 | 2363534 | 690912 | 15479836 | 62365042
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 208129457 | 1192267355 | 240781337 | 500266655 | 574276 | 4743877 | 2242311 | 14040601 | 5767781
Compressed block size varies within and between applications
Block size, bytes
BDI compression algorithm [Pekhimenko+, PACT’12]

## Slide 7: #3: Block Size Can Indicate Reuse
bzip2
Block size, bytes
Different sizes have different dominant reuse distances

## Slide 8: Code Example to Support Intuition
int A[N]; // small indices: compressible
double B[16]; // FP coefficients: incompressible
for (int i=0; i<N; i++) {
int idx = A[i];
for (int j=0; j<N; j++) {
sum += B[(idx+j)%16];
}
}
long reuse, compressible
short reuse, incompressible
Compressed size can be an indicator of reuse distance

## Slide 9: Size-Aware Cache Management
Compressed block size matters
Compressed block size varies
Compressed block size can indicate reuse

## Slide 10: Outline
Motivation
Key Observations
Key Ideas:
  Minimal-Value Eviction (MVE)
  Size-based Insertion Policy (SIP)
Evaluation
Conclusion

## Slide 11: Compression-Aware Management Policies (CAMP)
CAMP
MVE:
Minimal-Value Eviction
SIP:
Size-based
Insertion Policy

## Slide 12: Minimal-Value Eviction (MVE): Observations
Define a value (importance) of the block to the cache
Evict the block with the lowest value
Block #0
Block #1
Block #N
…
Highest priority: MRU
Lowest priority: LRU
Set:
Block #X
Block #X
…
Importance of the block depends on both the likelihood of reference and the compressed block size
Highest value
Lowest value

## Slide 13: Minimal-Value Eviction (MVE): Key Idea
Value =
Probability of reuse
Compressed block size
Probability of reuse:
Can be determined in many different ways
Our implementation is based on re-reference interval prediction value (RRIP [Jaleel+, ISCA’10])

## Slide 14: Compression-Aware Management Policies (CAMP)
CAMP
MVE:
Minimal-Value Eviction
SIP:
Size-based
Insertion Policy

## Slide 15: Size-based Insertion Policy (SIP): Observations
Sometimes there is a relation between the compressed block size and reuse distance
compressed
block size
data structure
This relation can be detected through the compressed block size
Minimal overhead to track this relation (compressed block information is a part of design)
reuse distance

## Slide 16: Size-based Insertion Policy (SIP): Key Idea
Insert blocks of a certain size with higher priority if this improves cache miss rate
Use dynamic set sampling [Qureshi, ISCA’06] to detect which size to insert with higher priority
set A
set B
set C
set D
set E
set G
set H
set F
set I
Main Tags
set A
8B
Auxiliary Tags
set D
64B
set F
8B
set I
64B
set A
set F
+ CTR8B -
…
miss
set F
8B
set A
8B
…
miss
decides policy
for steady state

## Slide 17: Outline
Motivation
Key Observations
Key Ideas:
  Minimal-Value Eviction (MVE)
  Size-based Insertion Policy (SIP)
Evaluation
Conclusion

## Slide 18: Methodology
Simulator
  x86 event-driven simulator (MemSim [Seshadri+, PACT’12])
Workloads
  SPEC2006 benchmarks, TPC, Apache web server
  1 – 4 core simulations for 1 billion representative instructions
System Parameters
  L1/L2/L3 cache latencies from CACTI
  BDI (1-cycle decompression) [Pekhimenko+, PACT’12]
  4GHz, x86 in-order core, cache size (1MB - 16MB)

## Slide 19: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy - size-unaware
RRIP | Re-reference Interval Prediction [Jaleel+, ISCA’10] - size-unaware

## Slide 20: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy - size-unaware
RRIP | Re-reference Interval Prediction [Jaleel+, ISCA’10] - size-unaware
ECM | Effective Capacity Maximizer [Baek+, HPCA’13] + size-aware

## Slide 21: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy - size-unaware
RRIP | Re-reference Interval Prediction [Jaleel+, ISCA’10] - size-unaware
ECM | Effective Capacity Maximizer [Baek+, HPCA’13] + size-aware
CAMP | Compression-Aware Management Policies (MVE + SIP)

## Slide 22: Size-Aware Replacement
Effective Capacity Maximizer (ECM)
[Baek+, HPCA’13]
  Inserts “big” blocks with lower priority
  Uses heuristic to define the threshold
Shortcomings
  Coarse-grained
  No relation between block size and reuse
  Not easily applicable to other cache organizations

## Slide 23: CAMP Single-Core
Chart: Normalized IPC
 | 1.1359 | 1.1822 | 1.0085 | 1.0102 | 1.0013 | 1.2166 | 0.96715 | 1.0362 | 0.92631 | 1.0075 | 1.0303 | 1.0056 | 1.0038 | 1.1624 | 1.0379 | 1.0003 | 0.95642 | 1.0021 | 1.0008 | 1.0918 | 1.0293 | 0.99622 | 1.0028 | 1.0532 | 1.0329
 | 1.1234 | 1.1422 | 1.0065 | 1.0071 | 0.99131 | 1.2538 | 0.9726 | 1.0324 | 0.92879 | 1.009 | 1.0455 | 1.0042 | 1.0063 | 1.1854 | 1.0483 | 1.0014 | 0.98478 | 1.0031 | 0.99943 | 1.097 | 1.0304 | 1.0015 | 1.0147 | 1.059 | 1.0362
 | 1.1663 | 1.1822 | 1.0124 | 1.0172 | 1.0026 | 1.2189 | 0.96722 | 1.0443 | 0.92631 | 1.0169 | 1.041 | 1.0085 | 1.0051 | 1.2072 | 1.0709 | 1.0057 | 0.96821 | 1.0022 | 0.98551 | 1.1059 | 1.0327 | 0.99581 | 1.011 | 1.063 | 1.0405
 | 1.136 | 1.1821 | 1.0174 | 1.0108 | 1.0013 | 1.3126 | 0.99881 | 1.0394 | 0.99843 | 1.0089 | 1.0504 | 1.0056 | 1.0037 | 1.1815 | 1.0394 | 1.0006 | 0.96152 | 1.0021 | 1.0008 | 1.0955 | 1.0303 | 0.99892 | 1.0061 | 1.072 | 1.0442
 | 1.1633 | 1.1821 | 1.0208 | 1.0179 | 1.0027 | 1.3149 | 0.99882 | 1.0434 | 0.99843 | 1.017 | 1.051 | 1.0086 | 1.0052 | 1.2272 | 1.0736 | 1.0115 | 0.9704 | 1.0025 | 0.99667 | 1.1076 | 1.0342 | 0.99855 | 1.0131 | 1.0816 | 1.0516
SPEC2006, databases, web workloads, 2MB L2 cache
CAMP improves performance over LRU, RRIP, ECM
31%
8%
5%

## Slide 24: Multi-Core Results
Classification based on the compressed block size distribution
  Homogeneous (1 or 2 dominant block size(s))
  Heterogeneous (more than 2 dominant sizes)
We form three different 2-core workload groups (20 workloads in each):
  Homo-Homo
  Homo-Hetero
  Hetero-Hetero

## Slide 25: Multi-Core Results (2)
Chart: Normalized Weighted Speedup
 | 1.0136 | 1.0324 | 1.0529 | 1.0328
 | 1.0172 | 1.0444 | 1.0669 | 1.0426
 | 1.0192 | 1.0442 | 1.0739 | 1.0455
 | 1.0228 | 1.039 | 1.0749 | 1.0453
 | 1.0314 | 1.0659 | 1.0816 | 1.0594
CAMP outperforms LRU, RRIP and ECM policies
Higher benefits with higher heterogeneity in size

## Slide 26: Effect on Memory Subsystem Energy
Chart: Normalized Energy
| astar | cactusADM | gcc | gobmk | h264ref | soplex | zeusmp | bzip2 | GemsFDTD | gromacs | leslie3d | perlbench | sjeng | sphinx3 | xalancbmk | milc | omnetpp | libquantum | lbm | mcf | tpch2 | tpch6 | apache | GMeanIntense | GMeanAll
RRIP | 0.91445 | 0.77376 | 0.98478 | 0.98594 | 1.0063 | 0.83878 | 1.044 | 0.94293 | 1.113 | 0.9923 | 1.0315 | 0.97103 | 0.9932 | 0.84952 | 0.8629 | 0.99861 | 1.0608 | 0.99879 | 1.0013 | 0.95106 | 0.97716 | 1.0052 | 1.0265 | 0.95011 | 0.96744
ECM | 0.91857 | 0.80075 | 0.97786 | 0.98732 | 0.99691 | 0.81331 | 1.0404 | 0.91982 | 1.1114 | 0.98096 | 1.0161 | 0.95417 | 0.99036 | 0.81866 | 0.83857 | 0.99805 | 1.0281 | 0.99864 | 1.0045 | 0.95812 | 0.97735 | 1.0057 | 1.0166 | 0.94296 | 0.95991
CAMP | 0.89718 | 0.79128 | 0.97016 | 0.97735 | 0.99074 | 0.81071 | 1.0022 | 0.91683 | 1.0021 | 0.96585 | 1.0117 | 0.95638 | 0.98796 | 0.79316 | 0.77993 | 0.99677 | 1.002 | 0.99874 | 1.0036 | 0.93621 | 0.96631 | 0.99778 | 1.0193 | 0.91797 | 0.94341
CAMP reduces energy consumption in the memory subsystem
5%
L1/L2 caches, DRAM, NoC, compression/decompression

## Slide 27: CAMP for Global Replacement
G-CAMP
G-MVE:
Global Minimal-Value Eviction
G-SIP:
Global Size-based
Insertion Policy
CAMP with V-Way [Qureshi+, ISCA’05] cache design
Reuse Replacement instead of RRIP
Set Dueling instead of Set Sampling

## Slide 28: G-CAMP Single-Core
SPEC2006, databases, web workloads, 2MB L2 cache
G-CAMP improves performance over LRU, RRIP, V-Way
Chart: Normalized IPC
 | 1.1359 | 1.1822 | 1.0085 | 1.0102 | 1.0013 | 1.2166 | 0.96715 | 1.0362 | 0.92631 | 1.0075 | 1.0303 | 1.0056 | 1.0038 | 1.1624 | 1.0379 | 1.0003 | 0.95642 | 1.0021 | 1.0008 | 1.0918 | 1.0293 | 0.99622 | 1.0028 | 1.0532 | 1.0329
 | 1.0886 | 1.2038 | 1.0061 | 1.0097 | 0.97356 | 1.6372 | 1.0152 | 1.0432 | 1.007 | 1.0045 | 1.0257 | 1.004 | 1.002 | 1.0491 | 1.0522 | 1.0015 | 1.0328 | 1.0012 | 1.0041 | 1.1194 | 1.0222 | 1.0122 | 1.0159 | 1.0868 | 1.0514
 | 1.1737 | 1.2038 | 1.0337 | 1.1072 | 1.0058 | 1.9266 | 1.0152 | 1.0509 | 1.007 | 0.96924 | 1.0371 | 1.0151 | 1.0063 | 1.2517 | 0.87169 | 1.0281 | 0.89181 | 1.0117 | 0.95666 | 1.2421 | 0.86677 | 1.0127 | 0.994 | 1.0861 | 1.0576
 | 1.1713 | 1.2038 | 1.001 | 1.0017 | 0.98823 | 1.7116 | 1.0152 | 1.0415 | 1.007 | 1.0054 | 1.0221 | 1.0085 | 1.0013 | 1.0917 | 1.0816 | 0.99971 | 1.0365 | 1.0012 | 1.0091 | 1.226 | 1.0348 | 1.0129 | 1.0165 | 1.1116 | 1.0651
 | 1.1697 | 1.2038 | 1.0355 | 1.1031 | 1.0058 | 1.9757 | 1.0152 | 1.0504 | 1.007 | 1.0047 | 1.0586 | 1.0103 | 1.0058 | 1.2513 | 1.0556 | 1.015 | 1.0333 | 1.0125 | 1.0161 | 1.2687 | 1.0247 | 1.0131 | 1.0168 | 1.1401 | 1.0888
14%
9%

## Slide 29: Storage Bit Count Overhead
Designs (with BDI) | LRU | CAMP | V-Way | G-CAMP
tag-entry | +14b | +14b | +15b | +19b
data-entry | +0b | +0b | +16b | +32b
total | +9% | +11% | +12.5% | +17%
Over uncompressed cache with LRU
2%
4.5%

## Slide 30: Cache Size Sensitivity
Chart: Normalized IPC
 | 1 | 1.0656 | 1.1157 | 1.2521 | 1.3885
 | 1.011 | 1.1007 | 1.1534 | 1.2954 | 1.3995
 | 1.0196 | 1.1043 | 1.1621 | 1.3066 | 1.4111
 | 1.0276 | 1.1217 | 1.1704 | 1.3132 | 1.4233
 | 1.0248 | 1.1204 | 1.2304 | 1.3996 | 1.4487
 | 1.0527 | 1.1603 | 1.271 | 1.4423 | 1.4873
CAMP/G-CAMP outperforms prior policies for all $ sizes
G-CAMP outperforms LRU with 2X cache sizes

## Slide 31: Other Results and Analyses in the Paper
Block size distribution for different applications
Sensitivity to the compression algorithm
Comparison with uncompressed cache
Effect on cache capacity
SIP vs. PC-based replacement policies
More details on multi-core results

## Slide 32: Conclusion
In a compressed cache, compressed block size is an additional dimension
Problem: How can we maximize cache performance utilizing both block reuse and compressed size?
Observations:
  Importance of the cache block depends on its compressed size
  Block size is indicative of reuse behavior in some applications
Key Idea: Use compressed block size in making cache replacement and insertion decisions
Two techniques: Minimal-Value Eviction and Size-based Insertion Policy
Results:
  Higher performance (9%/11% on average for 1/2-core)
  Lower energy (12% on average)

## Slide 33: Exploiting Compressed Block Size as an Indicator of Future Reuse
Gennady Pekhimenko,
Tyler Huberty, Rui Cai,
Onur Mutlu, Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch