## Slide 1: CSC 2231: Parallel Computer Architecture and Programming Main Memory Fundamentals
Prof. Gennady Pekhimenko
University of Toronto
Fall 2017
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU

## Slide 2: Why Is Memory So Important? (Especially Today)

## Slide 3: The Performance Perspective
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 4: The Energy Perspective
Dally, HiPEAC 2015

## Slide 5: The Energy Perspective
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 6: The Reliability Perspective
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 7: The Security Perspective

## Slide 8: Why Is DRAM So Slow?

## Slide 9: Motivation (by Vivek Seshadri)
Conversation with a friend from Stanford
Why is DRAM so slow?!
Really?
50 nanoseconds to serve one request? Is that a fundamental limit to DRAM’s access latency?
Him
Vivek

## Slide 10: Understanding DRAM
What is in here?
DRAM
Problems related to today’s DRAM design
Solutions proposed by our research

## Slide 11: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 12: What is DRAM?
DRAM – Dynamic Random Access Memory
3455434
Array of Values
43543
98734
0
847
42
873909
1729
WRITE address, value
READ address
Accessing any location takes the same amount of time
Data needs to be constantly refreshed

## Slide 13: DRAM in Today’s Systems
Why DRAM? Why not some other memory?

## Slide 14: Von Neumann Model
Processor
Memory
Program
Data
T1 = Read Data[1]
T2 = Read Data[2]
T3 = T1 + T2
Write Data[3], T3
3
4
8
2
T1 = Read Data[1]
4
4 instruction accesses +
3 data accesses
Memory performance is important

## Slide 15: Factors that Affect Choice of Memory
Speed
  Should be reasonably fast compared to processor
Capacity
  Should be large enough to fit programs and data
Cost
  Should be cheap

## Slide 16: Why DRAM?
Access Latency
Cost
Flip-flops
SRAM
DRAM
Flash
Disk
Higher Cost
Higher access latency
Favorable point in the trade-off spectrum

## Slide 17: Is DRAM Fast Enough?
Processor
Commodity DRAM
Request
3 GHz, 2 Instructions / cycle
300 Instructions
300 Instructions
300 Instructions
300 Instructions
Independent programs
Request
Request
Request
Served in parallel?
Core
Core
Core
Core
Latency
Parallelism
50ns

## Slide 18: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 19
processor
main memory
peripheral logic
bank
mat
high latency
DRAM Organization

## Slide 20
DRAM Cell Array: Mat
peripheral logic
cell
mat
mat
sense amplifier
wordline driver
cell
wordline
bitline

## Slide 21
Cell Array (Mat): High Latency

## Slide 22
DRAM Cell Array: High Latency
Outside mat
Inside mat
Narrow poly wire
  Large resistance
  Large capacitance
   Slow
Small cell
  Difficult to detect data in small cell
   Slow
Thick metal wire
  Small resistance
  Small capacitance
   Fast

## Slide 23: Memory Element (Cell)
0
1
Component that can be in at least two states
Can be electrical, magnetic, mechanical, etc.
DRAM → Capacitor

## Slide 24: Capacitor – Bucket of Electric Charge
Charge
“Charged”
“Discharged”
0
0
Vmax
0
Voltage level indicator. Not part of the actual circuit

## Slide 25: DRAM Chip
Contains billions of capacitors (also called cells)
0
?
DRAM Chip

## Slide 26: Divide and Conquer
DRAM Bank
?
Weak
Reading destroys state
Challenges

## Slide 27: Sense-Amplifier
Vmax
0
Vx
Vy
Vx > Vy
Vx
Vy
Vx+δ
Vx+δ
Vy-δ
Amplify the difference
Stable state

## Slide 28: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 29: DRAM Cell Read Operation
Vmax/2
Vmax/2
0
Vmax/2 + δ
0
Vmax
Vmax
Vmax/2 + δ
DRAM
Cell
Sense-Amplifier
Cell loses charge
Amplify the difference
Restore Cell Data
Access data
1
2

## Slide 30: DRAM Cell Read Operation
0
DRAM
Cell
Sense-Amplifier
Control Signal
DRAM
Cell
Address

## Slide 31: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 32: Problem
Sense-Amplifier
Control Signal
DRAM
Cell
Address
Much larger than a cell

## Slide 33: Cost Amortization
Bitline
Wordline

## Slide 34: DRAM Array Operation
1
0
0
1
1
0
1
0
0
1
0
1
½
½
½
½
½
½
½
½
½
½
½
½
Row Decoder
1
Row Address
?
?
?
?
?
?
?
?
?
?
?
?
↑½
↑½
↑½
↑½
↑½
↑½
½↓
½↓
½↓
½↓
½↓
½↓
m
1
0
0
1
1
0
1
0
0
1
0
1
Sensing & Amplification
Charge Restoration
Wordline Disable
Charge Sharing
Wordline Enable
Access Data (column n)
Restore
Sense-Amplifier
m
n
Sense-Amplifiers

## Slide 35: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013 Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 36: DRAM Bank
How to build a DRAM bank from a DRAM array?

## Slide 37: DRAM Bank: Single DRAM Array?
10000+ rows
Row Decoder
1
0
0
1
1
0
0
1
Long bitline
Difficult to sense data in far away cells
Row Address

## Slide 38: DRAM Bank: Collection of Arrays
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Data
Subarray

## Slide 39: DRAM Operation: Summary
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Row m, Col n
m
1. Enable row m
2. Access col n
3. Close row
n
m

## Slide 40: DRAM Chip Hierarchy
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Collection of Banks
Collection of Subarrays

## Slide 41: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 42: Factors That Affect Performance
Latency
  How fast can DRAM serve a request?
Parallelism
  How many requests can DRAM serve in parallel?

## Slide 43: DRAM Chip Hierarchy
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Collection of Banks
Collection of Subarrays
Latency
Parallelism

## Slide 44: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 45: Subarray Size: Rows/Subarray
Number of rows in subarray
Latency
Chip Area

## Slide 46: Subarray Size vs. Access Latency
Smaller subarrays => lower access latency
Shorter Bitlines => Faster access

## Slide 47: Subarray Size vs. Chip Area
Large Subarray
Smaller Subarrays
Area
Cost
Smaller subarrays => larger chip area

## Slide 48: Chip Area vs. Access Latency
Chart: Access Latency (ns)
| 23.10725021132788 | 24.617764350044737 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
Commodity DRAM
(512 rows/subarray)
32 rows/subarray
Why is DRAM so slow?

## Slide 49: Chip Area vs. Access Latency
Chart: Access Latency (ns)
| 23.10725021132788 | 24.617764350044741 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
Commodity DRAM
(512 rows/subarray)
32 rows/subarray
?
How to enable low latency without high area overhead?

## Slide 50: Our Proposal
Large Subarray
Small Subarray
Our Proposal
Low area cost

## Slide 51: Tiered-Latency DRAM
Near Segment
Far Segment
+ Lower access latency
+ Lower energy/access
- Higher access latency
- Higher energy/access
Map frequently accessed data to near segment

## Slide 52: Results Summary
Chart: 
 | 1
 | 1.12
Chart: 
 | 1
 | 0.73
12%
23%
Commodity DRAM
Tiered-Latency DRAM

## Slide 53: Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, Onur Mutlu
Published in the proceedings of 19th IEEE International Symposium on
High Performance Computer Architecture 2013

## Slide 54
DRAM Stores Data as Charge
1. Sensing
2. Restore
3. Precharge
DRAM cell
Sense amplifier
Three steps of charge movement

## Slide 55
Sensing
Restore
Timing Parameters
Data 0
Data 1
cell
time
charge
Sense amplifier
DRAM Charge over Time
Why does DRAM need the extra timing margin?
In theory
margin
cell
Sense amplifier
In practice

## Slide 56
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge;
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge

## Slide 57
Same size 
Same charge 
Different size 
Different charge 
Same latency
Different latency
Large variation in cell size 
Large variation in charge 
Large variation in access latency
DRAM Cells are Not Equal
Real
Ideal
Largest cell
Smallest cell

## Slide 58
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature

## Slide 59
Cells store small charge at high temperature
and large charge at low temperature
 Large variation in access latency
Charge Leakage Temperature
Room Temp.
Hot Temp. (85°C)
Small leakage
Large leakage

## Slide 60
DRAM Timing Parameters
DRAM timing parameters are dictated by the worst case
  The smallest cell with the smallest charge in all DRAM products
  Operating at the highest temperature
Large timing margin for the common case
Can lower latency for the common case

## Slide 61: DRAM Testing Infrastructure
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 62
Typical DIMM at
Low Temperature
Obs 1. Faster Sensing
More charge
Strong charge
flow
Faster sensing
Typical DIMM at Low Temperature
 More charge  Faster sensing
Timing
(tRCD)
17% ↓
No Errors
115 DIMM
characterization

## Slide 63
Obs 2. Reducing Restore Time
Larger cell &
Less leakage 
Extra charge
No need to fully
restore charge
Typical DIMM at lower temperature
 More charge  Restore time reduction
Read (tRAS)
37% ↓
Write (tWR)
54% ↓
No Errors
115 DIMM
characterization
Typical DIMM at
Low Temperature

## Slide 64
Empty (0V)
Full (Vdd)
Half
Obs 3. Reducing Precharge Time
Bitline
Sense amplifier
Sensing
Precharge
Precharge ?
– Setting bitline to half-full charge
Typical DIMM at
Low Temperature

## Slide 65
Empty (0V)
Full (Vdd)
Half
bitline
Not fully precharged
More charge
 strong sensing
Access empty cell
Access full cell
Timing
(tRP)
35% ↓
No Errors
115 DIMM
characterization
Typical DIMM at Lower Temperature
 More charge  Precharge time reduction
Obs 3. Reducing Precharge Time

## Slide 66: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer profiles multiple sets of
  reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature

## Slide 67
Chart: 
 | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
 | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
 | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
 | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
 | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
 | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
 | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
 | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
Real System Evaluation
AL-DRAM provides high performance improvement, greater for multi-core workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 68
Summary: AL-DRAM
Observation
  DRAM timing parameters are dictated by the worst-case cell (smallest cell at highest temperature)
Our Approach: Adaptive-Latency DRAM (AL-DRAM)
  Optimizes DRAM timing parameters for the common case (typical DIMM operating at low temperatures)
Analysis: Characterization of 115 DIMMs
  Great potential to lower DRAM timing parameters (17 – 54%) without any errors
Real System Performance Evaluation
  Significant performance improvement (14% for memory-intensive workloads) without errors (33 days)

## Slide 69: Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case
Donghyuk Lee, Yoongu Kim,
Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu
Published in the proceedings of 21st
International Symposium on High Performance Computer Architecture 2015

## Slide 70: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013;
  Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 71: Parallelism: Demand vs. Supply
Demand
Supply
Out-of-order Execution
Multi-cores
Prefetchers
Multiple
Banks

## Slide 72: Increasing Number of Banks?
How to improve available parallelism within DRAM?
Adding more banks → Replication of shared structures
Replication → Cost

## Slide 73: Our Observation
Time
1. Wordline enable
2. Charge sharing
3. Sense amplify
4. Charge restoration
5. Wordline disable
6. Restore sense-amps
Data Access
Local to a subarray

## Slide 74: Subarray-Level Parallelism
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Row Address
Row Address
Replicate
Time share

## Slide 75: Subarray-Level Parallelism: Benefits
Time
Data Access
Data Access
Data Access
Data Access
Saved Time
Commodity DRAM
Subarray-Level Parallelism
Two requests to different subarrays in same bank

## Slide 76: Results Summary
Chart: 
 | 1
 | 1.17
Chart: 
 | 1
 | 0.81
Commodity DRAM
Subarray-Level Parallelism
17%
19%

## Slide 77: A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, Onur Mutlu
Published in the proceedings of 39th
International Symposium on Computer Architecture 2012

## Slide 78: Review #5
RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization Vivek Seshadri et al., MICRO 2013

## Slide 79: Review #3 Results
Chart: Grades (out of 10) Mean: 8.6
 | 1 | 2 | 4 | 6 | 4

## Slide 80: CSC 2231: Parallel Computer Architecture and Programming Main Memory Fundamentals
Prof. Gennady Pekhimenko
University of Toronto
Fall 2017
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU