## Slide 1: CSC 2231: Parallel Computer Architecture and Programming GPUs
Prof. Gennady Pekhimenko
University of Toronto
Fall 2017
The content of this lecture is adapted from the slides of
Tor Aamodt (UBC)

## Slide 2: Project Progress Report
Due next week Friday (Nov. 3rd)
Ask questions after the class

## Slide 3: Review #7
GPUs and the Future of Parallel Computing Steve Keckler et al., IEEE Micro 2011
Due Nov. 10

## Slide 4: Review #5 Results
Chart: Grades (out of 10) Mean: 9.05
| 6s | 7s | 8s | 9s | 10s
 | 0 | 2 | 2 | 6 | 7

## Slide 5: What is a GPU?
GPU = Graphics Processing Unit
  Accelerator for raster based graphics (OpenGL, DirectX)
  Highly programmable (Turing complete)
  Commodity hardware
  100’s of ALUs; 10’s of 1000s of concurrent threads
NVIDIA Volta: V100

## Slide 6: The GPU is Ubiquitous
[APU13 keynote]
+

## Slide 7: “Early” GPU History
  1981: IBM PC Monochrome Display Adapter (2D)
  1996: 3D graphics (e.g., 3dfx Voodoo)
  1999: register combiner (NVIDIA GeForce 256)
  2001: programmable shaders (NVIDIA GeForce 3)
  2002: floating-point (ATI Radeon 9700)
  2005: unified shaders (ATI R520 in Xbox 360)
  2006: compute (NVIDIA GeForce 8800)
Notes:   GPGPU
    Origins
    Use in supercomputing
    CUDA => OpenCL => C++AMP, OpenACC, others
    Use in Smartphones (e.g., Imagination PowerVR)
    Cars (e.g., NVIDIA DRIVE PX)

## Slide 8: GPU: The Life of a Triangle
Texture
Host
/
Front End
/
Vertex Fetch
F
r
a
m
e
B
u
f
f
e
r
C
o
n
t
r
o
l
l
e
r
Vertex Processing
Primitive Assembly
,
Setup
Rasterize
&
Zcull
Pixel Shader
Pixel Engines
(
ROP
)
process commands
transform vertices
to screen
-
space
generate per
-
triangle equations
generate pixels
,
delete pixels
that cannot be seen
determine the colors
,
transparencies
and depth of the pixel
do final hidden surface test,
blend
and write out color and new depth
[David Kirk / Wen-mei Hwu]
+

## Slide 9
pixel color result of running “shader” program
+
Notes: Each pixel the result of a single thread run on the GPU

## Slide 10: Why use a GPU for computing?
GPU uses larger fraction of silicon for computation than CPU.
At peak performance GPU uses order of magnitude less energy per operation than CPU.
CPU
2nJ/op
GPU
200pJ/op
Rewrite Application
Order of Magnitude More Energy Efficient
However….
Application must perform well

## Slide 11: GPU uses larger fraction of silicon for computation than CPU?
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU
[NVIDIA]
+

## Slide 12: CSC 2231: Parallel Computer Architecture and Programming GPUs
Prof. Gennady Pekhimenko
University of Toronto
Fall 2017
The content of this lecture is adapted from the slides of
Tor Aamodt (UBC)