## Slide 1: CSC D70: Compiler Optimization Prefetching
Prof. Gennady Pekhimenko
University of Toronto
Winter 2019
The content of this lecture is adapted from the lectures of
Todd Mowry and Phillip Gibbons

## Slide 2: The Memory Latency Problem
 processor speed >>  memory speed
caches are not a panacea
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187

## Slide 3: Prefetching for Arrays: Overview
Tolerating Memory Latency
Prefetching Compiler Algorithm and Results
Implications of These Results

## Slide 4: Coping with Memory Latency
Reduce Latency:
  Locality Optimizations
    reorder iterations to improve cache reuse
Tolerate Latency:
  Prefetching
    move data close to the processor before it is needed

## Slide 5: Tolerating Latency Through Prefetching
overlap memory accesses with computation and other accesses
Without Prefetching
With Prefetching
Time
Load A
Load B
Fetch A
Fetch B
Load A
Load B
Prefetch A
Prefetch B
Fetch A
Fetch B
Executing Instructions
Stalled Waiting for Data

## Slide 6: Types of Prefetching
Cache Blocks:
(-) limited to unit-stride accesses
Nonblocking Loads:
(-) limited ability to move back before use
Hardware-Controlled Prefetching:
(-) limited to constant-strides and by branch prediction
(+) no instruction overhead
Software-Controlled Prefetching:
(-) software sophistication and overhead
(+) minimal hardware support and broader coverage

## Slide 7: Prefetching Goals
Domain of Applicability
Performance Improvement
  maximize benefit
  minimize overhead

## Slide 8: Prefetching Concepts
possible only if addresses can be determined ahead of time
coverage factor = fraction of misses that are prefetched
unnecessary if data is already in the cache
effective if data is in the cache when later referenced
Analysis: what to prefetch
  maximize coverage factor
  minimize unnecessary prefetches
Scheduling: when/how to schedule prefetches
  maximize effectiveness
  minimize overhead per prefetch

## Slide 9: Reducing Prefetching Overhead
instructions to issue prefetches
extra demands on memory system
important to minimize unnecessary prefetches
Hit Rates for Array Accesses

## Slide 10: Compiler Algorithm
Analysis: what to prefetch
Locality Analysis
Scheduling: when/how to issue prefetches
Loop Splitting
Software Pipelining

## Slide 11: Steps in Locality Analysis
1. Find data reuse
  if caches were infinitely large, we would be finished
2. Determine “localized iteration space”
  set of inner loops where the data accessed by an iteration is expected to fit within the cache
3. Find data locality:
  reuse  localized iteration space  locality

## Slide 12: Data Locality Example
for i = 0 to 2
for j = 0 to 100
A[i][j] = B[j][0] + B[j+1][0];
Hit
Miss
i
j
A[i][j]
Spatial
i
j
B[j+1][0]
Temporal
i
j
B[j][0]
Group

## Slide 13: Reuse Analysis: Representation
Map n loop indices into d array indices via array indexing function:
for i = 0 to 2
for j = 0 to 100
A[i][j] = B[j][0] + B[j+1][0];

## Slide 14: Finding Temporal Reuse
Temporal reuse occurs between iterations and whenever:
Rather than worrying about individual values of and, we say that reuse occurs along direction vector when:
Solution: compute the nullspace of H

## Slide 15: Temporal Reuse Example
Reuse between iterations (i1,j1) and (i2,j2) whenever:
True whenever j1 = j2, and regardless of the difference between i1 and i2.
  i.e. whenever the difference lies along the nullspace of ,
  which is span{(1,0)} (i.e. the outer loop).
for i = 0 to 2
for j = 0 to 100
A[i][j] = B[j][0] + B[j+1][0];

## Slide 16: Prefetch Predicate
Example:
Locality Type | Miss Instance | Predicate
None | Every Iteration | True
Temporal | First Iteration | i = 0
Spatial | Every l iterations (l = cache line size) | (i mod l) = 0
for i = 0 to 2
for j = 0 to 100
A[i][j] = B[j][0] + B[j+1][0];
Reference | Locality | Predicate
A[i][j] |  | (j mod 2) = 0
B[j+1][0] |  | i = 0
[
i
j
]
none
spatial
[
]
=
[
i
j
]
temporal
none
[
]
=

## Slide 17: Compiler Algorithm
Analysis: what to prefetch
Locality Analysis
Scheduling: when/how to issue prefetches
Loop Splitting
Software Pipelining

## Slide 18: Loop Splitting
Decompose loops to isolate cache miss instances
  cheaper than inserting IF statements
Apply transformations recursively for nested loops
Suppress transformations when loops become too large
  avoid code explosion
Locality Type | Predicate | Loop Transformation
None | True | None
Temporal | i = 0 | Peel loop i
Spatial | (i mod l) = 0 | Unroll loop i by l

## Slide 19: Software Pipelining
where l = memory latency, s = shortest path through loop body
Iterations Ahead =  
l
s
for (i = 0; i<100; i++)
a[i] = 0;
Original Loop
for (i = 0; i<5; i++) /* Prolog */
prefetch(&a[i]);
for (i = 0; i<95; i++) { /* Steady State*/
prefetch(&a[i+5]);
a[i] = 0;
}
for (i = 95; i<100; i++) /* Epilog */
a[i] = 0;
Software Pipelined Loop
(5 iterations ahead)

## Slide 20: Example Revisited
for (i = 0; i < 3; i++)
for (j = 0; j < 100; j++)
A[i][j] = B[j][0] + B[j+1][0];
Original Code
prefetch(&A[0][0]);
for (j = 0; j < 6; j += 2) {
prefetch(&B[j+1][0]);
prefetch(&B[j+2][0]);
prefetch(&A[0][j+1]);
}
for (j = 0; j < 94; j += 2) {
prefetch(&B[j+7][0]);
prefetch(&B[j+8][0]);
prefetch(&A[0][j+7]);
A[0][j] = B[j][0]+B[j+1][0];
A[0][j+1] = B[j+1][0]+B[j+2][0];
}
for (j = 94; j < 100; j += 2) {
A[0][j] = B[j][0]+B[j+1][0];
A[0][j+1] = B[j+1][0]+B[j+2][0];
}
for (i = 1; i < 3; i++) {
prefetch(&A[i][0]);
for (j = 0; j < 6; j += 2)
prefetch(&A[i][j+1]);
for (j = 0; j < 94; j += 2) {
prefetch(&A[i][j+7]);
A[i][j] = B[j][0] + B[j+1][0];
A[i][j+1] = B[j+1][0] + B[j+2][0];
}
for (j = 94; j < 100; j += 2) {
A[i][j] = B[j][0] + B[j+1][0];
A[i][j+1] = B[j+1][0] + B[j+2][0];
}
}
Code with Prefetching
i
j
A[i][j]
i
j
B[j+1][0]
Cache Hit
Cache Miss
i = 0
i > 0

## Slide 21: Prefetching Indirections
Analysis: what to prefetch
  both dense and indirect references
  difficult to predict whether indirections hit or miss
Scheduling: when/how to issue prefetches
  modification of software pipelining algorithm
for (i = 0; i<100; i++)
sum += A[index[i]];

## Slide 22: Software Pipelining for Indirections
for (i = 0; i<100; i++)
sum += A[index[i]];
Original Loop
for (i = 0; i<5; i++) /* Prolog 1 */
prefetch(&index[i]);
for (i = 0; i<5; i++) { /* Prolog 2 */
prefetch(&index[i+5]);
prefetch(&A[index[i]]);
}
for (i = 0; i<90; i++) { /* Steady State*/
prefetch(&index[i+10]);
prefetch(&A[index[i+5]]);
sum += A[index[i]];
}
for (i = 90; i<95; i++) { /* Epilog 1 */
prefetch(&A[index[i+5]]);
sum += A[index[i]];
}
for (i = 95; i<100; i++) /* Epilog 2 */
sum += A[index[i]];
Software Pipelined Loop
(5 iterations ahead)

## Slide 23: Summary of Results
Dense Matrix Code:
  eliminated 50% to 90% of memory stall time
  overheads remain low due to prefetching selectively
  significant improvements in overall performance (6 over 45%)
Indirections, Sparse Matrix Code:
  expanded coverage to handle some important cases

## Slide 24: Prefetching for Arrays: Concluding Remarks
Demonstrated that software prefetching is effective
  selective prefetching to eliminate overhead
  dense matrices and indirections / sparse matrices
  uniprocessors and multiprocessors
Hardware should focus on providing sufficient memory bandwidth

## Slide 25: Prefetching for Recursive Data Structures

## Slide 26: Recursive Data Structures
Examples:
  linked lists, trees, graphs, ...
A common method of building large data structures
  especially in non-numeric programs
Cache miss behavior is a concern because:
  large data set with respect to the cache size
  temporal locality may be poor
  little spatial locality among consecutively-accessed nodes
Goal:
Automatic Compiler-Based Prefetching for Recursive Data Structures

## Slide 27: Overview
Challenges in Prefetching Recursive Data Structures
Three Prefetching Algorithms
Experimental Results
Conclusions

## Slide 28: Scheduling Prefetches for Recursive Data Structures
Our Goal: fully hide latency
  thus achieving fastest possible computation rate of 1/W
e.g., if L = 3W, we must prefetch 3 nodes ahead to achieve this

## Slide 29: Performance without Prefetching
computation rate = 1 / (L+W)

## Slide 30: Prefetching One Node Ahead
Computation is overlapped with memory accesses
computation rate = 1/L

## Slide 31: Prefetching Three Nodes Ahead
computation rate does not improve (still = 1/L)!
Pointer-Chasing Problem:
any scheme which follows the pointer chain is limited to a rate of 1/L

## Slide 32: Our Goal: Fully Hide Latency
achieves the fastest possible computation rate of 1/W

## Slide 33: Overview
Challenges in Prefetching Recursive Data Structures
Three Prefetching Algorithms
  Greedy Prefetching
  History-Pointer Prefetching
  Data-Linearization Prefetching
Experimental Results
Conclusions

## Slide 34: Pointer-Chasing Problem
Key:
ni needs to know &ni+d without referencing the d-1 intermediate nodes
Our proposals:
use existing pointer(s) in ni to approximate &ni+d
  Greedy Prefetching
add new pointer(s) to ni to approximate &ni+d
  History-Pointer Prefetching
compute &ni+d directly from &ni (no ptr deref)
  History-Pointer Prefetching

## Slide 35: Greedy Prefetching
Prefetch all neighboring nodes (simplified definition)
  only one will be followed by the immediate control flow
  hopefully, we will visit other neighbors later
Reasonably effective in practice
However, little control over the prefetching distance
preorder(treeNode * t){
if (t != NULL){
pf(t->left);
pf(t->right);
process(t->data);
preorder(t->left);
preorder(t->right);
}
}

## Slide 36: History-Pointer Prefetching
Add new pointer(s) to each node
  history-pointers are obtained from some recent traversal
Trade space & time for better control over prefetching distances

## Slide 37: Data-Linearization Prefetching
No pointer dereferences are required
Map nodes close in the traversal to contiguous memory

## Slide 38: Summary of Prefetching Algorithms
 | Greedy | History-Pointer | Data-Linearization
Control over Prefetching Distance | little | more precise | more precise
Applicability to Recursive Data Structures | any RDS | revisited; changes only slowly | must have a major traversal order; changes only slowly
Overhead in Preparing Prefetch Addresses | none | space + time | none in practice
Ease of Implementation | relatively straightforward | more difficult | more difficulty

## Slide 39: Conclusions
Propose 3 schemes to overcome the pointer-chasing problem:
  Greedy Prefetching
  History-Pointer Prefetching
  Data-Linearization Prefetching
Automated greedy prefetching in SUIF
  improves performance significantly for half of Olden
  memory feedback can further reduce prefetch overhead
The other 2 schemes can outperform greedy in some situations