## Slide 1: Handout # 3: Programming Computer Networks
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
ganjali7@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali

## Slide 2: Announcements
List of papers for Week 4 are posted.
  10% bonus for Week 4 (Jan 27th) volunteers.
  Volunteers for Week 5?
    5% bonus
    Next week 0%
    The week after …. 
Each presentation is 20 minutes.
  Followed by 10 minutes of discussion and Q&A.
Please read the papers before each class.

## Slide 3: Final Project
Start choosing your team members
  Use Piazza if needed
Final Project Topic
  Consult with the instructor to choose a problem
    A high-level list of topics will be provided by the end of this week
    Choose 1-2 problems from the offered list
  Replicate & Improve
    Choose a paper related to the course topic, replicate existing solution, and improve (bonus)
  Survey of existing solutions
    Create new insights by looking at certain problems/solutions from different perspectives
  Apply your background/ideas
    Identify challenges and opportunities in the areas covered in the course to apply your own ideas.
Please discuss your ideas with me before submitting a proposal.

## Slide 4: Outline
Last week: Data-Center Networks
  Design
  Architecture
This week: Programming Computer Networks
  Software-Defined Networking
  Programmable Switches
Next week:
  DCN Transport
  DCN and ML

## Slide 5: Programming Data Center Networks
DCN Primary Objective:
  Transfer Packets
Also, provide high performance (bandwidth, latency, loss requirements)
  As well as new functions (e.g., network virtual functions or NFV, …),
Traditionally, forwarding, routing, load balancing, … implemented in a combination of hardware, software running on network devices
  Extremely difficult to change
  New functions take years

## Slide 6: Traditional Networks
Million of lines of source code
9,000 RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary
Networking industry with “mainframe” mind-set
Custom Hardware
OS
Routing, management, mobility management, access control, VPNs, …
Feature
Feature

## Slide 7: Reality is Even Worse
Operating System
App
App
App
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Operating
System
App
App
App
Lack of competition means glacial innovation
Closed architecture means blurry, closed interfaces

## Slide 8
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface

## Slide 9: What we need …

## Slide 10: 1) Separate Intelligence from Datapath
New function!
Operators, users, 3rd party developers, researchers, …

## Slide 11: 2) Cache Decisions
In minimal flow-based datapath
“If header = x, send to port 4”
Flow
Table
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”

## Slide 12: How Can We Do This?
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
OS
OS
OS
OS
OS
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 13: Software Defined Network (SDN)
Feature
Feature
Network OS
1. Open interface to packet forwarding
3. Consistent, up-to-date global network view
2. At least one Network OS probably many. Open- and closed-source
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 14: Consequences
More innovation in network services
  Owners, operators, 3rd party developers, researchers can improve the network
  E.g. energy management, data center management, policy routing, access control, denial of service, mobility
Lower barrier to entry for competition
  Healthier marketplace, new players
Lower cost
  Infrastructure
  Management

## Slide 15: Example: New Data Center
Cost
200,000 servers
Fanout of 20 a 10,000 switches
$5k commercial switch a $50M
$1k custom-built switch a $10M
Savings in 10 data centers = $400M
Control
Optimize for features needed
Customize for services & apps
Quickly improve and innovate
SDN can significantly reduce the CapEx and OpEx of data center networks.

## Slide 16: Example: Routing
OSPF
  RFC 2328: 245 pages
Distributed System
  Builds consistent, up-to-date map of the network: 101 pages
Dijkstra’s Algorithm
  Operates on map: 4 pages

## Slide 17: Example: Routing
OSPF = Dijkstra
IS-IS
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Distributed or Centralized System;
Centralized View
Custom Hardware
OS
OSPF
IS-IS
Distributed
System
Distributed
System

## Slide 18: Back to the story …

## Slide 19: Network OS
Network OS: distributed system that creates a consistent, up-to-date network view
  Runs on servers (controllers) in the network
  NOX, ONIX, HyperFlow, Kandoo, Floodlight, Trema, Beacon, Maestro, Beehive, OpenDayLight, … + moreentity_id: sensor.home_alert_level
Uses forwarding abstraction to:
  Get state information from forwarding elements
  Give control directives to forwarding elements

## Slide 20: Control Program
Control program operates on view of network
  Input: global network view (graph/database)
  Output: configuration of each network device
Control program is not necessarily a distributed system
  Ideally, the abstraction hides details of distributed state
  Lots of practical challenges though.

## Slide 21: Forwarding Abstraction
Purpose: Abstract away forwarding hardware
  Flexible
    Behavior specified by control plane
    Built from basic set of forwarding primitives
  Minimal
    Streamlined for speed and low-power
    Control program not vendor-specific
OpenFlow is an example of such an abstraction

## Slide 22: Forwarding Substrate
Flow-based
Small number of actions for each flow
  Plumbing: Forward to port(s)
  Control: Forward to controller
  Routing between flow-spaces: Rewrite header
  Bandwidth isolation: Min/max rate
External open API to flow-table

## Slide 23
What is a flow?
Application flow
All http
Jim’s traffic
All packets to Canada
…
Types of Action
Allow/deny flow
Route & re-route flow
Isolate flow
Make flow private
Remove flow
…

## Slide 24: Substrate: “Flowspace”
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace

## Slide 25: OpenFlow
  Started as open standard to run experimental protocols in production networks
    API between the forwarding elements and the network OS
  Based in Stanford, supported by various companies (Cisco, Juniper, HP, NEC, …)
  Used by universities to deploy innovative networking technology
Later, many similar (sometimes proprietary) interfaces used by various companies

## Slide 26: Traditional Switch
Ethernet Switch

## Slide 27: Traditional Switch
Data Path (Hardware)
Control Path
Control Path (Software)

## Slide 28: OpenFlow Switch
OpenFlow Protocol (SSL)
Data Path (Hardware)
Control Path
OpenFlow
Ethernet Switch
Network OS
Control Program A
Control Program B

## Slide 29: OpenFlow Rules
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Flow
Table(s)
“If header = p, send to port 4”
“If header = ?, send to me”
“If header = q, overwrite header with r, add header s, and send to ports 5,6”

## Slide 30: Plumbing Primitives
<Match, Action>
Match arbitrary bits in headers:
  Match on any header, or new header
  Allows any flow granularity
Action
  Forward to port(s), drop, send to controller
  Overwrite header with mask, push or pop
  Forward at specific bit-rate
Header
Data
Match: 1000x01xx0101001x

## Slide 31: OpenFlow Rules – Cont’d
Exploit the flow table in switches, routers, and chipsets
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Default Action
Statistics
Flow 1.
Flow 2.
Flow 3.
Flow N.
Notes: 31

## Slide 32: Flow Table Entry
OpenFlow Protocol Version 1.0
+ mask what fields to match
Packet + byte counters
Rule
Action
Statistics
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort

## Slide 33: Examples
Switching
*
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
Firewall
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
port 3
00:2…
00:1f:..
0800
vlan1
1.2.3.4
5.6.7.8
4
17265
80
port6
*
*
*
*
*
*
*
*
*
80
drop

## Slide 34: Examples
Routing
*
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
*
*
*
*
vlan1
*
*
*
*
*
port5, port6, port7
Virtual Local Area Network (VLAN): a logical grouping of devices that creates a separate broadcast domain within a physical network, allowing multiple virtual networks to coexist on the same infrastructure.

## Slide 35: What about Data Plane?

## Slide 36: Data Plane Functionalities
So far, we have focused on control plane
  It distinguishes SDN from traditional networks
  Source of many (perceived) challenges …
  … and opportunities
What about the data plane?
  Which features should be provided in the data plane?
What defines the boundary between control and data planes?

## Slide 37: OpenFlow and Data Plane
Historically, OpenFlow defined data plane’s role as forwarding.
  Other functions are left to middleboxes and edge nodes in this model.
Question. Why only forwarding?
  Other data path functionalities exist in today’s routers/switches too.
  What distinguishes forwarding from other functions?

## Slide 38: Adding New Functionalities
Consider a new functionality we want to implement in a software-defined network.
Where is the best place to add that function?
  Controller?
  Switches?
  Middleboxes?
  Endhosts?
?
?
?
?

## Slide 39: Adding New Functionalities
What metrics/criteria do we have to decide where new functionalities should be implemented?
Example: Elephant flow detection
  Data plane: change forwarding elements (e.g., DevoFlow)
  Control plane: push functionality close to the path (e.g., Kandoo)
What does the development process look like?
  Changing ASIC expensive and time-consuming
  Changing software fast

## Slide 40: Alternative View
Decouple based on development cycle
  Fast: mostly software
  Slow: mostly hardware
Development process
  Start in software
  As function matures, move towards hardware
Not a new idea
  Model has been used for a long-time in industry.

## Slide 41: Changing the Control Plane
I can tailor my network to meet my needs ...
Quickly deploy new protocols.
Monitor precisely what my forwarding plane is doing.
Fold expensive middlebox functions into the network, for free.
Try out beautiful new ideas. Tailor my network to meet my needs.
Differentiate. Now I own my intellectual property.
Notes: With software-defined network controllers, it seems like we should be able to do all of these, but that’s not true!
There is a caveat here!

## Slide 42: But wait a minute…

## Slide 43
New
Switch OS
Driver
OSPF
BGP
etc.
Notes: Traditionally:
The chip doing the switching is built out of a fixed pipeline that processes different parts of the header.
Fixed function to keep it low cost and efficient
Example:
VXLAN was introduced in 2010.
- To separate tenants
2 pages description of the protocol
The software part can be implemented in a few days.
It took Cisco and VMWare 4.5 years to add the new entry in the pipeline
Not a complex application: the most profitable, and simple application took 4.5 years to

## Slide 44
Network Equipment Vendor
Network Owner
ASIC
Team
Software
Team
Feature
Weeks
Years
Years
Feature
Feature

## Slide 45: When you need a new feature…
Equipment vendor can’t just send you a software upgrade
New forwarding features take years to develop
By then, you’ve figured out a kludge to work around it
Your network gets more complicated, more brittle
Eventually, when the upgrade is available, it either
  No longer solves your problem, or
  You need a fork-lift upgrade, at huge expense.

## Slide 46: Network Systems Are Built “Bottom-up”
Switch OS
Fixed-function switch
Driver
“This is how I process packets …”

## Slide 47: “Top-Down” Network Programming
Programmable Switch
Driver
Switch OS
“This is precisely how you must process packets”

## Slide 48: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
Networking
?
Language
Compiler
>>>

## Slide 49: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
PISA
Networking
P4
Compiler
>>>

## Slide 50
Match+Action Stage
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
PISA: Protocol Independent Switch Architecture

## Slide 51
PISA: Protocol Independent Switch Architecture

## Slide 52: Example P4 Program
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
header_type ethernet_t { … }
header_type l2_metadata_t { … }
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[2];
metadata l2_metadata_t l2_meta;
Header and Data Declarations
Parser Program
parser parse_ethernet { extract(ethernet); return switch(ethernet.ethertype) { 0x8100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x8847 : parse_mpls; default: ingress; }
Tables and Control Flow
table port_table { … }
control ingress { apply(port_table); if (l2_meta.vlan_tags == 0) { process_assign_vlan();
} }

## Slide 53: Example: Barefoot Tofino 6.5Tb/s Switch
Forwarding defined in software (P4).
Programs always run at line-rate.
Same power.
Same cost.

## Slide 54: Network Programmability: Consequences
Reducing Complexity
1
Notes: Removed unneeded functionality

## Slide 55: Reducing Complexity
Compiler
Programmable Switch
Driver
Switch OS
switch.p4
IPv4 and IPv6 routing
- Unicast Routing
- Routed Ports & SVI
- VRF
- Unicast RPF - Strict and Loose
- Multicast
- PIM-SM/DM & PIM-Bidir
Ethernet switching
- VLAN Flooding
- MAC Learning & Aging
- STP state
- VLAN Translation
Load balancing
- LAG
- ECMP & WCMP
- Resilient Hashing
- Flowlet Switching
Fast Failover
– LAG & ECMP
Tunneling
- IPv4 and IPv6 Routing & Switching
- IP-in-IP (6in4, 4in4)
- VXLAN, NVGRE, GENEVE & GRE
- Segment Routing, ILA
MPLS
- LER and LSR
- IPv4/v6 routing (L3VPN)
- L2 switching (EoMPLS, VPLS)
- MPLS over UDP/GRE
ACL
- MAC ACL, IPv4/v6 ACL, RACL
- QoS ACL, System ACL, PBR
- Port Range lookups in ACLs
QOS
- QoS Classification & marking
- Drop profiles/WRED
- RoCE v2 & FCoE
- CoPP (Control plane policing)
NAT and L4 Load Balancing
Security Features
- Storm Control, IP Source Guard
Monitoring & Telemetry
Ingress Mirroring and Egress Mirroring
Negative Mirroring
Sflow
INT
Counters
Route Table Entry Counters
VLAN/Bridge Domain Counters
Port/Interface Counters
Protocol Offload
- BFD, OAM
Multi-chip Fabric Support
- Forwarding, QOS
Notes: A group of people implemented all these in p4.
Many people will comment most of these out. Then compile, and no need to worry about them.

## Slide 56: Reducing Complexity
Compiler
Driver
Switch OS
My switch.p4
Programmable Switch

## Slide 57: Network Programmability: Consequences
Adding New Features
2

## Slide 58: Protocol Complexity 30 Years Ago
Ethernet
IPv4
IPX
ethtype
ethtype

## Slide 59: Programmable DCN Switch
Switch.p4

## Slide 60: Adding Features: Some Examples
New encapsulations and tunnels
New ways to tag packets for special treatment
New approaches to routing: e.g. source routing in MSDCs
New approaches to congestion control
New ways to process packets: e.g. processing ticker-symbols

## Slide 61: New applications: Some Examples
Layer-4 Load Balancer
  Replace 100 servers or 10 dedicated boxes with one programmable switch
  Track and maintain mapping for 5-10 million http flows
Fast stateless firewall
  Add/delete and track 100s of thousands of new connections per second
Cache for Key-value store
  Memcache in-network cache for 100 servers
  1-2 billion operations per second

## Slide 62: Network Programmability: Consequences
Network Telemetry
3

## Slide 63
“Which path did my packet take?”
1
“I visited Switch 1 @780ns, Switch 9 @1.3µs, Switch 12 @2.4µs”
“Which rules did my packet follow?”
2
“In Switch 1, I followed rules 75 and 250. In Switch 9, I followed rules 3 and 80. ”
# | Rule
1 | 
2 | 
3 | 
… | 
75 | 192.168.0/24
… | 

## Slide 64
“How long did my packet queue at each switch?”
3
“Delay: 100ns, 200ns, 19740ns”
Time
Queue
“Who did my packet share the queue with?”
4

## Slide 65
“How long did my packet queue at each switch?”
3
“Delay: 100ns, 200ns, 19740ns”
Time
Queue
“Who did my packet share the queue with?”
4
Aggressor flow!

## Slide 66: We’d like the network to answer these questions
“Which path did my packet take?”
“Which rules did my packet follow?”
“How long did it queue at each switch?”
“Who did it share the queues with?”
A PISA device programmed using P4 can answer all four questions at line rate, for the first time. Without generating additional packets.

## Slide 67: INT: Inband Network Telemetry
Log, Analyze
Replay
Add: SwitchID, Arrival Time, Queue Delay, Matched Rules, …
Original Packet
Visualize

## Slide 68
Log, Analyze
Replay
Visualize
/* INT: add switch id */
action int_set_header_0() {
add_header(int_switch_id_header);
modify_field(int_switch_id_header.switch_id,
global_config_metadata.switch_id);
}
/* INT: add ingress timestamp */
action int_set_header_1() {
add_header(int_ingress_tstamp_header);
modify_field(int_ingress_tstamp_header.ingress_tstamp, i2e_metadata.ingress_tstamp);
}
/* INT: add egress timestamp */
action int_set_header_2() {
add_header(int_egress_tstamp_header);
modify_field(int_egress_tstamp_header.egress_tstamp,
eg_intr_md_from_parser_aux.egress_global_tstamp);
}
P4 code snippet: Insert switch ID, ingress and egress timestamp

## Slide 69: Network Programmability: Consequences
3
2
Reducing Complexity
Adding New Features
Network Telemetry
1

## Slide 70: Final Comments
Network programmability:
  Significantly powerful, makes change feasible
  Innovation in “control plane” and “data path”
Academia vs. industry
  Programmability allows development and testing of new ideas.
  Has had a major impact in academic research
    Creating proof-of-concept solutions in days/weeks
  Opens doors for innovation and high impact research
  Programmable switches in production: limited use cases
    Programmable core vs. edge: which one do you think is more useful?