## Slide 1: Handout # 26: Software-Defined Networking
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
ganjali7@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali

## Slide 2: Announcements
Problem Set 2
  Submit electronically as ps2.pdf.
  Due: today
Programming Assignment 2: Simple Router
  Due: Friday November 28 at 5pm.
This week’s tutorial:
  Problem Set 2 Review and Q&A

## Slide 3: The Story So Far
Layering
  Link layer
    Media, framing, error detection/correction, switches, hubs, …
  Network layer
    Addressing (CIDR, subnet), routing and forwarding, DNS, BGP, …
  Transport layer
    TCP, UDP, flow control, congestion control, queue management, …
Misc: Queueing Mechanisms, Middleboxes
Today: Software-Defined Networking (SDN)

## Slide 4: Innovation – Computers vs. Networks
How difficult is it to create/modify a computer application?
How difficult is it to create/modify a network feature?
What is the difference?
What are the tools available for each?

## Slide 5: Innovation in Applications
Computer
Application
Computer
Application
Application
OS
OS abstracts hardware substrate
 Innovation in applications

## Slide 6: Innovation in OS and Applications
x86
(Computer)
Windows
(OS)
Application
Application
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
or
or
Application
Application
Simple, common, stable, hardware substrate below
+ Programmability
+ Competition
 Innovation in OS and applications

## Slide 7: Innovation in Infrastructure
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
or
or
Application
Application
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization
App
Simple, common, stable, hardware substrate below
+ Programmability + Strong isolation model
+ Competition above
 Innovation in infrastructure

## Slide 8
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Notes: The mainframe industry in the 1980s was vertical and closed: it consisted of specialized hardware, operating system and applications --- all from the same company.
A revolution happened when open interfaces started to appear. The industry became horizontal. Innovation exploded.

## Slide 9: We Have Lost Our Way
Million of lines of source code
9,000 RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary
Networking industry with “mainframe” mind-set
Custom Hardware
OS
Routing, management, mobility management, access control, VPNs, …
Feature
Feature

## Slide 10: Reality is Even Worse
Operating System
App
App
App
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Operating
System
App
App
App
Lack of competition means glacial innovation
Closed architecture means blurry, closed interfaces

## Slide 11
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface

## Slide 12: What we need …

## Slide 13: 1) Separate Intelligence from Datapath
New function!
Operators, users, 3rd party developers, researchers, …

## Slide 14: 2) Cache Decisions
In minimal flow-based datapath
“If header = x, send to port 4”
Flow
Table
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”

## Slide 15: How Can We Do This?
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
OS
OS
OS
OS
OS
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 16: Software Defined Network (SDN)
Feature
Feature
Network OS
1. Open interface to packet forwarding
3. Consistent, up-to-date global network view
2. At least one Network OS probably many. Open- and closed-source
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 17: Consequences
More innovation in network services
  Owners, operators, 3rd party developers, researchers can improve the network
  E.g. energy management, data center management, policy routing, access control, denial of service, mobility
Lower barrier to entry for competition
  Healthier marketplace, new players
Lower cost
  Infrastructure
  Management

## Slide 18: Example: Routing
OSPF
  RFC 2328: 245 pages
Distributed System
  Builds consistent, up-to-date map of the network: 101 pages
Dijkstra’s Algorithm
  Operates on map: 4 pages

## Slide 19: Example: Routing
OSPF = Dijkstra
IS-IS
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Distributed or Centralized System;
Centralized View
Custom Hardware
OS
OSPF
IS-IS
Distributed
System
Distributed
System

## Slide 20: Back to the story …

## Slide 21: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 22: Network OS
Network OS: distributed system that creates a consistent, up-to-date network view
  Runs on servers (controllers) in the network
  NOX, ONIX, HyperFlow, Kandoo, Floodlight, Trema, Beacon, Maestro, Beehive, OpenDayLight, … + more
Uses forwarding abstraction to:
  Get state information from forwarding elements
  Give control directives to forwarding elements

## Slide 23: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 24: Control Program
Control program operates on view of network
  Input: global network view (graph/database)
  Output: configuration of each network device
Control program is not necessarily a distributed system
  Ideally, the abstraction hides details of distributed state
  Lots of practical challenges though.

## Slide 25: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 26: Forwarding Abstraction
Purpose: Abstract away forwarding hardware
  Flexible
    Behavior specified by control plane
    Built from basic set of forwarding primitives
  Minimal
    Streamlined for speed and low-power
    Control program not vendor-specific
OpenFlow is an example of such an abstraction

## Slide 27: Forwarding Substrate
Flow-based
Small number of actions for each flow
  Plumbing: Forward to port(s)
  Control: Forward to controller
  Routing between flow-spaces: Rewrite header
  Bandwidth isolation: Min/max rate
External open API to flow-table

## Slide 28
What is a flow?
Application flow
All http
Jim’s traffic
All packets to Canada
…
Types of Action
Allow/deny flow
Route & re-route flow
Isolate flow
Make flow private
Remove flow
…

## Slide 29: Substrate: “Flowspace”
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace

## Slide 30: OpenFlow
  Started as open standard to run experimental protocols in production networks
    API between the forwarding elements and the network OS
  Based in Stanford, supported by various companies (Cisco, Juniper, HP, NEC, …)
  Used by universities to deploy innovative networking technology
Later, many similar (sometimes proprietary) interfaces used by various companies

## Slide 31: Traditional Switch
Ethernet Switch

## Slide 32: Traditional Switch
Data Path (Hardware)
Control Path
Control Path (Software)

## Slide 33: OpenFlow Switch
OpenFlow Protocol (SSL)
Data Path (Hardware)
Control Path
OpenFlow
Ethernet Switch
Network OS
Control Program A
Control Program B

## Slide 34: OpenFlow Rules
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Flow
Table(s)
“If header = p, send to port 4”
“If header = ?, send to me”
“If header = q, overwrite header with r, add header s, and send to ports 5,6”

## Slide 35: Plumbing Primitives
<Match, Action>
Match arbitrary bits in headers:
  Match on any header, or new header
  Allows any flow granularity
Action
  Forward to port(s), drop, send to controller
  Overwrite header with mask, push or pop
  Forward at specific bit-rate
Header
Data
Match: 1000x01xx0101001x

## Slide 36: OpenFlow Rules – Cont’d
Exploit the flow table in switches, routers, and chipsets
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Default Action
Statistics
Flow 1.
Flow 2.
Flow 3.
Flow N.
Notes: 36

## Slide 37: Flow Table Entry
OpenFlow Protocol Version 1.0
+ mask what fields to match
Packet + byte counters
Rule
Action
Statistics
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort

## Slide 38: Examples
Switching
*
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
Firewall
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
port 3
00:2…
00:1f:..
0800
vlan1
1.2.3.4
5.6.7.8
4
17265
80
port6
*
*
*
*
*
*
*
*
*
80
drop

## Slide 39: Examples
Routing
*
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
Switch
Port
MAC
Src
Mac Dst
Eth Type
VLAN ID
IP Src
IP Dst
IP Prot
TCP sPort
TCP dPort
Action
*
*
*
*
vlan1
*
*
*
*
*
port5, port6, port7
Virtual Local Area Network (VLAN): a logical grouping of devices that creates a separate broadcast domain within a physical network, allowing multiple virtual networks to coexist on the same infrastructure.

## Slide 40: OpenFlow Hardware
Cisco Catalyst 6k
NEC IP8800
HP Procurve 5400
Juniper MX-series
WiMax (NEC)
PC Engines
Quanta LB4G
More ...

## Slide 41: OpenFlow Usage Example
OpenFlowSwitch.org
Controller
OpenFlow
Switch
PC
Dedicated OpenFlow Network
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Protocol
Peter’s code
Rule
Action
Statistics
Rule
Action
Statistics
Rule
Action
Statistics
Peter
Notes: 41

## Slide 42: Usage examples
Peter’s code:
  Static “VLANs”
  His own new routing protocol: unicast, multicast, multipath, load-balancing
  Network access control
  Home network manager
  Mobility manager
  Energy manager
  Packet processor (in controller)
  IPvPeter
  Network measurement and visualization
  …
Notes: 42

## Slide 43: Research/Production VLANS
Normal L2/L3 Processing
Flow Table
Production VLANs
Research VLANs
Controller

## Slide 44: Virtualize OpenFlow Switch
Normal L2/L3 Processing
Flow Table
Flow Table
Flow Table
Researcher A VLANs
Researcher B VLANs
Researcher C VLANs
Production VLANs
Controller A
Controller B
Controller C

## Slide 45: Virtualizing OpenFlow
OpenFlow
Switch
OpenFlow
Protocol
C’s
Controller
B’s
Controller
A’s
Controller
OpenFlow
Protocol
OpenFlow
Switch
OpenFlow
Switch
OpenFlow FlowVisor & Policy Control

## Slide 46: Virtualizing OpenFlow
OpenFlow
Protocol
Broadcast
Multicast
OpenFlow
Protocol
http
Load-balancer
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
OpenFlow FlowVisor & Policy Control

## Slide 47: Food for Thought
What are the challenges in switching from traditional networks to software-defiend networks?
What are the opportunities?