## Slide 1: Handout # 32: Overlay Networks
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
ganjali7@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali

## Slide 2: Announcements
Midterm solutions posted.
Programming Assignment 2: Buffer Sizing
  Due Friday November 28th at 5pm.
This week’s tutorial:
  Sample final exam review
  Sample final and solutions posted on class website
Course evaluations
  You have received an email about this.
  Please take a few minutes to provide feedback about the course.
Final Exam
  Please check time/location

## Slide 3: Today
Routing overlays
  Experimental versions of IP (e.g., 6Bone)
  Multicast (e.g., MBone and end-system multicast)
  Robust routing (e.g., Resilient Overlay Networks)
Types of peer-to-peer networks
  Directory-based (e.g., original Napster design)
  Unstructured (e.g., Gnutella, Kazaa, BitTorrent)
  Structured (e.g., distributed hash tables)

## Slide 4: Overlay Networks

## Slide 5: Overlay Networks
Focus at the application level

## Slide 6: Overlay Networks
A logical network built on top of a physical network
  Overlay links are tunnels through the underlying network
Many logical networks may coexist at once
  Over the same underlying network
  And providing its own particular service
Nodes are often end hosts
  Acting as intermediate nodes that forward traffic
  Providing a service, such as access to files
Who controls the nodes providing service?
  The party providing the service (e.g., Akamai)
  Distributed collection of end users (e.g., peer-to-peer)

## Slide 7: Routing Overlays
Alternative routing strategies
  No application-level processing at the overlay nodes
  Packet-delivery service with new routing strategies
Incremental enhancements to IP
  IPv6
  Multicast
  Mobility
  Security
Revisiting where a function belongs
  End-system multicast: multicast distribution by end hosts
Customized path selection
  Resilient Overlay Networks: robust packet delivery

## Slide 8: IP Tunneling
IP tunnel is a virtual point-to-point link
  Illusion of a direct link between two separated nodes
Encapsulation of the packet inside an IP datagram
  Node B sends a packet to node E
  … containing another packet as the payload
A
B
E
F
tunnel
Logical view:
Physical view:
A
B
E
F

## Slide 9: 6Bone: Deploying IPv6 over IP4
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
C
D
IPv4
IPv4
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
A-to-B:
IPv6
E-to-F:
IPv6
B-to-C:
IPv6 inside
IPv4
D-to-E:
IPv6 inside
IPv4

## Slide 10: Tunneling in Other Layers
IP Tunneling: encapsulate IP packets inside another IP packet.
We can do the same in other layers: transport, application, …
Example:
  TCP Tunneling: encapsulate IP packets inside a new TCP packet
  Need to establish a connection between two ends of the tunnel
Question: what would be the benefit of TCP tunneling?

## Slide 11: Secure Communication Over Insecure Links
Encrypt packets at entry and decrypt at exit
  Application layer tunnels
Eavesdropper cannot snoop the data
  … or determine the real source and destination

## Slide 12: Tor Project
An overlay to enhance anonymity and privacy
  Volunteer operated servers (?)
How Tor Works
  Obtain a list of Tor nodes from a directory
  Pick a random path to destination server
  Select a different path for other servers
encrypted
unencrypted

## Slide 13: Communicating With Mobile Users
A mobile user changes locations frequently
  So, the IP address of the machine changes often
The user wants applications to continue running
  So, the change in IP address needs to be hidden
Solution: fixed gateway forwards packets
  Gateway has a fixed IP address
  … and keeps track of the mobile’s address changes
  Mobile IP address can change
    DHCP assigns new IP address when you move
  Gateway can change accordingly
gateway
www.cnn.com

## Slide 14: MBone: IP Multicast
Multicast
  Delivering the same data to many receivers
  Avoiding sending the same data many times
IP multicast
  Special addressing, forwarding, and routing schemes
  Not widely deployed, so MBone tunneled between nodes
unicast
multicast

## Slide 15: End-System Multicast
IP multicast still is not widely deployed
  Technical and business challenges
  Should multicast be a network-layer service?
Multicast tree of end hosts
  Allow end hosts to form their own multicast tree
  Hosts receiving the data help forward to others

## Slide 16: RON: Resilient Overlay Networks
Premise: by building application overlay network, can increase performance and reliability of routing
Two-hop (application-level)
Berkeley-to-Princeton route
application-layer
router
Princeton
Yale
Berkeley

## Slide 17: RON Can Outperform IP Routing
IP routing does not adapt to congestion
  But RON can reroute when the direct path is congested
IP routing is sometimes slow to converge
  But RON can quickly direct traffic through intermediary
IP routing depends on AS routing policies
  But RON may pick paths that circumvent policies
Then again, RON has its own overheads
  Packets go in and out at intermediate nodes
    Performance degradation, load on hosts, and financial cost
  Probing overhead to monitor the virtual links
    Limits RON to deployments with a small number of nodes

## Slide 18: Today
Routing overlays
  Experimental versions of IP (e.g., 6Bone)
  Multicast (e.g., MBone and end-system multicast)
  Robust routing (e.g., Resilient Overlay Networks)
Types of peer-to-peer networks
  Directory-based (e.g., original Napster design)
  Unstructured (e.g., Gnutella, Kazaa, BitTorrent)
  Structured (e.g., distributed hash tables)

## Slide 19: Peer-to-Peer Networks: Napster
Napster history: the rise
  January 1999: Napster version 1.0
  May 1999: company founded
  September 1999: first lawsuits
  2000: 80 million users
Napster history: the fall
  Mid 2001: out of business due to lawsuits
  Mid 2001: dozens of P2P alternatives that were harder to touch, though these have gradually been constrained
  2003: growth of pay services like iTunes
Napster history: the resurrection
  2003: Napster reconstituted as a pay service
  2011: Acquired by Rhapsody from Best Buy
Shawn Fanning,
Northeastern freshman

## Slide 20: Napster Technology: Directory Service
User installing the software
  Download the client program
  Register name, password, local directory, etc.
Client contacts Napster (via TCP)
  Provides a list of music files it will share
  … and Napster’s central server updates the directory
Client searches on a title or performer
  Napster identifies online clients with the file
  … and provides IP addresses
Client requests the file from the chosen supplier
  Supplier transmits the file to the client
  Both client and supplier report status to Napster

## Slide 21: Napster Technology: Properties
Server’s directory continually updated
  Always know what music is currently available
  Point of vulnerability for legal action
Peer-to-peer file transfer
  No load on the server
  Plausible deniability for legal action (but not enough)
Proprietary protocol
  Login, search, upload, download, and status operations
  No security: clear-text passwords and other vulnerabilities
Bandwidth issues
  Suppliers ranked by apparent bandwidth & response time

## Slide 22: Napster: Limitations of Central Directory
Single point of failure
Performance bottleneck
Copyright infringement
So, later P2P systems were more distributed
File transfer is decentralized, but locating content is highly centralized

## Slide 23: Peer-to-Peer Networks: Gnutella
Gnutella history
  2000: J. Frankel & T. Pepper released Gnutella
  Soon after: many other clients (e.g., Morpheus, Limewire, Bearshare)
  2001: protocol enhancements, e.g., “ultrapeers”
Query flooding
  Join: contact a few nodes to become neighbors
  Publish: no need!
  Search: ask neighbors, who ask their neighbors
  Fetch: get file directly from another node

## Slide 24: Gnutella: Query Flooding
Fully distributed
  No central server
Public domain protocol
Many Gnutella clients implementing protocol
Overlay network: graph
Edge between peer X and Y if there’s a TCP connection
All active peers and edges is overlay net
Given peer will typically be connected with < 10 overlay neighbors

## Slide 25: Gnutella: Protocol
Query message sent over existing TCP connections
Peers forward Query message
QueryHit sent over reverse path
Query
Query
Query
Query
Query
QueryHit
QueryHit
Query Hit
File transfer:
HTTP
Scalability:
limited scope flooding

## Slide 26: Gnutella: Peer Joining
Joining peer X must find some other peer in Gnutella network: use list of candidate peers
X sequentially attempts to make TCP with peers on list until connection setup with Y
X sends Ping message to Y; Y forwards Ping message.
All peers receiving Ping message respond with Pong message
X receives many Pong messages. It can then setup additional TCP connections

## Slide 27: Gnutella: Pros and Cons
Advantages
  Fully decentralized
  Search cost distributed
  Processing per node permits powerful search semantics
Disadvantages
  Search scope may be quite large
  Search time may be quite long
  High overhead and nodes come and go often

## Slide 28: Peer-to-Peer Networks: KaAzA
KaZaA history
  2001: created by Dutch company (Kazaa BV)
  Single network called FastTrack used by other clients as well
  Eventually the protocol changed so other clients could no longer talk to it
Smart query flooding
  Join: on start, the client contacts a super-node (and may later become one)
  Publish: client sends list of files to its super-node
  Search: send query to super-node, and the super-nodes flood queries among themselves
  Fetch: get file directly from peer(s); can fetch from multiple peers at once

## Slide 29: KaZaA: Exploiting Heterogeneity
Each peer is either a group leader or assigned to a group leader
  TCP connection between peer and its group leader
  TCP connections between some pairs of group leaders
Group leader tracks the content in all its children

## Slide 30: KaZaA: Motivation for Super-Nodes
Query consolidation
  Many connected nodes may have only a few files
  Propagating query to a sub-node may take more time than for the super-node to answer itself
Stability
  Super-node selection favors nodes with high up-time
  How long you’ve been on is a good predictor of how long you’ll be around in the future

## Slide 31: Peer-to-Peer Networks: BitTorrent
BitTorrent history and motivation
  2002: B. Cohen debuted BitTorrent
  Key motivation: popular content
    Popularity exhibits temporal locality (Flash Crowds)
    E.g., Slashdot effect, CNN Web site on 9/11, release of a new movie or game
  Focused on efficient fetching, not searching
    Distribute same file to many peers
    Single publisher, many downloaders
  Preventing free-loading

## Slide 32: BitTorrent: Simultaneous Downloading
Divide large file into many pieces
  Replicate different pieces on different peers
  A peer with a complete piece can trade with other peers
  Peer can (hopefully) assemble the entire file
Allows simultaneous downloading
  Retrieving different parts of the file from different peers at the same time

## Slide 33: BitTorrent Components
Seed
  Peer with entire file
  Fragmented in pieces
Leacher
  Peer with an incomplete copy of the file
Torrent file
  Passive component
  Stores summaries of the pieces to allow peers to verify their integrity
Tracker
  Allows peers to find each other
  Returns a list of random peers

## Slide 34: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Web Server
.torrent

## Slide 35: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Web Server

## Slide 36: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Response-peer list
Web Server

## Slide 37: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Shake-hand
Web Server
Shake-hand

## Slide 38: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
Web Server

## Slide 39: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
pieces
Web Server

## Slide 40: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Response-peer list
pieces
pieces
pieces
Web Server

## Slide 41: Free-Riding Problem in P2P Networks
Vast majority of users are free-riders
  Most share no files and answer no queries
  Others limit # of connections or upload speed
A few “peers” essentially act as servers
  A few individuals contributing to the public good
  Making them hubs that basically act as a server
BitTorrent prevent free riding
  Allow the fastest peers to download from you
  Occasionally let some free loaders download

## Slide 42: Conclusions
Overlay networks
  Tunnels between host computers
  Hosts implement new protocols and services
  Effective way to build networks on top of the Internet
Peer-to-peer networks
  Nodes are end hosts
  Primarily for file sharing, and recently telephony
  Centralized directory (Napster), query flooding (Gnutella), super-nodes (KaZaA), and distributed downloading and anti-free-loading (BitTorrent)
Great example of how change can happen so quickly in application-level protocols

## Slide 43: Extra Slides

## Slide 44: A Case Study: Skype
A peer-to-peer VoIP client
Developed by Kazaa (2003)
Works seamlessly across NATs and firewalls
Great voice quality
Encrypts calls end-to-end
Acquired by Microsoft (2011)
  Significant changes
RIP: 2025
We cover historical lessons here
S.A. Baset and H.G. Schulzrinne, “An Analysis of the Skype Peer-to-Peer Internet Telephony Protocol,” INFOCOM 2006. 25th IEEE International Conference on Computer Communications. Proceedings, 2006, pp. 1-11.

## Slide 45: Types of Nodes
Ordinary hosts
Super nodes (SN)
Login server

## Slide 46: Host Cache
A list of super node IP address and port pairs that Skype client builds and refresh regularly.
At least one valid entry must be present in the HC.
Client stores HC locally.
After running a client for two days, HC contains a many as 200 entries.
The SN is selected by the Skype protocol based on a number of factors like CPU and available bandwidth.

## Slide 47: Encryption
Skype uses encryption to protect sensitive information.
Uses 256-bit encryption, which has a total of 1.1X1077 possible keys.
Uses 1536 to 2048 bit RSA to negotiate symmetric AES keys.
User public keys are certified by login server at login.

## Slide 48: Detecting Skype
Some ISPs are interested in detecting Skype
  Enforced by governments
  To degrade performance
  …
Detecting Skype traffic is not easy
  Peer-to-peer makes the network dynamic in nature
  Super-nodes are not easy to detect
  Packets are encrypted: deep packet inspection does not work

## Slide 49: Detecting Skype Traffic
Key invariants:
  Many packets with small inter-arrival times
  Small sized packets
  Random content
Test for all of these and mark as Skype.
For more details see the following paper.
D. Bonfiglio, M. Mellia, M. Meo, D. Rossi, and P. Tofanelli, “Revealing skype traffic: when randomness plays with you,” Proceedings ACM Sigcomm 2007, Kyoto, Japanpp. 37-48.