## Slide 1: Software-Define Networking
Soheil Abbasloo
Department of Computer Science
University of Toronto
Fall 2022

## Slide 2: Outline
Innovation: Computers vs. Networks
SDN
OpenFlow

## Slide 3: Innovation Computers vs. Networks
How difficult is it to create/modify a computer application?
How difficult is it to create/modify a network feature?
What is the difference?
What are the tools available for each?

## Slide 4: Innovation in Applications
Computer
Application
Computer
Application
Application
OS
OS abstracts hardware substrate
 Innovation in applications

## Slide 5: Innovation in OS and Applications
x86
(Computer)
Windows
(OS)
Application
Application
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
or
or
Application
Application
Simple, common, stable, hardware substrate below
+ Programmability
+ Competition
 Innovation in OS and applications

## Slide 6: Innovation in Infrastructure
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
or
or
Application
Application
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization
App
Simple, common, stable, hardware substrate below
+ Programmability + Strong isolation model
+ Competition above
 Innovation in infrastructure

## Slide 7
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Notes: The mainframe industry in the 1980s was vertical and closed: it consisted of specialized hardware, operating system and applications --- all from the same company.
A revolution happened when open interfaces started to appear. The industry became horizontal. Innovation exploded.

## Slide 8: We Have Lost Our Way
Million of lines of source code
6,000 RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary
Networking industry with “mainframe” mind-set
Custom Hardware
OS
Routing, management, mobility management, access control, VPNs, …
Feature
Feature

## Slide 9: Reality is Even Worse
Operating System
App
App
App
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Operating
System
App
App
App
Lack of competition means glacial innovation
Closed architecture means blurry, closed interfaces

## Slide 10
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface

## Slide 11: What we need …

## Slide 12: 1) Separate Intelligence from Datapath
New function!
Operators, users, 3rd party developers, researchers, …

## Slide 13: 2) Cache Decisions
In minimal flow-based datapath
“If header = x, send to port 4”
Flow
Table
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”

## Slide 14: How Can We Do This?
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
OS
OS
OS
OS
OS
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 15: Software Defined Network (SDN)
Feature
Feature
Network OS
1. Open interface to packet forwarding
3. Consistent, up-to-date global network view
2. At least one Network OS probably many. Open- and closed-source
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 16: Consequences
More innovation in network services
  Owners, operators, 3rd party developers, researchers can improve the network
  E.g. energy management, data center management, policy routing, access control, denial of service, mobility
Lower barrier to entry for competition
  Healthier market place, new players
Lower cost
  Infrastructure
  Management

## Slide 17: Example: Routing
OSPF
  RFC 2328: 245 pages
Distributed System
  Builds consistent, up-to-date map of the network: 101 pages
Dijkstra’s Algorithm
  Operates on map: 4 pages

## Slide 18: Example: Routing
OSPF = Dijkstra
IS-IS
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Distributed System
Custom Hardware
OS
OSPF
IS-IS
Distributed
System
Distributed
System

## Slide 19: Back to the main storyline …

## Slide 20: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 21: 1) Network OS
Network OS: distributed system that creates a consistent, up-to-date network view
  Runs on servers (controllers) in the network
  NOX, ONIX, HyperFlow, Kandoo, Floodlight, Trema, Beacon, Maestro, Beehive, OpenDayLight, … + more
Uses forwarding abstraction to:
  Get state information from forwarding elements
  Give control directives to forwarding elements

## Slide 22: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 23: 2) Control Program
Control program operates on view of network
  Input: global network view (graph/database)
  Output: configuration of each network device
Control program is not a distributed system
  Abstraction hides details of distributed state

## Slide 24: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 25: 3) Forwarding Abstraction
Purpose: Abstract away forwarding hardware
  Flexible
    Behavior specified by control plane
    Built from basic set of forwarding primitives
  Minimal
    Streamlined for speed and low-power
    Control program not vendor-specific
OpenFlow is an example of such an abstraction

## Slide 26: 4) Forwarding Substrate
Flow-based (next slides)
Small number of actions for each flow
  Plumbing: Forward to port(s)
  Control: Forward to controller
  Routing between flow-spaces: Rewrite header
  Bandwidth isolation: Min/max rate
External open API to flow-table

## Slide 27
Types of action
Allow/deny flow
Route & re-route flow
Isolate flow
Make flow private
Remove flow
What is a flow?
Application flow
All http
Jim’s traffic
All packets to Canada
…

## Slide 28: Flowspace
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace

## Slide 29
Open standard to run experimental protocols in production networks
  API between the forwarding elements and the network OS
Based in Stanford, supported by various companies (Cisco, Juniper, HP, NEC, …)
Used by universities to deploy innovative networking technology

## Slide 30: Traditional Switch
Ethernet Switch

## Slide 31: Traditional Switch
Data Path (Hardware)
Control Path
Control Path (Software)

## Slide 32: OpenFlow Switch
OpenFlow Protocol (SSL,TLS)
Data Path (Hardware)
OpenFlow
Ethernet Switch
Network OS
Control Program A
Control Program B

## Slide 33: OpenFlow Rules
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Flow
Table(s)
“If header = p, send to port 4”
“If header = ?, send to me”
“If header = q, overwrite header with r, add header s, and send to ports 5,6”

## Slide 34: Plumbing Primitives
<Match, Action>
Match arbitrary bits in headers:
  Match on any header, or new header
  Allows any flow granularity
Action
  Forward to port(s), drop, send to controller
  Overwrite header with mask, push or pop
  Forward at specific bit-rate
Header
Data
Match: 1000x01xx0101001x

## Slide 35: OpenFlow Rules – Cont’d
Exploit the flow table in switches, routers, and chipsets
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Action
Statistics
Rule
(exact & wildcard)
Default Action
Statistics
Flow 1.
Flow 2.
Flow 3.
Flow N.
Notes: 35

## Slide 36: Flow Table Entry
OpenFlow Protocol Version 1.0
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask what fields to match
Packet + byte counters

## Slide 37: Examples
Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
port3
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
00:2e..
00:1f..
0800
vlan1
1.2.3.4
5.6.7.8
4
17264
80
port6
Firewall
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop

## Slide 38: Examples
Routing
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
vlan1
*
*
*
*
*
port6,
port7,port9

## Slide 39: OpenFlow Hardware
Cisco Catalyst 6k
NEC IP8800
HP Procurve 5400
Juniper MX-series
WiMax (NEC)
PC Engines
Quanta LB4G
More ...

## Slide 40: Some fun facts …
VMware purchased Nicira for $1.26 billion in 2012
  VMware Purchased VeloCloud Networks in 2017 (amount unknown!)
Orion (2022)
  Google’s 2nd generation SDN control plane
  Responsible for configuration, management, real-time network control
  In all their data center, campus, and private Wide Area (B4) networks
  In production for over 4 years
Notes: A startup SDN company that was made by a grad @ Stanford, Martin Casado, same student that came up with the idea of a centralized controller for the network!

## Slide 41: OpenFlow Usage Example
OpenFlowSwitch.org
Controller
OpenFlow
Switch
PC
Dedicated OpenFlow Network
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Protocol
Peter’s code
Rule
Action
Statistics
Rule
Action
Statistics
Rule
Action
Statistics
Peter
Notes: 41

## Slide 42: Usage examples
Peter’s code:
  Static “VLANs”
  His own new routing protocol: unicast, multicast, multipath, load-balancing
  Network access control
  Home network manager
  Mobility manager
  Energy manager
  Packet processor (in controller)
  IPvPeter
  Network measurement and visualization
  …
Notes: 42

## Slide 43: Another Example: Production networks as Research Test-beds!
Normal L2/L3 Processing
Flow Table
Production Slice
Research Slice
Controller

## Slide 44: Virtualize OpenFlow Switch
Normal L2/L3 Processing
Flow Table
Flow Table
Flow Table
Researcher A Slice
Researcher B Slice
Researcher C Slice
Production Slice
Controller A
Controller B
Controller C

## Slide 45: Virtualizing OpenFlow FlowVisor OSDI’10
OpenFlow
Switch
OpenFlow
Protocol
FlowVisor & Policy Control
C’s
Controller
B’s
Controller
A’s
Controller
OpenFlow
Protocol
OpenFlow
Switch
OpenFlow
Switch
Policy Check:
Who can control certain packets?
Is this rule allowed?
Notes: Hypervisor ->FloVisor

## Slide 46: Virtualizing OpenFlow FlowVisor OSDI’10
OpenFlow
Switch
OpenFlow
Protocol
FlowVisor & Policy Control
http
Load-balancer
Multicast
Broadcast
OpenFlow
Protocol
OpenFlow
Switch
OpenFlow
Switch
Policy Check:
Who can control certain packets?
Is this rule allowed?
Notes: Hypervisor ->FloVisor

## Slide 47: Food for Thought
What are the challenges in switching from traditional networks to OpenFlow networks?
What are the opportunities?