## Slide 1: A Case for Toggle-Aware Compression for GPU Systems
Gennady Pekhimenko,
Nandita Vijaykumar,
Onur Mutlu, Todd C. Mowry
Evgeny Bolotin, Stephen W. Keckler

## Slide 2: Executive Summary
Data compression is a known technique to decrease the bandwidth pressure
Observation: Compression significantly increases the energy cost of communication by increasing the number of bit toggles (bit flips)
Our approach: Toggle-Aware Compression
Energy Control (EC): send compressed data only when it is beneficial
Metadata Consolidation (MC): consolidates metadata bits to reduce the bit toggle count
Key results: 2.2X increase in bit toggles reduced to only 1.1X with most of the performance benefits preserved

## Slide 3: Performance and Energy Efficiency
Energy efficiency
Applications today are data-intensive
Memory Caching
Databases
Graphics

## Slide 4: Computation vs. Communication
Data movement is very costly
  Integer operation: ~1 pJ
  Floating operation: ~20 pJ
  Low-power memory access: ~1200 pJ
Implication
  Transfer less or keep data near processing units
Modern memory systems are bandwidth constrained
Sources:
Bill Dally (NVIDIA/Stanford)
Kayvon Fatahalian (CMU)
Notes: This data intensity puts a significant pressure on the available bandwidth of modern memory systems – hence bandwidth is limited.
Moreover, more efficient today tends to mean less data to transfer (transfer less and keep more information near processing elements).
1/2 the BW of modern LPDDR continuously exceeds the entire power budget of a mobile phone.

## Slide 5: Potential for Data Compression
Significant redundancy in memory transfers:
0x00000000
How can we exploit this redundancy?
  Bandwidth compression
    Provides effect of a higher effective bandwidth without increasing the number of wires or raising the frequency
0x0000000B
0x00000003
0x00000004
…

## Slide 6: Bandwidth Compression for GPUs
Chart: Compression Ratio
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.2773 | 1.2912 | 1.3721 | 1.2468 | 1.4379 | 1.0061 | 1.2549 | 1.2557 | 1.5687 | 1.4733 | 1.4291 | 1.6303 | 1.7156 | 1.724 | 1.5616
Compression is effective in providing higher bandwidth
221 apps
from NVIDIA
21 apps

## Slide 7: Common Wisdom about Compression
Higher effective capacity
Higher effective bandwidth
(Usually) lower energy consumption
Compression/Decompression overhead
Complexity/Cost to support variable size
A new problem:
Significant increase in the bit toggle count
(# bit flips), despite less bits sent

## Slide 8: What is a Bit Toggle?
0
1
0011
Previous data:
Bit Toggles
Energy = C*V2
How energy is spent in data transfers:
0101
New data:
0
0
1
0
1
1
Energy:
Energy of data transfers (e.g., NoC, DRAM) is proportional to the bit toggle count

## Slide 9: Excessive Number of Bit Toggles
0x00003A00
0x8001D000
0x00003A01
0x8001D008
…
Flit 0
Flit 1
XOR
000000010….01000
=
# Toggles = 2
Compressed Cache Line (FPC)
0x5 0x3A00
0x7 8001D000
0x5 0x3A01
Flit 0
Flit 1
XOR
001001111 … 110100011000
=
# Toggles = 31
0x7 8001D008
…
5 3A00 7 8001D000 5 1D
1 01 7 8001D008 5 3A02 1
Uncompressed Cache Line

## Slide 10: Effect of Compression on Bit Toggles
Chart: Normalized Bit Toggle #
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.1884 | 1.1267 | 1.1487 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.9797 | 2.1896 | 1.93 | 1.4886 | 1.6155 | 1.2358 | 2.0462
Compression significantly increases bit toggle count

## Slide 11: Outline
Motivation
Key Observations
Toggle-Aware Compression:
  Energy Control (EC)
  Metadata Consolidation (MC)
Evaluation
Conclusion

## Slide 12: Energy Control Decision Flow
$Line
Compress
Comp. $Line
Count Toggles
Select
EC
Decision
T0
T1
BW
Utilization
CR
$Line
Send compressed
or uncompressed

## Slide 13: How to Make the EC Decision?
Energy
  Battery life
Energy X Delay
  Balance performance and energy
Energy X Delay2
  Fixed power with voltage scaling
Energy: ~ Toggle #, Delay ~ 1/(Comp. Ratio)
  When bandwidth utilization (BU) is high (>50%) use 1 / (1 - BU) coefficient

## Slide 14: EC in the System
Streaming Multiprocessor
L1D
Compressor/
Decompressor
Energy Control
Compressor/
Decompressor
Energy Control
NoC
LLC
LLC
Compressor/
Decompressor
Energy Control
Compressor/
Decompressor
Energy Control
off-chip bus
DRAM

## Slide 15: Energy Control Summary
Bit toggle count: compressed vs. uncompressed
Use a heuristic (Energy X Delay or Energy X Delay2 metric) to estimate the trade-off
Take bandwidth utilization into account
Throttle compression when it is not beneficial

## Slide 16: Metadata Consolidation
Compressed Cache Line with FPC, 4-byte flits
Toggle-aware FPC: all metadata consolidated
0x5,0x3A00,
0x5, 0x3A01,
0x5, 0x3A02,
…
Consolidated
Metadata
0x5, 0x3A03,
0x3A00,
0x3A01,
0x3A02,
0x3A03,
0x5 0x5 … 0x5
# Toggles = 18
# Toggles = 2

## Slide 17: Outline
Motivation
Key Observations
Toggle-Aware Compression:
  Energy Control (EC)
  Metadata Consolidation (MC)
Evaluation
Conclusion

## Slide 18: Methodology
Simulator: GPGPU-Sim 3.2.x and in-house simulator
Workloads:
  NVIDIA apps (discrete and mobile): 221 apps
  Open-source (Lonestar, Rodinia, MapReduce): 21 apps
System parameters (Fermi):
  15 SMs, 32 threads/warp
  48 warps/SM, 32768 registers, 32KB Shared Memory
  Core: 1.4GHz, GTO scheduler, 2 schedulers/SM
  Memory: 177.4GB/s BW, GDDR5
  Cache: L1 - 16KB; L2 - 768KB

## Slide 19: Effect of EC on Bit Toggle Count
Chart: Normalized Bit Toggle Count
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.1884 | 1.1267 | 1.1487 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.9797 | 2.1896 | 1.93 | 1.4886 | 1.6155 | 1.2358 | 2.0462
With EC | 1.0382 | 1.0284 | 1.0494 | 1.009 | 1.047 | 1.0021 | 1.0345 | 1.0352 | 1.1484 | 1.1513 | 1.5484 | 1.3533 | 1.4125 | 1.0317 | 1.7288
EC significantly reduces the bit toggle count
Works for different compression algorithms

## Slide 20: Effect of EC on Compression Ratio
Chart: Compression Ratio
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.2773 | 1.2912 | 1.3721 | 1.2468 | 1.4379 | 1.0061 | 1.2549 | 1.2557 | 1.5687 | 1.4733 | 1.4291 | 1.6303 | 1.7156 | 1.724 | 1.5616
With EC | 1.2653 | 1.2793 | 1.3631 | 1.2174 | 1.419 | 1.0034 | 1.1321 | 1.1324 | 1.4144 | 1.3154 | 1.3681 | 1.5866 | 1.6537 | 1.6867 | 1.5121
EC preserves most of the benefits of compression

## Slide 21: Bit Toggles for C-Pack Algorithm
Chart: Normalized Bit Toggle Count
| CUDA | BFS | CONS | FWT | JPEG | LPS | MUM | RAY | SLA | TRA | lonestar | bfs | bh | mst | sp | sssp | Mars | Kmeans | MatrixMul | PageViewCount | PageViewRank | SimilarityScore | rodinia | heartwall | nw | GeoMean

Without EC | 2.0124 | 1.7547 | 1.0001 | 1.4307 | 0.85681 | 1.4375 | 0.95824 | 2.767 | 2.3753 | 1.1673 | 1.119 | 1.8597 | 1.216 | 1.2967 | 1.8163 | 9.6691 | 4.1442 | 10.6658 | 5.8057 | 2.4409 | 2.0521 | 2.0462
EC | 1.4185 | 1.6763 | 1 | 1.4103 | 0.83794 | 1.2693 | 0.9243 | 1.4034 | 1.3029 | 0.95982 | 1.1082 | 1.7146 | 1.1923 | 0.99703 | 1.6611 | 8.2521 | 3.9372 | 9.3507 | 4.4751 | 1.8181 | 1.8321 | 1.7288
Different tradeoffs for different applications

## Slide 22: DRAM Energy for C-Pack
Chart: Normalized DRAM Energy
| CUDA | BFS | CONS | FWT | JPEG | LPS | MUM | RAY | SLA | TRA | lonestar | bfs | bh | mst | sp | sssp | Mars | Kmeans | MatrixMul | PageViewCount | PageViewRank | SimilarityScore | rodinia | heartwall | nw | GeoMean
Without EC | 1.0504 | 1.161 | 1 | 0.44893 | 0.51053 | 1.061 | 0.92636 | 1.0449 | 1.2798 | 0.45092 | 0.74298 | 0.97325 | 1.0275 | 0.64906 | 0.8655 | 2.6804 | 1.3811 | 3.0811 | 1.766 | 1.4082 | 0.7788 | 1.0204
EC | 0.9229 | 1.1169 | 1 | 0.44772 | 0.50935 | 1.0039 | 0.91495 | 0.76017 | 0.99855 | 0.44076 | 0.73899 | 0.96069 | 1.0191 | 0.60737 | 0.84222 | 2.4184 | 1.3729 | 2.6284 | 1.6502 | 1.1468 | 0.76193 | 0.94944
7% average DRAM energy reduction, up to 28% for TRA

## Slide 23: Effect of Metadata Consolidation (MC)
Chart: Normalized Bit Toggle Count
| CUDA | BFS | CONS | FWT | JPEG | LPS | MUM | RAY | SLA | TRA | lonestar | bfs | bh | mst | sp | sssp | Mars | Kmeans | MatrixMul | PageViewCount | PageViewRank | SimilarityScore | rodinia | heartwall | nw | GeoMean
Without EC | 1.6416 | 1.8493 | 1 | 2.1026 | 1.7013 | 1.3774 | 1.0576 | 6.0516 | 1.9667 | 1.0189 | 1.1229 | 1.3015 | 1.5273 | 1.0696 | 1.9302 | 3.9289 | 4.44 | 3.8981 | 3.8166 | 2.4636 | 1.756 | 1.93
MC | 1.6438 | 1.472 | 1 | 1.994 | 1.2783 | 1.2235 | 1.0204 | 4.5703 | 1.2445 | 0.9913 | 1.1022 | 1.2238 | 1.272 | 1.0495 | 1.9442 | 2.8622 | 4.1657 | 2.6888 | 2.8214 | 2.1127 | 1.5833 | 1.6674
EC | 1.4981 | 1.7535 | 1 | 1.8462 | 1.1343 | 1.2262 | 1.0241 | 2.9997 | 1.1329 | 0.97083 | 1.0969 | 1.2064 | 1.087 | 1.0188 | 1.6748 | 2.8533 | 3.422 | 2.5959 | 2.5079 | 1.8066 | 1.5132 | 1.5484
MC+EC | 1.477 | 1.4489 | 1 | 1.8571 | 0.94169 | 1.1559 | 0.99921 | 2.5299 | 1.0798 | 0.97335 | 1.0933 | 1.1944 | 1.1154 | 1.0043 | 1.7395 | 2.4021 | 3.3113 | 2.1397 | 2.2446 | 1.7869 | 1.4538 | 1.4618
FPC compression algorithm
MC is effective in reducing the bit toggle count
But less effective than EC

## Slide 24: Other Results in the Paper
On-chip interconnect results
  Higher impact of bit toggles on the interconnect energy, but lower overall energy impact
Data bus inversion (DBI)
  EC and MC benefits are independent on whether DBI encoding is used
Complexity estimation
  Energy and latency
Analyzing different EC decision functions
  Energy x Delay vs. Energy x Delay2

## Slide 25: Conclusion
Data compression is a known technique to decrease the bandwidth pressure
Observation: Compression significantly increases the energy cost of communication by increasing the number of bit toggles (bit flips)
Our approach: Toggle-Aware Compression
Energy Control (EC): send compressed data only when it is beneficial
Metadata Consolidation (MC): consolidate metadata bits to reduce the bit toggle count
Key results: 2.2X increase in bit toggles reduced to only 1.1X with most of the performance benefits preserved

## Slide 26: A Case for Toggle-Aware Compression for GPU Systems
Gennady Pekhimenko,
Nandita Vijaykumar,
Onur Mutlu, Todd C. Mowry
Evgeny Bolotin, Stephen W. Keckler