## Slide 1: Energy-Efficient Data Compression for Modern Memory Systems
Gennady Pekhimenko
ACM Student Research Competition
March, 2015

## Slide 2: High Performance Computing Is Everywhere
Modern memory systems are bandwidth constrained
Energy efficiency is key across the board
Data Compression is a promising technique to address these challenges
Applications today are data-intensive
Notes: Traditionally, memory systems were optimized for high capacity and low latency, as the key performance limiting factors in the CPU-oriented world. More recently, GPU-based systems make stronger than ever presence on the market both as discrete accelerators …
and as a part of SoC systems in modern mobile devices, for example, cell phones and tablets.

## Slide 3: Potential of Data Compression
Multiple simple patterns: zeros, repeated values, narrow values, pointers
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
Different Algorithms:
  BΔI [PACT’12] is based on Base-Delta Encoding
  Frequent Pattern Compression (FPC) [ISCA’04]
  C-Pack [Trans. on VLSI’12]
  Statistical Compression (SC2) [ISCA’14]
  . . .
These algorithms improve performance
But there are challenges…
Low Dynamic Range:
Differences between values are significantly smaller than the values themselves

## Slide 4: Energy Efficiency: Bit Toggles
0
1
0011
Previous data:
Toggles
Energy = C*V2
How energy is spent in data transfers:
0101
New data:
0
0
1
0
1
1
Energy:
Energy of data transfers (e.g., NoC, DRAM) is proportional to the number of toggles

## Slide 5: Excessive Number of Bit Toggles
0x00003A00
0x8001D000
0x00003A01
0x8001D008
…
Flit 0
Flit 1
XOR
000000010….00001
=
# Toggles = 2
Compressed Cache Line (FPC)
0x5 0x3A00
0x7 8001D000
0x5 0x3A01
Flit 0
Flit 1
XOR
001001111 … 110100011000
=
# Toggles = 31
0x7 8001D008
…
5 3A00 7 8001D000 5 1D
1 01 7 8001D008 5 3A02 1
Uncompressed Cache Line

## Slide 6: Effect of Compression on Bit Toggles
Chart: Normalized Toggle #
| FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | Discrete | Mobile
Base | 1.1884 | 1.1267 | 1.1487 | 1.2039 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.8349 | 1.9797 | 2.1896
NVIDIA Apps: Mobile GPU – 54 in total, Discrete GPU – 167 in total
Significant increase in the number of toggles, hence potentially increase in consumed energy

## Slide 7: Toggle-Aware Data Compression
Problem:
1.53X effective compression ratio
2.19X increase in toggle count
Goal:
Find the optimal tradeoff between toggle count and compression ratio
Key Idea:
Determine toggle rate for compressed vs. uncompressed data
Use a heuristic (Energy X Delay or Energy X Delay2 metric) to estimate the tradeoff
Throttle compression to reach estimated tradeoff

## Slide 8: Energy Control (EC) Flow
$Line
Compression
Comp. $Line
# Toggles
# Toggles
Energy Control
T0
T1
Comp.
ratio
Decision function
Send compressed
or uncompressed
Select

## Slide 9: Energy Control: Effect on Bit Toggles
NVIDIA Apps: Mobile GPU – 54 in total, Discrete GPU – 167 in total
Chart: Normalized Toggle #
| FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | Discrete | Mobile
Base | 1.1884 | 1.1267 | 1.1487 | 1.2039 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.8349 | 1.9797 | 2.1896
EC | 1.0382 | 1.0284 | 1.0494 | 1.0565 | 1.009 | 1.047 | 1.0021 | 1.0345 | 1.0352 | 1.2366 | 1.1484 | 1.1513
Significant decrease in the number of toggles

## Slide 10: Energy Control: Effect on Compression Ratio
NVIDIA Apps: Mobile GPU – 54 in total, Discrete GPU – 167 in total
Modest decrease in compression ratio
Chart: Compression Ratio
| FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | Discrete | Mobile
Base | 1.2773 | 1.2912 | 1.3721 | 1.3496 | 1.2468 | 1.4379 | 1.0061 | 1.2549 | 1.2557 | 1.5255 | 1.5687 | 1.4733
EC | 1.2653 | 1.2793 | 1.3631 | 1.3285 | 1.2174 | 1.419 | 1.0034 | 1.1321 | 1.1324 | 1.4436 | 1.4144 | 1.3154

## Slide 11: Optimization: Metadata Consolidation
Compressed Cache Line with FPC, 4-byte flits
Toggle-aware FPC: all metadata consolidated
0x5, 0x3A00,
0x5, 0x3A01,
0x5, 0x3A02,
…
All metadata
0x5, 0x3A03,
0x3A00,
0x3A01,
0x3A02,
0x3A03,
0x5 …0x5 0x5
# Toggles = 18
# Toggles = 2
Additional 3.2%/2.9% reduction in toggles for FPC/C-Pack

## Slide 12: Summary
Bandwidth and energy efficiency are the first order concerns in modern systems
Data compression is an attractive way to get higher effective bandwidth efficiently
  Problem: Excessive toggles (‘0’’1’) waste power/energy
  Key Idea:
    Estimate the tradeoff between compression ratio and energy efficiency (Energy X Delay or Energy X Delay2 )
    Throttle compression when the overall energy increases

## Slide 13: Energy-Efficient Data Compression for Modern Memory Systems
Gennady Pekhimenko
ACM Student Research Competition
March, 2015