## Slide 1: Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency
Gennady Pekhimenko,
Vivek Seshadri , Yoongu Kim, Hongyi Xin, Onur Mutlu,
Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 2: Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Old Idea: Compress data in main memory
Notes: Main memory is a limited shared resource in modern systems.
At the same time, we observe that there is a significant redundancy in in-memory data.
We exploit this observation by revising an old idea – data compression in main memory.

## Slide 3: Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Old Idea: Compress data in main memory
Problem: How to avoid inefficiency in address computation?
Notes: Unfortunately, there is major problem that needs to be addressed to employ hardware-based memory compression --
inefficiency in address computation that is required to locate the data after compression.

## Slide 4: Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Old Idea: Compress data in main memory
Problem: How to avoid inefficiency in address computation?
Solution: Linearly Compressed Pages (LCP): fixed-size cache line granularity compression
Notes: We propose a solution to this problem – Linearly Compressed Pages (LCP) – with the key idea that it is more efficient to use fixed-size cache line
granularity compression per page to simplify the address computation.

## Slide 5: Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Old Idea: Compress data in main memory
Problem: How to avoid inefficiency in address computation?
Solution: Linearly Compressed Pages (LCP): fixed-size cache line granularity compression
1. Increases capacity (62% on average)
2. Decreases bandwidth consumption (24%)
3. Improves overall performance (13.9%)
Notes: Our extensive evaluation shows that LCP …

## Slide 6: Linearly Compressed Pages (LCP)
64B
64B
64B
64B
. . .
64B
Uncompressed Page (4KB: 64*64B)
Notes: We start with an uncompressed 4KB page.

## Slide 7: Linearly Compressed Pages (LCP)
64B
64B
64B
64B
. . .
. . .
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed
Data (1KB)
Notes: In LCP, we restrict the compression algorithm to provide the same fixed compressed size for all cache lines.
The primary advantage of this restriction is that now address computation is a simple linear scaling of the previous offset before compression.
This also leads to a compressed data region being fixed in size (e.g., 1KB with 4:1 compression).

## Slide 8: Linearly Compressed Pages (LCP)
64B
64B
64B
64B
. . .
. . .
M
Metadata (64B): ? (compressible)
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed
Data (1KB)

## Slide 9: Linearly Compressed Pages (LCP)
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B): ? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed
Data (1KB)
Notes: Unfortunately, not all data is compressible, hence we need to keep exceptional cache lines in a separate exception region in the uncompressed form.
With metadata region storing a bit per cache line -- to represent the fact that some cache lines are compressed and some are not.

## Slide 10: Linearly Compressed Pages (LCP)
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B): ? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed
Data (1KB)
Tomorrow, 8:30am, Session 3A