## Slide 1: Introduction
Soheil Abbasloo
Department of Computer Science
University of Toronto
Fall 2022

## Slide 2
Barrett Lyon, The Opte Project

## Slide 3: The Internet

## Slide 4: The Internet An exciting place

## Slide 5: 26 Billion
estimated* # of Internet connected devices in 2022

## Slide 6: 30 Billion
estimated* # of Internet connected devices in 2023

## Slide 7: 13 Exabyte
estimated* daily global IP traffic in 2022
Exa

## Slide 8: If = 1 Byte

## Slide 9
5000 Volume(Great Wall of China) 1 Exabyte

## Slide 10: The Internet A fragile place

## Slide 11
Despite being absolutely critical,
the Internet infrastructure is
inherently fragile

## Slide 12
“An update in our [Rogers] core IP [internet protocol] network …
caused our IP routing network to malfunction,"

## Slide 14
“Someone in Google fat-thumbed a
Border Gateway Protocol (BGP) advertisement
and sent Japanese Internet traffic into a black hole.”

## Slide 15: Course Goals

## Slide 16: Course Goals
How the Internet works
With the focus on
Key intuitions and design ideas

## Slide 17: Course Goals
How the Internet works
With the focus on
Key intuitions and design ideas
From Basics: Naming, Layering, Socket Programming, Packet Switching, Reliability, Sharing, etc.
To Advance Networking: Routers and Switches, Security, Congestion Control, Software Defined Networking, etc.
Notes: Make you ready
to reason about (and architect) a distributed system/network ;)

## Slide 18
Course Web Page:
http://www.cs.toronto.edu/~abbasloo/teaching/csc458/
Slides, assignments, readings, course info, …
Class on Piazza:
https://piazza.com/utoronto.ca/fall2022/csc458
Access Code: csc458#fall22!
Q&A, Questions related to the course, a response time guarantee < 48 hours!

## Slide 19
Each TA is responsible for certain assignment!
  Please check class web page for the list of TAs
  And which assignments they are responsible for.
  Only contact TAs regarding their assigned assignments!
Textbook
  “Computer Networks: A Systems Approach”, (5th Edition), Peterson, Davie, 2011
Recommended books
  “UNIX Network Programming, Volume I: The Sockets Networking API”, W. Richard Stevens, Bill Fenner, and Andrew M. Rudoff, 3rd edition, 2003
  “TCP/IP Illustrated, Volume 1: The Protocols”, W. Richard Stevens, 1993

## Slide 20
Your Final Grade
Programming Assignments
Problem Sets
Midterm Exam
Final Exam
30%
20%
20%
30%

## Slide 21
Academic Integrity
  All submissions must present original, independent work.
  We take academic offenses very seriously.
  Please read
    Course information sheet
    “Guideline for avoiding plagiarism” http://www.cs.toronto.edu/~fpitt/documents/plagiarism.html
    “Advice about academic offenses” http://www.cs.toronto.edu/~clarke/acoffences/

## Slide 22
Accessibility Needs
  The University of Toronto is committed to accessibility.
  If you require accommodations or have any accessibility concerns, please visit http://studentlife.utoronto.ca/accessibility as soon as possible.

## Slide 23
Special Thanks To:
  Scott Shenker & Sylvia Ratnasamy from UC, Berkeley
  Jennifer Rexford from Princeton University
  Nick McKeown from Stanford University

## Slide 24: How the Internet Works
(a very very short version!)

## Slide 25
www.cs.toronto.edu

## Slide 26
My
Program
Someone else’s
Program

## Slide 27
Data
Data

## Slide 28
Notes: Let’s see how this image is sent across the Internet from one smartphone to another….

## Slide 30: A more accurate model
Soheil Abbasloo
40 St George St,
Toronto, ON M5S 2E4
CA
Me
You
From
Address
To
Address

## Slide 31: Multiple packets in pipeline at same time
Soheil Abbasloo
40 St George St,
Toronto, ON M5S 2E4
CA
Me
You
Soheil Abbasloo
40 St George St,
Toronto, ON M5S 2E4
CA
Soheil Abbasloo
40 St George St,
Toronto, ON M5S 2E4
CA
Soheil Abbasloo
40 St George St,
Toronto, ON M5S 2E4
CA
Soheil Abbasloo
40 St George St,
Toronto, ON M5S 2E4
CA

## Slide 32: Packets may be damaged
Data
Data
?!%%*

## Slide 33: Packets may arrive out of order
1
2

## Slide 34: Packets may be duplicated
Data
Data
Duplicate

## Slide 35: They may not arrive at all!
Data
Data
Full

## Slide 36: Summary so far
Applications send and receive data in packets….
…over an Internet that is unreliable.

## Slide 37: How packets find their way across the Internet

## Slide 38: Internet addresses
Data
Internet “IP”
Address
Data

## Slide 39: Internet Addresses (“IP address”)
All Internet packets carry a destination IP address.
We usually write the IP address like this:
128.100.20.20
Data
Internet “IP”
Address

## Slide 40: Routers forward packets one at a time.
Data
Data
Routers look at IP addresses, then send packets to a router closer to the destination.

## Slide 41: IP Addresses
The IP address tells a router where to send the packet next.
IP addresses have structure
128.100.20.20
UofT
A network in the CS department at UofT
A computer at that network
213.233.161.70
An address at Sharif University of Technology
A network in Middle East
A computer There

## Slide 42: Can we see the path our packets take?
Yes!
On your computer, try: “ping google.com”
and “traceroute google.com”
(Windows: “tracert google.com”)
Notes: traceroute –q1 yuba.stanford.edu

## Slide 43: ping www.doshisha.ac.jp
From Toronto, it takes about 190ms to reach Japan and back again (“round-trip-time”)

## Slide 44
Kyoto
10,565km
RTT = 106ms
Q: So why did my “ping” take 190ms?

## Slide 45: traceroute

## Slide 46: From Toronto to Doshisha University (Kyoto)
Soheil@ Home on Bell Network > traceroute –f 4 -q1 istc.doshisha.ac.jp
traceroute to istc.doshisha.ac.jp (202.23.190.159), 30 hops max, 60 byte packets
4 *
5 tcore4-toronto12_37.net.bell.ca (64.230.59.200) 24.838 ms
6 cr01-mtrlpq01h33_bundle-ether9.net.bell.ca (142.124.127.231) 19.103 ms
7 tcore4-montreal02_bundle-ether57.net.bell.ca (142.124.127.250) 26.140 ms
8 tcore4-newyorkaa_hundredgige0-3-0-0.net.bell.ca (64.230.79.144) 24.725 ms
9 bx7-newyork83_hundredgige0-7-0-0.net.bell.ca (64.230.79.91) 23.612 ms
10 NYIIX.IIJ.Net (198.32.160.42) 27.037 ms
11 nyc002bb00.IIJ.Net (58.138.81.49) 29.022 ms
12 sea001bb00.IIJ.Net (58.138.81.58) 73.050 ms
13 tky009bb00.IIJ.Net (58.138.88.225) 156.554 ms
14 tky009ix50.IIJ.Net (58.138.114.230) 167.123 ms
15 202.232.6.18 (202.232.6.18) 162.362 ms
16 150.99.18.34 (150.99.18.34) 192.893 ms
17 doshisha-LAN.gw.sinet.ad.jp (150.99.196.66) 189.294 ms
18 *

## Slide 47
Internet Initiative Japan’s (IIJ’s) Backbone Network
Toronto -> Montreal -> NYC -> London -> Tokyo -> Kyoto !
https://bit.ly/3Jd9kM1
Notes: Internet Service Providers -> Tier 1, 2, and 3 …

## Slide 48
Kyoto
Toronto-Montreal : 550km
Montreal-NYC: 600km
NYC-London: 5,600km
London-Tokyo: 9,500km
Tokyo-Kyoto: 500km
RTT ~= 170ms

## Slide 49: Try traceroute to….
www.ntua.gr, www.netflix.com, wikipedia.org, …

## Slide 50: Competition (optional)
Task: Find the longest loop-free traceroute in the Internet
Rules
The source and destination can be any addresses you can reach.
At most one hop may return a “*” (i.e. not respond)
Packets must flow over physical links and through real routers. i.e. not a virtual, simulated or emulated network.
Prize: Big bragging rights!

## Slide 51: Summary so far
Applications send and receive data in packets….
…over an Internet that is unreliable.
Packets are forwarded hop-by-hop based on the final destination address.

## Slide 52: The Internet cannot be trusted!!
Data
The Internet doesn’t promise to deliver packets in order.
It doesn’t promise to deliver packets quickly, or on time.
It doesn’t even promise to deliver them at all!
It just makes a “best-effort” attempt.

## Slide 53: Sending data reliably over an Internet that is unreliable

## Slide 54: How Network Applications Communicate
My
Program
Someone else’s
Program
The most common method:
  Communication is in both directions – “bidirectional”.
  Communication is reliable (if there is a working path between the two computers).
It’s like an unformatted pipe:
  You push data in at one end, and it pops out correctly at the other end.
  The applications decide how the data is formatted inside the pipe.

## Slide 55: Byte Stream Model
Internet
Setup connection
A
B

## Slide 56: Byte Stream Model
A
B
Stream of bytes
Internet
Stream of bytes

## Slide 57: Byte Stream Model
Internet
Close connection
A
B

## Slide 58: World Wide Web (HTTP)
Internet
Setup connection
www.utoronto.ca
Client
Server

## Slide 59: World Wide Web (HTTP)
Internet
www.utoronto.ca
GET/HTTP/1.1 index.html
Stream of bytes
HTTP/1.1 200 OK <…contents of index.html…>
Stream of bytes
Client
Server

## Slide 60: World Wide Web (HTTP)
Internet
www.utoronto.ca
Client
Server
Close connection

## Slide 61
“IP”
Your Application program
e.g. Chrome, Skype
Data
“IP”
The server
e.g. Google, Facebook
“TCP”
“TCP”
TCP makes sure all
the data is delivered

## Slide 62: TCP’s job
Makes sure all data is delivered correctly.
Delivers data to the application in the right order.
How?
  Add sequence numbers to every packet (so the receiver can check if any are missing, and put them in right order)
  When a packet arrives, send an acknowledgment of receipt or “ACK” back to the sender
  If no acknowledgment is received, resend the data

## Slide 64: Packets are “encapsulated” by different “layers” of processing

## Slide 65: http client (e.g. Chrome)
IP
Application
Ethernet
TCP
http request
TCP
(http)
GET index.html
IP
IP address
(TCP)
TCP
(http)
Ethernet
Ethernet “MAC” address
(IP)
Chrome
TCP
(http)
IP
IP address
(TCP)
TCP
(http)
IP
IP address
(TCP)
Ethernet
Ethernet “MAC” address
(IP)
“Deliver to the http server”
“…at this destination”
“…starting with this link”

## Slide 66: Here it goes….
TCP data
(http)
IP data
IP Address
(TCP)
Ethernet data
Ethernet “MAC” address
(IP)

## Slide 67: http server (e.g. www.google.com)
IP
Application
Ethernet
TCP
http request
TCP
(http)
TCP
(http)
IP
IP address (TCP)
TCP
(http)
IP
IP address
(TCP)
Ethernet
Ethernet “MAC” address
(IP)
GET file
“Deliver to the http server”
“Deliver to TCP”
http server

## Slide 68: Summary of what we learned
Applications send and receive data in packets….
…over an Internet that is unreliable.
Packets are forwarded hop-by-hop using the IP destination address.
Our applications use TCP to make sure they are
delivered and put back in the correct order.
My
Program
Someone else’s
Program

## Slide 69: That was a very big picture of how the Internet works

## Slide 70: That was a very big picture of How the Internet works Now, Let’s go back and start from the basics . . .

## Slide 71: Back to the Basics: Part I

## Slide 72: What is a network made of?

## Slide 73: Three main components of a network
1- End-system

## Slide 74
End-systems: send & receive data
Car navigator
Smart Refrigerator
Smart Watch
Win PC
Linux Server
MAC Laptop

## Slide 75
2- Switch/Router

## Slide 76
Switches & routers forward data to the destination
Home modem
20cm
0.5kg
1Gbps
Internet Core Router
200cm
700kg
>12Tbps
https://www.cisco.com/c/en/us/products/collateral/routers/carrier-routing-system/data_sheet_c78-726136.html

## Slide 77
Links connect end-systems and switches
3- Link

## Slide 78
Different types of links for different types of usages
Copper
Optical Fiber
Wireless Links

## Slide 79: How is a network shared?

## Slide 80
shared link and switch resources

## Slide 81
How do we scale a network to many end-systems?
Full mesh
number of links?
per-node capacity?
Chain
Bus

## Slide 82
How do we scale a network to many end-systems?
Switched networks enable efficient scaling!

## Slide 83: Two approaches to sharing
Reservations
On demand

## Slide 84: Intuition: Three sources of “bursty” traffic
12Mbps
Time
Link capacity = 30Mbps
11Mbps
13Mbps

## Slide 85: Intuition: reservations
12Mbps
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading

## Slide 86: Intuition: on demand
No overloading
Time
Link capacity = 30Mbps

## Slide 87
Switching on-demand exploits statistical multiplexing better than reservations
Sharing using the statistics of demand
Good for bursty traffic (average << peak demand)

## Slide 88: Intuition: on demand
What do we do under overload?
Time
Link capacity = 30Mbps

## Slide 89: Statistical multiplexing is a recurrent theme in computer science
Phone network rather than dedicated lines
  ancient history
Packet switching rather than circuits
  today’s lecture
Cloud computing
  shared vs. dedicated machines

## Slide 90: Two approaches to sharing
Reservations
On demand
How are these implemented?

## Slide 91: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching
How are these implemented?

## Slide 92: Two approaches to sharing
Packet switching
  packets treated on demand
  admission control: per packet
Circuit switching
  resources reserved per active "connection"
  admission control: per connection

## Slide 93: Circuit Switching
src sends a reservation request to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 94: Circuit Switching
switch
src
dst
Reservation establishes a “circuit” within a switch

## Slide 95: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 96: Timing in Circuit Switching
time

## Slide 97: Timing in Circuit Switching
time

## Slide 98: Timing in Circuit Switching
time

## Slide 99: Timing in Circuit Switching
time

## Slide 100: Timing in Circuit Switching
time
Circuit establishment

## Slide 101: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer

## Slide 102: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 103
time
Example of poor efficiency:
The circuit is mostly idle due to traffic bursts
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 104
Information
time
Example of poor efficiency:
The circuit is used for a short amount of time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 105: Another problem of circuit switching
A
B
Circuit switching doesn’t “route around trouble”

## Slide 106: Circuit Switching
Pros
  predictable performance
  simple/fast switching (once circuit established)
Cons
  complexity of circuit setup/teardown
  inefficient when traffic is bursty
  circuit setup adds delay
  switch fails  its circuit(s) fails

## Slide 107: Packet switching
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 108: Packet switching
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 109: Packet Switching
Pros
  efficient use of network resources
  simpler to implement
  robust: can “route around trouble”
Cons
  unpredictable performance
  requires buffer management and congestion control

## Slide 110
To Reserve or not to Reserve?!