## Slide 1: Hardware Architectures for Deep Learning
Andrew Ling, Ph.D. – Engineering Manager Machine Learning Acceleration
OpenCL and the OpenCL logo are trademarks of Apple Inc.

## Slide 2: Disclaimer
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance of Intel products as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance. Buyers should consult other sources of information to evaluate the performance of systems or components they are considering purchasing. For more information on performance tests and on the performance of Intel products, visit Intel Performance Benchmark Limitations.
Some Results have been simulated and are provided for informational purposes only. Results were derived using simulations run on an architecture simulator. Any difference in system hardware or software design or configuration may affect actual performance.
Intel does not control or audit the design or implementation of third party benchmarks or websites referenced in this document. Intel encourages all of its customers to visit the referenced websites or others where similar performance benchmarks are reported and confirm whether the referenced benchmarks are accurate and reflect performance of systems available for purchase.

## Slide 3: End of Scaling
NVIDIA SC’13 Session
Additional transistors used for additional computation in space

## Slide 4: Taking Advantage of Parallelism
Intel® Stratix 10: up to 280M equivalent logic elements
FPGAs
CPUs
Intel® Xeon® processor E7 v4 product family: up to 24 Cores
Intel® Xeon® Phi Processor Family: up to 72 Cores
Multi-Cores
Towards more parallelism through spatial computing
Coarse Grain Parallelism
Fine Grain Parallelism
Notes: I just highlighted three very distinct trends that effect implementation choice
Increasing development costs of custom & ASSP solution
Market dynamics of shorter time in market & shorter time to market
Product Fragmentation - geographic driven or product feature driven
The solution is programmable!
It is programmable technologies that offer the greatest flexibility in solving our development problems.
I’ve shown here the spectrum of programmable solutions, from fine grain solutions like memories to course grain solutions like DSP & microprocessors.
Although we traditionally think of these devices as being very different they all share the same programming method through a simple digital bit stream.
The biggest difference has been the way in which we design for these technologies Today

## Slide 5: Temporal vs Spatial

## Slide 6: A simple program
add: R0  Load Mem[100]
  R1  Load Mem[101]
  R2  Load #42
  R2  Mul R1, R2
  R0  Add R2, R0
  Store R0  Mem[100]
kernel void
add( global int* Mem ) {
...
Mem[100] += 42*Mem[101];
}
OpenCL Code
Instruction Level (IR)
How does a program execute on a CPU?

## Slide 7: A simple 3-address CPU
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 8: Load memory value into register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData
R0  Load Mem[100]
R1Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 9: Load immediate value into register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 10: Multiply two registers, store result in register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 11: Add two registers, store result in register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 12: Store register value into memory
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0Mem[100]

## Slide 13: CPU activity, step by step
Time
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A

## Slide 14: Fixed Architectures and Flat Memory Systems
Worked well if your clock speed / MIPS increased every 18 months
Extremely easy to program
Power becoming the main limit to performance now – this approach will not scale anymore!

## Slide 15: Unroll the CPU hardware…
Space
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A

## Slide 16: … and specialize by position
Instructions are fixed. Remove “Fetch”
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A

## Slide 17: … and specialize
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A

## Slide 18: … and specialize
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A

## Slide 19: … and specialize
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
Wire up registers properly! And propagate state.
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 20: … and specialize
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
Wire up registers properly! And propagate state.
Remove dead data.
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 21: … and specialize
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
Wire up registers properly! And propagate state.
Remove dead data.
Reschedule!
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]

## Slide 22
Custom Datapath: Your Algorithm, in Space
load
load
store
42

## Slide 23
Build exactly what you need:
Operations
Data widths
Memory size, configuration
Efficiency:
Throughput / Latency / Power
Custom Datapath: Your Algorithm, in Space

## Slide 24: Rise of Deep learning

## Slide 25: Rise of Convolutional Neural Nets
Convolutions validated as a practical means of tackling deep learning classification problems.
FPGAs are known to be efficient when performing convolutions.

## Slide 26: CNN Computation in One Slide
Input Feature Map
(Set of 2D Images)
Filter
(3D Space)
Output Feature Map
-1
-1
-1
-1
9
-1
-1
-1
-1
Repeat for Multiple Filters to Create Multiple “Layers” of Output Feature Map
-1
3
-1
-1
-2
-1
7
-1
-1
1
-1
-1
-1
5
-1
-1
1
-1
-1
-1
3
4
0
-1
-1
-1
-1

## Slide 27: A Brief Introduction to FPGAs

## Slide 28: FPGAs and the Traditional FPGA Market
Notes: Talk about tradeoffs:
  Slower and larger than ASIC
    Because of programmability
  More expensive per unit at high volumes

## Slide 29: What’s in my FPGA?
Variable Precision DSP Blocks with Hardened Floating Point
M20K Internal Memory Blocks
I/O PLLs
Hard Memory Controllers, General Purpose IO Cells, LVDS
Transceiver Channels
Hard IP Per Transceiver, 8b/10b PCS, 64b/66b PCS, 10GBase-KR FEC, Interlaken PCS
Fractional PLLs
PCI Express Gen3 Hard IP
Core Logic Fabric

## Slide 30: What’s in my FPGA?
1-bit configurable
operation
Logic Element
1-bit register
(store result)
data_out
data_in
DSPs
On-chip Memory
Block
addr
data_in
data_out
Logic Elements are surrounded with a flexible interconnect

## Slide 31: A Case for FPGA Acceleration: Deep Learning

## Slide 32: Bringing Intel’s Deep Learning Accelerator (DLA) for Inference to the Masses
Development of Efficient Spatial Architecture for Deep Learning
  Leverage Flexibility of FPGA to generate energy efficient architectures
API calls to abstract FPGA use
  SW callable accelerator
  Support wide array of Deep Learning Frameworks
Model Optimizer & Inference Engine

## Slide 33: One Architecture Any Device Any Market
FPGA
Leverages 3 insights from SGEMM:
  Customized Spatial architecture that optimizes data accesses and creates efficient dataflow
  Creates large double-buffer to store all feature maps on-die
  Creates a systolic PE array to map nicely on 2D Spatial Logic Array on FPGA
Double-Buffer On-Chip RAM
3
6
7
8
9
2
4
5
1
3
6
7
8
9
2
4
5
1
9
6
8
5
7
4
3
2
1
9
6
8
5
7
4
3
2
1
9
6
8
5
7
4
3
2
1
DDR
Filters (on-chip RAM)

## Slide 34: Keys to DLA efficiency: leveraging the flexibility of the FPGA
1. Flexible compute and memory architecture
  Tune the geometry of the PE array, the width of the data path, etc.
  Tune number of banks, port widths and the size of the memories
2. Flexible precision: FP32  FP11  FP8  Ternary/Binary
  Reduce precision as much as topology allows
3. Flexible platforms
  DLA architecture can be implemented on different boards/platforms
4. Flexible graph structure
  Map complex and large graphs to DLA  general-purpose DL solution

## Slide 35: Keys to DLA efficiency: leveraging the flexibility of the FPGA
1. Flexible compute and memory architecture
  Tune the geometry of the PE array, the width of the data path, etc.
  Tune number of banks, port widths and the size of the memories
2. Flexible precision: FP32  FP11  FP8  Ternary/Binary
  Reduce precision as much as topology allows
3. Flexible platforms
  DLA architecture can be implemented on different boards/platforms
4. Flexible graph structure
  Map complex and large graphs to DLA  general-purpose DL solution

## Slide 36: Flexible levels of parallelism
FPGA
Double-Buffer On-Chip RAM
3
6
7
8
9
2
4
5
1
3
6
7
8
9
2
4
5
1
9
6
8
5
7
4
3
2
1
9
6
8
5
7
4
3
2
1
9
6
8
5
7
4
3
2
1
Filters (on-chip RAM)
Input depth
parallelism
Filter parallelism
(output depth)
External DDR
Levels of parallelism:
  Filter (output depth)
  Input depth
  Input width
  Input height
  Image (batching)
2
1
  PE array geometry can be customized to hyperparameters of given DL topology
  Achieve efficient execution of convolutions and inner products
Notes: * Describe the hardware first

## Slide 37: Flexible activation/weight buffering
FPGA
Double-Buffer On-Chip RAM
3
6
7
8
9
2
4
5
1
3
6
7
8
9
2
4
5
1
9
6
8
5
7
4
3
2
1
9
6
8
5
7
4
3
2
1
9
6
8
5
7
4
3
2
1
Filters (on-chip RAM)
Stream buffer size
Filter cache size
External DDR
2
1
  Buffers and pre-fetch scheme can be customized to hyperparameters of given DL topology
  Achieve efficient execution of convolutions and inner products
Minimize on-chip/off-chip data move:
  Stream buffer size
  Filter cache size
  Pre-fetch mechanisms
    On-demand
    Pre-load all / partial
Notes: * Describe the hardware first

## Slide 38: Feature Cache (Stream Buffer) and Slicing
Convolution
73x73x128
73x73x32
Un-Sliced Graph
720 M20Ks
Convolution Slice#1
73x73x128
73x37x32
Sliced Graph
Feature Cache
Feature Cache
180 M20Ks
Convolution Slice#2
DDR
Feature Cache
Feature Cache
DDR
Feature Cache Required: 900 M20Ks
73x36x32
73x37x128
73x36x128
73x73x16
Feature Cache Required: 384 M20Ks

## Slide 39: Feature Cache (Stream Buffer) and Slicing
Performance
Feature Cache Size
Small Feature Cache
Bigger PE array,
but more slicing
Performance Bottleneck = DDR
Big Feature Cache
Less slicing,
but smaller PE array
Performance Bottleneck = PE Compute
Sweet spot varies based on graph dimensions
PE Array Size

## Slide 40: Feature Cache (Stream Buffer) and Slicing
Performance
Small Feature Cache
Bigger PE array,
but more slicing
Performance Bottleneck = DDR
Big Feature Cache
Less slicing,
but smaller PE array
Performance Bottleneck = PE Compute
Slicing and DDR optimizations can improve performance at smaller feature cache sizes, allowing for the PE array to be scaled up
PE Array Size
Feature Cache Size

## Slide 41: Hardware / Software convergence

## Slide 42: Redefining Software
F. Vahid. It's Time to Stop Calling Circuits "Hardware“, IEEE Computer Magazine, September 2007
“The advent of field-programmable gate arrays requires that we stop calling circuits “hardware” and, more generally, that we broaden our concept of what constitutes “software” ... Developing modern embedded software capable of executing on multiprocessor and FPGA platforms requires expertise not just in temporally oriented modeling (W comes after X) like writing sequential code but also in spatially oriented modeling (Y connects with Z) like creating circuits.”