## Slide 1: Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches
Gennady Pekhimenko
Vivek Seshadri
Onur Mutlu , Todd C. Mowry
Phillip B. Gibbons*
Michael A. Kozuch*
*
Notes: This is a joint work between CMU and Intel Labs Pittsburgh.

## Slide 2: Executive Summary
Off-chip memory latency is high
  Large caches can help, but at significant cost
Compressing data in cache enables larger cache at low cost
Problem: Decompression is on the execution critical path
Goal: Design a new compression scheme that has
1. low decompression latency, 2. low cost, 3. high compression ratio
Observation: Many cache lines have low dynamic range data
Key Idea: Encode cachelines as a base + multiple differences
Solution: Base-Delta-Immediate compression with low decompression latency and high compression ratio
  Outperforms three state-of-the-art compression mechanisms

## Slide 3: Motivation for Cache Compression
Significant redundancy in data:
0x00000000
How can we exploit this redundancy?
  Cache compression helps
  Provides effect of a larger cache without making it physically larger
0x0000000B
0x00000003
0x00000004
…

## Slide 4: Background on Cache Compression
Key requirements:
  Fast (low decompression latency)
  Simple (avoid complex hardware changes)
  Effective (good compression ratio)
CPU
L2 Cache
Uncompressed
Compressed
Decompression
Uncompressed
L1 Cache
Hit

## Slide 5: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 

## Slide 6: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 

## Slide 7: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 

## Slide 8: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 
Our proposal: BΔI |  |  | 

## Slide 9: Outline
Motivation & Background
Key Idea & Our Mechanism
Evaluation
Conclusion

## Slide 10: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region

## Slide 11: How Common Are These Patterns?
Chart: Cache Coverage (%)
| libquantum | lbm | mcf | tpch17 | sjeng | omnetpp | tpch2 | sphinx3 | xalancbmk | bzip2 | tpch6 | leslie3d | apache | gromacs | astar | gobmk | soplex | gcc | hmmer | wrf | h264ref | zeusmp | cactusADM | GemsFDTD | Average
Zero | 1.2e-05 | 7e-06 | 0.008911 | 0.033323 | 0.032362 | 2.7e-05 | 0.065765 | 0.022031 | 0.000272 | 0.000176 | 0.12314 | 0.16955 | 0.072498 | 0.065675 | 0.016314 | 0.34373 | 0.26863 | 0.30068 | 0.003261 | 0.81434 | 0.00837 | 0.83736 | 0.66632 | 0.99428 | 0.20196
Repeated Values | 0.0001 | 6.5e-05 | 0.0001 | 0.000508 | 0.000146 | 0.0001 | 0.000529 | 0.008812 | 2e-06 | 0.036901 | 0.002005 | 0.095993 | 0.005072 | 0.010873 | 0.005914 | 0.020917 | 0.29969 | 0.038812 | 0.031345 | 0.083856 | 0.006414 | 0.13684 | 0.32178 | 0.001628 | 0.046184
Other Patterns | 0.000177 | 0.000138 | 0.060209 | 0.045394 | 0.070763 | 0.11701 | 0.075432 | 0.1168 | 0.21336 | 0.18863 | 0.12998 | 0.016265 | 0.23912 | 0.24082 | 0.42076 | 0.086109 | 0.18536 | 0.45647 | 0.84697 | 0.017818 | 0.91843 | 0.000306 | 0.000699 | 0.000345 | 0.18531
SPEC2006, databases, web workloads, 2MB L2 cache
“Other Patterns” include Narrow Values
  43% of the cache lines belong to key patterns

## Slide 12: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region
  Low Dynamic Range:
  Differences between values are significantly smaller than the values themselves

## Slide 13: Key Idea: Base+Delta (B+Δ) Encoding
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
4 bytes
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Fast Decompression: vector addition
   Simple Hardware:
  arithmetic and comparison
   Effective: good compression ratio

## Slide 14: Can We Do Better?
Uncompressible cache line (with a single base):
Key idea:
Use more bases, e.g., two instead of one
Pro:
  More cache lines can be compressed
Cons:
  Unclear how to find these bases efficiently
  Higher overhead (due to additional bases)
0x00000000
0x09A40178
0x0000000B
0x09A4A838
…

## Slide 15: B+Δ with Multiple Arbitrary Bases
Chart: Compression Ratio
| GeoMean
1 | 1.3961
2 | 1.5113
3 | 1.4982
4 | 1.4326
8 | 1.3118
10 | 1.2742
16 | 1.2242
   2 bases – the best option based on evaluations

## Slide 16: How to Find Two Bases Efficiently?
  First base - first element in the cache line
  Second base - implicit base of 0
Advantages over 2 arbitrary bases:
  Better compression ratio
  Simpler compression logic
   Base+Delta part
   Immediate part
  Base-Delta-Immediate (BΔI) Compression

## Slide 17: B+Δ (with two arbitrary bases) vs. BΔI
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
B+Δ (2 bases) | 1.0625 | 1.0125 | 1.0254 | 1.1979 | 1.1332 | 1.375 | 1.7477 | 1.5346 | 1.3347 | 1.2446 | 1.5238 | 1.447 | 1.2608 | 1.4753 | 1.7447 | 1.3954 | 1.9793 | 1.7868 | 1.9739 | 1.9919 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5113
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
  Average compression ratio is close, but BΔI is simpler

## Slide 18: BΔI Implementation
Decompressor Design
  Low latency
Compressor Design
  Low cost and complexity
BΔI Cache Organization
  Modest complexity

## Slide 19: BΔI Decompressor Design
Δ0
B0
Δ1
Δ2
Δ3
Compressed Cache Line
V0
V1
V2
V3
+
+
Uncompressed Cache Line
+
+
B0
Δ0
B0
B0
B0
B0
Δ1
Δ2
Δ3
V0
V1
V2
V3
  Vector addition

## Slide 20: BΔI Compressor Design
32-byte Uncompressed Cache Line
8-byte B0
1-byte Δ
CU
8-byte B0
2-byte Δ
CU
8-byte B0
4-byte Δ
CU
4-byte B0
1-byte Δ
CU
4-byte B0
2-byte Δ
CU
2-byte B0
1-byte Δ
CU
Zero
CU
Rep.
Values
CU
Compression Selection Logic (based on compr. size)
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
Compression Flag & Compressed Cache Line
CFlag &
CCL
Compressed Cache Line

## Slide 21: BΔI Compression Unit: 8-byte B0 1-byte Δ
32-byte Uncompressed Cache Line
V0
V1
V2
V3
8 bytes
-
-
-
-
B0=
V0
V0
B0
B0
B0
B0
V0
V1
V2
V3
Δ0
Δ1
Δ2
Δ3
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Is every element within 1-byte range?
Δ0
B0
Δ1
Δ2
Δ3
B0
Δ0
Δ1
Δ2
Δ3
Yes
No

## Slide 22: BΔI Cache Organization
Tag0
Tag1
…
…
…
…
Tag Storage:
Set0
Set1
Way0
Way1
Data0
…
…
Set0
Set1
Way0
Way1
…
Data1
…
32 bytes
Data Storage:
Conventional 2-way cache with 32-byte cache lines
BΔI: 4-way cache with 8-byte segmented data
Tag0
Tag1
…
…
…
…
Tag Storage:
Way0
Way1
Way2
Way3
…
…
Tag2
Tag3
…
…
Set0
Set1
Twice as many tags
C - Compr. encoding bits
C
Set0
Set1
…
…
…
…
…
…
…
…
S0
S0
S1
S2
S3
S4
S5
S6
S7
…
…
…
…
…
…
…
…
8 bytes
Tags map to multiple adjacent segments
2.3% overhead for 2 MB cache

## Slide 23: Qualitative Comparison with Prior Work
Zero-based designs
  ZCA [Dusser+, ICS’09]: zero-content augmented cache
  ZVC [Islam+, PACT’09]: zero-value cancelling
  Limited applicability (only zero values)
FVC [Yang+, MICRO’00]: frequent value compression
  High decompression latency and complexity
Pattern-based compression designs
  FPC [Alameldeen+, ISCA’04]: frequent pattern compression
    High decompression latency (5 cycles) and complexity
  C-pack [Chen+, T-VLSI Systems’10]: practical implementation of FPC-like algorithm
    High decompression latency (8 cycles)

## Slide 24: Outline
Motivation & Background
Key Idea & Our Mechanism
Evaluation
Conclusion

## Slide 25: Methodology
Simulator
  x86 event-driven simulator based on Simics [Magnusson+, Computer’02]
Workloads
  SPEC2006 benchmarks, TPC, Apache web server
  1 – 4 core simulations for 1 billion representative instructions
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  4GHz, x86 in-order core, 512kB - 16MB L2, simple memory model (300-cycle latency for row-misses)

## Slide 26: Compression Ratio: BΔI vs. Prior Work
BΔI achieves the highest compression ratio
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
ZCA | 1 | 1.0125 | 1.0002 | 1.0055 | 1.0288 | 1 | 1.1561 | 1.0914 | 1.0241 | 1 | 1.0005 | 1.1898 | 1 | 1.1083 | 1.0549 | 1 | 1.0013 | 1.2794 | 1.9738 | 1.5235 | 1.5406 | 1.801 | 1.9951 | 1.9966 | 1.2005
FVC | 1.0297 | 1.0125 | 1.0012 | 1.017 | 1.1457 | 1.4988 | 1.1857 | 1.1438 | 1.4157 | 1.3573 | 1.0143 | 1.4596 | 1.3574 | 1.3745 | 1.1968 | 1.3874 | 1.9381 | 1.7894 | 1.9738 | 1.9859 | 1.9598 | 1.9947 | 1.995 | 1.9966 | 1.4212
FPC | 1.004 | 1.0125 | 1.0225 | 1.0568 | 1.2307 | 1.3121 | 1.1774 | 1.4064 | 1.4705 | 1.5235 | 1.5442 | 1.5994 | 1.5763 | 1.7269 | 1.2651 | 1.6749 | 1.9072 | 1.9167 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5149
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
1.53
SPEC2006, databases, web workloads, 2MB L2

## Slide 27: Single-Core: IPC and MPKI
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 1.0859 | 1.1498 | 1.1819 | 1.2753 | 1.3788
BΔI | 1.0817 | 1.1425 | 1.2085 | 1.2401 | 1.346 | 1.4285
8.1%
5.2%
5.1%
4.9%
5.6%
3.6%
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 0.819 | 0.59143 | 0.46593 | 0.37544 | 0.27527
BΔI | 0.84292 | 0.62368 | 0.466 | 0.40552 | 0.30364 | 0.23666
16%
24%
21%
13%
19%
14%
BΔI achieves the performance of a 2X-size cache
Performance improves due to the decrease in MPKI

## Slide 28: Multi-Core Workloads
Application classification based on
  Compressibility: effective cache size increase
  (Low Compr. (LC) < 1.40, High Compr. (HC) >= 1.40)
  Sensitivity: performance gain with more cache
  (Low Sens. (LS) < 1.10, High Sens. (HS) >= 1.10; 512kB -> 2MB)
Three classes of applications:
  LCLS, HCLS, HCHS, no LCHS applications
For 2-core - random mixes of each possible class pairs (20 each, 120 total workloads)

## Slide 29: Multi-Core: Weighted Speedup
BΔI performance improvement is the highest (9.5%)
Chart: Normalized Weighted Speedup
| LCLS - LCLS | LCLS - HCLS | HCLS - HCLS | LCLS - HCHS | HCLS - HCHS | HCHS - HCHS | Low Sensitivity | High Sensitivity | GeoMean
ZCA | 1.0268 | 1.0154 | 1.0259 | 1.0182 | 1.1193 | 1.01 | 1.0353
FVC | 1.0277 | 1.0179 | 1.0345 | 1.0727 | 1.1468 | 1.08 | 1.0624
FPC | 1.0312 | 1.0197 | 1.0276 | 1.1 | 1.1495 | 1.176 | 1.0822
BΔI | 1.0446 | 1.0342 | 1.0431 | 1.1091 | 1.1651 | 1.18 | 1.0944
If at least one application is sensitive, then the performance improves

## Slide 30: Other Results in Paper
IPC comparison against upper bounds
  BΔI almost achieves performance of the 2X-size cache
Sensitivity study of having more than 2X tags
  Up to 1.98 average compression ratio
Effect on bandwidth consumption
  2.31X decrease on average
Detailed quantitative comparison with prior work
Cost analysis of the proposed changes
  2.3% L2 cache area increase

## Slide 31: Conclusion
A new Base-Delta-Immediate compression mechanism
Key insight: many cache lines can be efficiently represented using base + delta encoding
Key properties:
  Low latency decompression
  Simple hardware implementation
  High compression ratio with high coverage
Improves cache hit ratio and performance of both single-core and multi-core workloads
  Outperforms state-of-the-art cache compression techniques: FVC and FPC

## Slide 32: Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches
Gennady Pekhimenko,
Vivek Seshadri ,
Onur Mutlu , Todd C. Mowry
Phillip B. Gibbons*,
Michael A. Kozuch*
*
Notes: This is a joint work between CMU and Intel Labs Pittsburgh.

## Slide 33: Backup Slides

## Slide 34: B+Δ: Compression Ratio
  Good average compression ratio (1.40)
Chart: Compression Ratio
| libquantum | lbm | wrf | hmmer | sphinx3 | tpch17 | mcf | omnetpp | sjeng | xalancbmk | tpch2 | leslie3d | apache | astar | gromacs | h264ref | bzip2 | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
B+Δ | 1 | 1.0013 | 1.0125 | 1.0256 | 1.0872 | 1.1038 | 1.1209 | 1.1343 | 1.1644 | 1.2387 | 1.3785 | 1.3894 | 1.407 | 1.4563 | 1.4616 | 1.5287 | 1.5394 | 1.564 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.3961
  But some benchmarks have low compression ratio
SPEC2006, databases, web workloads, L2 2MB cache

## Slide 35: Single-Core: Effect on Cache Capacity
BΔI achieves performance close to the upper bound
Chart: Normalized IPC
| libquantum | sjeng | wrf | GemsFDTD | cactusADM | gcc | hmmer | tpch6 | lbm | zeusmp | leslie3d | gobmk | h264ref | sphinx3 | apache | gromacs | tpch17 | tpch2 | omnetpp | mcf | xalancbmk | soplex | bzip2 | astar | GeoMean
512kB-2way | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
512kB-4way-BΔI | 1.0008 | 1.0066 | 1.0243 | 1.046 | 1.0208 | 1.0191 | 1.0522 | 1.0679 | 1.0006 | 1.0312 | 1.0655 | 1.1164 | 1.0416 | 1.0344 | 1.117 | 1.1266 | 1.2654 | 1.3029 | 1.0867 | 1.0632 | 1.0353 | 1.1152 | 1.2419 | 1.3193 | 1.088
1MB-4way | 1.0033 | 1.0092 | 1.0248 | 1.05 | 1.0234 | 1.0207 | 1.0679 | 1.0701 | 1.0454 | 1.0316 | 1.0829 | 1.1189 | 1.0436 | 1.0759 | 1.1206 | 1.2059 | 1.2802 | 1.3067 | 1.0986 | 1.1449 | 1.0541 | 1.1167 | 1.3107 | 1.3647 | 1.1068
1MB-8way-BΔI | 1.004 | 1.0128 | 1.0347 | 1.0581 | 1.0319 | 1.0414 | 1.0808 | 1.0969 | 1.0454 | 1.0811 | 1.115 | 1.1401 | 1.0855 | 1.084 | 1.1952 | 1.2504 | 1.3479 | 1.4208 | 1.2023 | 1.2184 | 1.1093 | 1.3002 | 1.5808 | 2.006 | 1.1729
2MB-8way | 1.0063 | 1.0145 | 1.0347 | 1.0581 | 1.0319 | 1.0414 | 1.0868 | 1.0976 | 1.0508 | 1.0811 | 1.129 | 1.1402 | 1.0859 | 1.1289 | 1.1971 | 1.3043 | 1.381 | 1.4335 | 1.2521 | 1.3004 | 1.146 | 1.3025 | 1.7519 | 2.093 | 1.1942
2MB-16way-BΔI | 1.0129 | 1.0191 | 1.0357 | 1.063 | 1.0708 | 1.0728 | 1.0968 | 1.1091 | 1.0507 | 1.1405 | 1.1333 | 1.1624 | 1.1841 | 1.1335 | 1.2491 | 1.3225 | 1.3828 | 1.4524 | 1.4006 | 1.4208 | 1.3591 | 1.6612 | 1.9382 | 2.6246 | 1.2597
4MB-16way | 1.019 | 1.0219 | 1.036 | 1.0672 | 1.0737 | 1.074 | 1.1024 | 1.1124 | 1.1202 | 1.1411 | 1.1454 | 1.1647 | 1.1883 | 1.2002 | 1.2623 | 1.3644 | 1.4192 | 1.4774 | 1.5011 | 1.559 | 1.5671 | 1.6669 | 1.9947 | 2.7934 | 1.2941
1.3%
1.7%
2.3%
Fixed L2 cache latency

## Slide 36: Multiprogrammed Workloads - I

## Slide 37: Cache Compression Flow
CPU
L1 Data Cache
Uncompressed
L2 Cache
Compressed
Memory
Uncompressed
Hit L1
Miss
Miss
Hit L2
Decompress
Compress
Writeback
Decompress
Writeback
Compress

## Slide 38: Example of Base+Delta Compression
Narrow values (taken from h264ref):