## Slide 1: CSC 2224: Parallel Computer Architecture and Programming Memory Hierarchy & Caches
Prof. Gennady Pekhimenko
University of Toronto
Fall 2018
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU and ETH

## Slide 2: Reviews: Cache Compression
Review:
  Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012

## Slide 3: Project Proposal Deadline
Deadline is on October 2nd
Send emails with your proposals (PDFs) to csc2224arch@gmail.com

## Slide 4: Memory (Programmer’s View)

## Slide 5: Virtual vs. Physical Memory
Programmer sees virtual memory
  Can assume the memory is “infinite”
Reality: Physical memory size is much smaller than what the programmer assumes
The system (system software + hardware, cooperatively) maps virtual memory addresses to physical memory
  The system automatically manages the physical memory space transparently to the programmer
+ Programmer does not need to know the physical size of memory nor manage it  A small physical memory can appear as a huge one to the programmer  Life is easier for the programmer
-- More complex system software and architecture
A classic example of the programmer/(micro)architect tradeoff

## Slide 6: (Physical) Memory System
You need a larger level of storage to manage a small amount of physical memory automatically
   Physical memory has a backing store: disk
We will first start with the physical memory system
For now, ignore the virtual  physical indirection
We will get back to it when the needs of virtual memory start complicating the design of physical memory…

## Slide 7: Idealism
Instruction
Supply
Pipeline
(Instruction
execution)
Data
Supply
- Zero latency access
- Infinite capacity
- Zero cost
- Perfect control flow
No pipeline stalls
Perfect data flow
(reg/memory dependencies)
Zero-cycle interconnect
(operand communication)
Enough functional units
Zero latency compute
Zero latency access
Infinite capacity
- Infinite bandwidth
Zero cost

## Slide 8: The Memory Hierarchy

## Slide 9: Memory in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 10: Ideal Memory
Zero access time (latency)
Infinite capacity
Zero cost
Infinite bandwidth (to support multiple accesses in parallel)

## Slide 11: The Problem
Ideal memory’s requirements oppose each other
Bigger is slower
  Bigger  Takes longer to determine the location
Faster is more expensive
  Memory technology: SRAM vs. DRAM vs. Disk vs. Tape
Higher bandwidth is more expensive
  Need more banks, more ports, higher frequency, or faster technology

## Slide 12: Memory Technology: DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
row enable
_bitline

## Slide 13: Memory Technology: SRAM
Static random access memory
Two cross coupled inverters store a single bit
  Feedback path enables the stored value to persist in the “cell”
  4 transistors for storage
  2 transistors for access
row select
bitline
_bitline

## Slide 14: Memory Bank Organization and Operation
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 15: SRAM (Static Random Access Memory)
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m diff pairs
2n
n
m
1
row select
bitline
_bitline
n+m
Read Sequence
  1. address decode
  2. drive row select
  3. selected bit-cells drive bitlines
  (entire row is read together)
  4. differential sensing and column select
  (data is ready)
  5. precharge all bitlines
  (for next read or write)
Access latency dominated by steps 2 and 3
Cycling time dominated by steps 2, 3 and 5
  step 2 proportional to 2m
  step 3 and 5 proportional to 2n

## Slide 16: DRAM (Dynamic Random Access Memory)
row enable
_bitline
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m
2n
n
m
1
RAS
CAS
A DRAM die comprises
of multiple such arrays
Bits stored as charges on node capacitance (non-restorative)
  bit cell loses charge when read
  bit cell loses charge over time
Read Sequence
  1~3 same as SRAM
  4. a “flip-flopping” sense amp amplifies and regenerates the bitline, data bit is mux’ed out
  5. precharge all bitlines
Destructive reads
Charge loss over time
Refresh: A DRAM controller must periodically read each row within the allowed refresh time (10s of ms) such that charge is restored

## Slide 17: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 18: The Problem
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 10$ per Megabyte
  DRAM, < 1$ per Megabyte
  Hard Disk < 1$ per Gigabyte
  These sample values (circa ~2011) scale with time
Other technologies have their place as well
  Flash memory, PC-RAM, MRAM, RRAM (not mature yet)

## Slide 19: Why Memory Hierarchy?
We want both fast and large
But we cannot achieve both with a single level of memory
Idea: Have multiple levels of storage (progressively bigger and slower as the levels are farther from the processor) and ensure most of the data the processor needs is kept in the fast(er) level(s)

## Slide 20: The Memory Hierarchy
fast
small
big but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte

## Slide 21: Memory Hierarchy
Fundamental tradeoff
  Fast memory: small
  Large memory: slow
Idea: Memory hierarchy
Latency, cost, size,
bandwidth
CPU
Main
Memory
(DRAM)
RF
Cache
Hard Disk

## Slide 22: Locality
One’s recent past is a very good predictor of his/her near future.
Temporal Locality: If you just did something, it is very likely that you will do the same thing again soon
  since you are here today, there is a good chance you will be here again and again regularly
Spatial Locality: If you did something, it is very likely you will do something similar/related (in space)
  every time I find you in this room, you are probably sitting close to the same people

## Slide 23: Memory Locality
A “typical” program has a lot of locality in memory references
  typical programs are composed of “loops”
Temporal: A program tends to reference the same memory location many times and all within a small window of time
Spatial: A program tends to reference a cluster of memory locations at a time
  most notable examples:
    1. instruction memory references
    2. array/data structure references

## Slide 24: Caching Basics: Exploit Temporal Locality
Idea: Store recently accessed data in automatically managed fast memory (called cache)
Anticipation: the data will be accessed again soon
Temporal locality principle
  Recently accessed data will be again accessed in the near future
  This is what Maurice Wilkes had in mind:
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
    “The use is discussed of a fast core memory of, say 32000 words as a slave to a slower core memory of, say, one million words in such a way that in practical cases the effective access time is nearer that of the fast memory than that of the slow memory.”

## Slide 25: Caching Basics: Exploit Spatial Locality
Idea: Store addresses adjacent to the recently accessed one in automatically managed fast memory
  Logically divide memory into equal size blocks
  Fetch to cache the accessed block in its entirety
Anticipation: nearby data will be accessed soon
Spatial locality principle
  Nearby data in memory will be accessed in the near future
    E.g., sequential instruction access, array traversal
  This is what IBM 360/85 implemented
    16 Kbyte cache with 64 byte blocks
    Liptay, “Structural aspects of the System/360 Model 85 II: the cache,” IBM Systems Journal, 1968.

## Slide 26: The Bookshelf Analogy
Book in your hand
Desk
Bookshelf
Boxes at home
Boxes in storage
Recently-used books tend to stay on desk
  Comp Arch books, books for classes you are currently taking
  Until the desk gets full
Adjacent books in the shelf needed around the same time
  If I have organized/categorized my books well in the shelf

## Slide 27: Caching in a Pipelined Design
The cache needs to be tightly integrated into the pipeline
  Ideally, access in 1-cycle so that dependent operations do not stall
High frequency pipeline  Cannot make the cache large
  But, we want a large cache AND a pipelined design
Idea: Cache hierarchy
CPU
Main
Memory
(DRAM)
RF
Level1
Cache
Level 2
Cache

## Slide 28: A Note on Manual vs. Automatic Management
Manual: Programmer manages data movement across levels
  -- too painful for programmers on substantial programs
  “core” vs “drum” memory in the 50’s
  still done in some embedded processors (on-chip scratch pad SRAM in lieu of a cache) and GPUs (called “shared memory”)
Automatic: Hardware manages data movement across levels, transparently to the programmer
  ++ programmer’s life is easier
  the average programmer doesn’t need to know about it
    You don’t need to know how big the cache is and how it works to write a “correct” program! (What if you want a “fast” program?)

## Slide 29: A Modern Memory Hierarchy
Register File
32 words, sub-nsec
L1 cache
~32 KB, ~nsec
L2 cache
512 KB ~ 1MB, many nsec
L3 cache,
.....
Main memory (DRAM),
GB, ~100 nsec
Swap Disk
100 GB, ~10 msec
manual/compiler
register spilling
automatic
demand
paging
Automatic
HW cache
management
Memory
Abstraction

## Slide 30: Hierarchical Latency Analysis
For a given memory hierarchy level i it has a technology-intrinsic access time of ti, The perceived access time Ti is longer than ti
Except for the outer-most hierarchy, when looking for a given address there is
  a chance (hit-rate hi) you “hit” and access time is ti
  a chance (miss-rate mi) you “miss” and access time ti +Ti+1
  hi + mi = 1
Thus
Ti = hi·ti + mi·(ti + Ti+1)
Ti = ti + mi ·Ti+1
hi and mi are defined to be the hit-rate
and miss-rate of just the references that missed at Li-1

## Slide 31: Hierarchy Design Considerations
Recursive latency equation
Ti = ti + mi ·Ti+1
The goal: achieve desired T1 within allowed cost
Ti  ti is desirable
Keep mi low
  increasing capacity Ci lowers mi, but beware of increasing ti
  lower mi by smarter management (replacement::anticipate what you don’t need, prefetching::anticipate what you will need)
Keep Ti+1 low
  faster lower hierarchies, but beware of increasing cost
  introduce intermediate hierarchies as a compromise

## Slide 32
90nm P4, 3.6 GHz
L1 D-cache
  C1 = 16K
  t1 = 4 cyc int / 9 cycle fp
L2 D-cache
  C2 =1024 KB
  t2 = 18 cyc int / 18 cyc fp
Main memory
  t3 = ~ 50ns or 180 cyc
Notice
  best case latency is not 1
  worst case access latencies are into 500+ cycles
if m1=0.1, m2=0.1
T1=7.6, T2=36
if m1=0.01, m2=0.01
T1=4.2, T2=19.8
if m1=0.05, m2=0.01
T1=5.00, T2=19.8
if m1=0.01, m2=0.50
T1=5.08, T2=108
Intel Pentium 4 Example

## Slide 33: Cache Basics and Operation

## Slide 34: Cache
Generically, any structure that “memoizes” frequently used results to avoid repeating the long-latency operations required to reproduce the results from scratch, e.g. a web cache
Most commonly in the on-die context: an automatically-managed memory hierarchy based on SRAM
  memoize in SRAM the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 35: Caching Basics
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    Maybe have to kick something else out to do it
Some important cache design decisions
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 36: Cache Abstraction and Metrics
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Average memory access time (AMAT)
= ( hit-rate * hit-latency ) + ( miss-rate * miss-latency )
Aside: Can reducing AMAT reduce performance?
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 37: A Basic Hardware Cache Design
We will start with a basic hardware cache design
Then, we will examine a multitude of ideas to make it better

## Slide 38: Blocks and Addressing the Cache
Memory is logically divided into fixed-size blocks
Each block maps to a location in the cache, determined by the index bits in the address
  used to index into the tag and data stores
Cache access:
  1) index into the tag and data stores with index bits in address
  2) check valid bit in tag store
  3) compare tag bits in address with the stored tag in tag store
If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block
8-bit address
tag
index
byte in block
3 bits
3 bits
2b

## Slide 39: Direct-Mapped Cache: Placement and Access
Assume byte-addressable memory: 256 bytes, 8-byte blocks  32 blocks
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location: Cause conflict misses
Tag store
Data store
Address
tag
index
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data

## Slide 40: Direct-Mapped Caches
Direct-mapped cache: Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses

## Slide 41: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 42: Higher Associativity
4-way
+ Likelihood of conflict misses even lower
-- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 43: Full Associativity
Fully associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 44: Associativity (and Tradeoffs)
Degree of associativity: How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time
  (hit latency and data access latency)
  -- More expensive hardware
  (more comparators)
Diminishing returns from
higher associativity
associativity
hit rate

## Slide 45: Issues in Set-Associative Caches
Think of each block in a set having a “priority”
  Indicating how important it is to keep the block in the cache
Key issue: How do you determine/adjust block priorities?
There are three key decisions in a set:
  Insertion, promotion, eviction (replacement)
Insertion: What happens to priorities on a cache fill?
  Where to insert the incoming block, whether or not to insert the block
Promotion: What happens to priorities on a cache hit?
  Whether and how to change block priority
Eviction/replacement: What happens to priorities on a cache miss?
  Which block to evict and how to adjust priorities

## Slide 46: Eviction/Replacement Policy
Which block in the set to replace on a cache miss?
  Any invalid block first
  If all are valid, consult the replacement policy
    Random
    FIFO
    Least recently used (how to implement?)
    Not most recently used
    Least frequently used?
    Least costly to re-fetch?
      Why would memory accesses have different cost?
    Hybrid replacement policies
    Optimal replacement policy?

## Slide 47: Implementing LRU
Idea: Evict the least recently accessed block
Problem: Need to keep track of access ordering of blocks
Question: 2-way set associative cache:
  What do you need to implement LRU perfectly?
Question: 4-way set associative cache:
  What do you need to implement LRU perfectly?
  How many different orderings possible for the 4 blocks in the set?
  How many bits needed to encode the LRU order of a block?
  What is the logic needed to determine the LRU victim?

## Slide 48: Approximations of LRU
Most modern processors do not implement “true LRU” (also called “perfect LRU”) in highly-associative caches
Why?
  True LRU is complex
  LRU is an approximation to predict locality anyway (i.e., not the best possible cache management policy)
Examples:
  Not MRU (not most recently used)
  Hierarchical LRU: divide the N-way set into M “groups”, track the MRU group and the MRU way in each group
  Victim-NextVictim Replacement: Only keep track of the victim and the next victim

## Slide 49: Hierarchical LRU (not MRU)
Divide a set into multiple groups
Keep track of only the MRU group
Keep track of only the MRU block in each group
On replacement, select victim as:
  A not-MRU block in one of the not-MRU groups (randomly pick one of such blocks/groups)

## Slide 50: Cache Replacement Policy: LRU or Random
LRU vs. Random: Which one is better?
  Example: 4-way cache, cyclic references to A, B, C, D, E
    0% hit rate with LRU policy
Set thrashing: When the “program working set” in a set is larger than set associativity
  Random replacement policy is better when thrashing occurs
In practice:
  Depends on workload
  Average hit rate of LRU and Random are similar
Best of both Worlds: Hybrid of LRU and Random
  How to choose between the two? Set sampling
    See Qureshi et al., “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 51: What Is the Optimal?
Belady’s OPT
  Replace the block that is going to be referenced furthest in the future by the program
  Belady, “A study of replacement algorithms for a virtual-storage computer,” IBM Systems Journal, 1966.
  How do we implement this? Simulate?
Is this optimal for minimizing miss rate?
Is this optimal for minimizing execution time?
  No. Cache miss latency/cost varies from block to block!
  Two reasons: Remote vs. local caches and miss overlapping
  Qureshi et al. “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 52: What’s In A Tag Store Entry?
Valid bit
Tag
Replacement policy bits
Dirty bit?
  Write back vs. write through caches

## Slide 53: Handling Writes (I)
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More bandwidth intensive; no combining of writes

## Slide 54: Handling Writes (II)
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Can combine writes instead of writing each of them individually to next level
  + Simpler because write misses can be treated the same way as read misses
  -- Requires (?) transfer of the whole cache block
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 55: Handling Writes (III)
What if the processor writes to an entire block over a small amount of time?
Is there any need to bring the block into the cache from memory in the first place?
Ditto for a portion of the block, i.e., subblock
  E.g., 4 bytes out of 64 bytes

## Slide 56: Cache Performance

## Slide 57: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 58: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 59: Block Size
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each with V bit)
      Can improve “write” performance
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and
  bandwidth/energy:
  if spatial locality is not high
hit rate
block
size

## Slide 60: Large Blocks: Critical-Word and Subblocking
Large cache blocks can take a long time to fill into the cache
  fill cache line critical word first
  restart cache access before complete fill
Large cache blocks can waste bus bandwidth
  divide a block into subblocks
  associate separate valid bits for each subblock
  When is this useful?
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 61: Associativity
How many blocks can be present in the same index (i.e., set)?
Larger associativity
  lower miss rate (reduced conflicts)
  higher hit latency and area cost (plus diminishing returns)
Smaller associativity
  lower cost
  lower hit latency
    Especially important for L1 caches
Is power of 2 associativity required?
associativity
hit rate

## Slide 62: Classification of Cache Misses
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 63: How to Reduce Each Miss Type
Compulsory
  Caching cannot help
  Prefetching can
Conflict
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Better, randomized indexing
    Software hints?
Capacity
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set such that each “phase” fits in cache

## Slide 64: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost
The above three together affect performance

## Slide 65: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 66: Cheap Ways of Reducing Conflict Misses
Instead of building highly-associative caches:
Victim Caches
Hashed/randomized Index Functions
Pseudo Associativity
Skewed Associative Caches
…

## Slide 67: Victim Cache: Reducing Conflict Misses
Jouppi, “Improving Direct-Mapped Cache Performance by the Addition of a Small Fully-Associative Cache and Prefetch Buffers,” ISCA 1990.
Idea: Use a small fully-associative buffer (victim cache) to store recently evicted blocks
  + Can avoid ping ponging of cache blocks mapped to the same set (if two cache blocks continuously accessed in nearby time conflict with each other)
  -- Increases miss latency if accessed serially with L2; adds complexity
Direct Mapped Cache
Next Level
Cache
Victim cache

## Slide 68: Hashing and Pseudo-Associativity
Hashing: Use better “randomizing” index functions
  + can reduce conflict misses
    by distributing the accessed memory blocks more evenly to sets
    Example of conflicting accesses: strided access pattern where stride value equals number of sets in cache
  -- More complex to implement: can lengthen critical path
Pseudo-associativity (Poor Man’s associative cache)
  Serial lookup: On a miss, use a different index function and access cache again
  Given a direct-mapped array with K cache blocks
    Implement K/N sets
    Given address Addr, sequentially look up: {0,Addr[lg(K/N)-1: 0]}, {1,Addr[lg(K/N)-1: 0]}, … , {N-1,Addr[lg(K/N)-1: 0]}
  + Less complex than N-way; -- Longer cache hit/miss latency

## Slide 69: Skewed Associative Caches
Idea: Reduce conflict misses by using different index functions for each cache way
Seznec, “A Case for Two-Way Skewed-Associative Caches,” ISCA 1993.

## Slide 70: Skewed Associative Caches (I)
Basic 2-way associative cache structure
Way 0
Way 1
Tag Index Byte in Block
Same index function
for each way
=?
=?

## Slide 71: Skewed Associative Caches (II)
Skewed associative caches
  Each bank has a different index function
Way 0
Way 1
tag index byte in block
f0
same index
same set
same index
redistributed to
different sets
=?
=?

## Slide 72: Skewed Associative Caches (III)
Idea: Reduce conflict misses by using different index functions for each cache way
Benefit: indices are more randomized (memory blocks are better distributed across sets)
  Less likely two blocks have same index (esp. with strided access)
    Reduced conflict misses
Cost: additional latency of hash function

## Slide 73: Software Approaches for Higher Hit Rate
Restructuring data access patterns
Restructuring data layout
Loop interchange
Data structure separation/merging
Blocking
…

## Slide 74: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
What if multiple arrays? Unknown array size at compile time?
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 75: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
But, there are still self-conflicts in a block
  1. there can be conflicts among different arrays
  2. array sizes may be unknown at compile/programming time

## Slide 76: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1B nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* next;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 77: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* next;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 78: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 79: Miss Latency/Cost
What is miss latency or miss cost affected by?
  Where does the miss get serviced from?
    Local vs. remote memory
    What level of cache in the hierarchy?
    Row hit versus row miss in DRAM
    Queueing delays in the memory controller and the interconnect
    …
  How much does the miss stall the processor?
    Is it overlapped with other latencies?
    Is the data immediately needed?
    …

## Slide 80: Memory Level Parallelism (MLP)
Memory Level Parallelism (MLP) means generating and servicing multiple memory accesses in parallel [Glew’98]
Several techniques to improve MLP (e.g., out-of-order execution)
MLP varies. Some misses are isolated and some parallel
How does this affect cache replacement?
time
A
B
C
isolated miss
parallel miss
Notes: Processors are fast, Memory is slow. One way to bridge this gap is to service the memory accesses in parallel. If misses are serviced in parallel, the processor incurs only one long latency stall for all the parallel misses. The notion of generating and servicing off-chip accesses in parallel is termed as Memory Level Parallelism or MLP. Out of order processors improve MLP by continuing processing of independent instructions till the instruction window is full. If there is a miss during the processing of independent instructions, the miss is serviced concurrently with the stalling miss. There are several techniques, such as Runahead, CFP, to improve the MLP of out-of-order processors. MLP is not uniform for all cache misses. Some misses, such as pointer chasing loads, are typically serviced with low MLP while other misses, such as array accesses are serviced with high MLP. Current cache management techniques are not aware of this variation in MLP.

## Slide 81: Traditional Cache Replacement Policies
Traditional cache replacement policies try to reduce miss count
Implicit assumption: Reducing miss count reduces memory-related stall time
Misses with varying cost/MLP breaks this assumption!
Eliminating an isolated miss helps performance more than eliminating a parallel miss
Eliminating a higher-latency miss could help performance more than eliminating a lower-latency miss

## Slide 82: An Example
Misses to blocks P1, P2, P3, P4 can be parallel
Misses to blocks S1, S2, and S3 are isolated
Two replacement algorithms:
  Minimizes miss count (Belady’s OPT)
  Reduces isolated miss (MLP-Aware)
For a fully associative cache containing 4 blocks
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Notes: There are 11 memory access instructions in the loop. The accesses to cache blocks P1, P2, P3, P4 occur in the instruction window at same time. If these accesses result in more than 1 miss, then those misses are serviced in parallel. Conversely, misses to the S blocks are spaced far apart in time to misses to the S blocks are always serviced in isolation. This loop executes many time. I will analyze the cache behavior of this loop for two replacement algorithms. The first minimizes the number of misses. The well known Belady's opt algorithm provides a theoretical lower bound on the number of misses. The other is MLP-aware replacement, which tries to reduce the number of isolated miss.

## Slide 83: Fewest Misses = Best Performance
P3
P2
P1
P4
H H H H
M
H H H M
Hit/Miss
Misses=4 Stalls=4
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Time
stall
Belady’s OPT replacement
M
M
MLP-Aware replacement
Hit/Miss
P3
P2
S1
P4
P3
P2
P1
P4
P3
P2
S2
P4
P3
P2
S3
P4
S1
S2
S3
P1
P3
P2
S3
P4
S1
S2
S3
P4
H H H
S1
S2
S3
P4
H M M M
H M M M
Time
stall
Misses=6Stalls=2
Saved cycles
Cache
Notes: Although Belady’s OPT minimizes misses, it is impossible to implement it in a real processor as it requires knowledge of the future. We employ the commonly used LRU policy in our experiments

## Slide 84: MLP-Aware Cache Replacement
How do we incorporate MLP into replacement decisions?
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2006.

## Slide 85: Paper Review #1: Summary
Spent two paragraphs talking about the key insights of the paper, without covering the strengths.
Blaming the model for being over-simplified, but without making any concrete suggestions on how to further improve it. Authors already explain that including power consumption of memory subsystems only reduce the amount of speedup (because they eat away the allocated power budgets).
Making lots of claims in their reviews, but did not use any citations to support their claims.
Notes: Therefore, the authors' conclusion will not be affected unless people can show that some components (e.g. hardware accelerators that most people talk about) can greatly boost the system performance without introducing must power or area overhead.

## Slide 86: Paper Review #1: Grades Distribution
Chart: Grade Distribution
| 8 | 9 | 10
Grades (out of 10) | 5 | 6 | 5

## Slide 87: Review #3: Cache Compression
Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012

## Slide 88: CSC 2224: Parallel Computer Architecture and Programming Memory Hierarchy & Caches
Prof. Gennady Pekhimenko
University of Toronto
Fall 2018
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU and ETH