## Slide 1: CSC 2224: Parallel Computer Architecture and Programming Advanced Memory
Prof. Gennady Pekhimenko
University of Toronto
Fall 2018
The content of this lecture is adapted from the slides of
Vivek Seshadri, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU

## Slide 2: Review: Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 3: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 4: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processor chip?
  software and hardware interfaces?
  system software and languages?
  algorithms?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 5: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation
Dally, HiPEAC 2015

## Slide 6: Two Approaches to In-Memory Processing
1. Minimally change DRAM to enable simple yet powerful computation primitives
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory
  PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture (Ahn et al., ISCA 2015)
  A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing (Ahn et al., ISCA 2015)
  Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation (Hsieh et al., ICCD 2016)

## Slide 7: Approach 1: Minimally Changing DRAM
DRAM has great capability to perform bulk data movement and computation internally with small changes
  Can exploit internal bandwidth to move data
  Can exploit analog computation capability
  …
Examples: RowClone, In-DRAM AND/OR, Gather/Scatter DRAM
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)

## Slide 8: Starting Simple: Data Copy and Initialization
Bulk Data Copy
Bulk Data Initialization
src
dst
dst
val

## Slide 9: Bulk Data Copy and Initialization
Bulk Data Copy
Bulk Data Initialization
src
dst
dst
val

## Slide 10: Bulk Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 11: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 12: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 13: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 14: RowClone: Intra-Subarray
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst

## Slide 15: RowClone: Intra-Subarray (II)
r
c
r
o
w
s
s
t
o
w
d
r
Row Buffer
r
c
r
o
w
s
s
r
c
r
o
w
1. Activate src row (copy data from src to row buffer)
2. Activate dst row (disconnect src from row buffer, connect dst – copy data from row buffer to dst)

## Slide 16: RowClone: Inter-Bank
Memory Channel
Chip I/O
Bank
Shared internal bus
Overlap the latency of the read and the write
1.9X latency reduction, 3.2X energy reduction

## Slide 17: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)
0.01% area cost

## Slide 18: RowClone: Fast Row Initialization
0
0
0
0
0
0
0
0
0
0
0
0
Fix a row at Zero
(0.5% loss in capacity)

## Slide 19: RowClone: Bulk Initialization
Initialization with arbitrary data
  Initialize one row
  Copy the data to other rows
Zero initialization (most common)
  Reserve a row in each subarray (always zero)
  Copy data from reserved row (FPM mode)
  6.0X lower latency, 41.5X lower DRAM energy
  0.2% loss in capacity

## Slide 20: RowClone: Latency & Energy Benefits
Chart: Latency Reduction
| Intra-Subarray | Inter-Bank | Inter-Subarray | Intra-Subarray | Copy | Zero
Latency | 11.62 | 1.93 | 0.99 | 6.06
Chart: Energy Reduction
| Intra-Subarray | Inter-Bank | Inter-Subarray | Intra-Subarray | Copy | Zero
Energy | 74.4 | 3.2 | 1.5 | 41.5
11.6x
1.9x
6.0x
1.0x
74.4x
3.2x
1.5x
41.5x
Very low cost: 0.01% increase in die area

## Slide 21: Copy and Initialization in Workloads
Chart: Fraction of Memory Traffic
| bootup | compile | forkbench | mcached | mysql | shell
Read | 0.27394 | 0.34894 | 0.054305 | 0.45435 | 0.43893 | 0.099545
Write | 0.27185 | 0.33217 | 0.32279 | 0.45421 | 0.43769 | 0.089756
Copy | 0.21551 | 0 | 0.61578 | 0 | 0 | 0.42016
Zero | 0.23871 | 0.31889 | 0.007122 | 0.091442 | 0.12338 | 0.39054

## Slide 22: RowClone: Application Performance
Chart: % Compared to Baseline
| bootup | compile | forkbench | mcached | mysql | shell
IPC Improvement | 15 | 9 | 43 | 4 | 4 | 40
Energy Reduction | 40 | 32 | 60 | 15 | 17 | 67

## Slide 23: End-to-End System Design
DRAM (RowClone)
Microarchitecture
ISA
Operating System
Application
How to communicate occurrences of bulk copy/initialization across layers?
How to maximize latency and energy savings?
How to ensure cache coherence?
How to handle data reuse?

## Slide 24: Ambit In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology
Vivek Seshadri
Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, Todd C. Mowry

## Slide 25: Executive Summary
Problem: Bulk bitwise operations
  present in many applications, e.g., databases, search filters
  existing systems are memory bandwidth limited
Our Proposal: Ambit
  perform bulk bitwise operations completely inside DRAM
  bulk bitwise AND/OR: simultaneous activation of three rows
  bulk bitwise NOT: inverters already in sense amplifiers
  less than 1% area overhead over existing DRAM chips
Results compared to state-of-the-art baseline
  average across seven bulk bitwise operations
    32X performance improvement, 35X energy reduction
  3X-7X performance for real-world data-intensive applications
Notes: Talk about energy more
Explicitly state the performance improvement numbers
Range for throughput and energy?
Color more? Bulk AND/OR or NOT
Mechanism for NOT – fix the description. (use inverters already in sense amplifiers}?
Cost not coming out – mention the area cost

## Slide 26
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017
Bulk Bitwise Operations
BitWeaving
(database queries)
BitFunnel
(web search)
Bitmap indices
(database indexing)
Set operations
Encryption algorithms
DNA
sequence mapping
...
Notes: Add … (signify more applications)
Add references to some works (bitweaving, bitfunnel)

## Slide 27: Today, DRAM is just a storage device!
Processor
(CPU, GPU, FPGA)
DRAM
Channel
Write
Read
Throughput of bulk bitwise operations limited by available memory bandwidth

## Slide 28: Our Approach
Processor
(CPU, GPU, FPGA or PiM)
DRAM
Channel
Use analog operation of DRAM to perform bitwise operations completely inside memory!

## Slide 29: Inside a DRAM Chip
…
…
…
…
…
…
2D Array
of DRAM Cells
Sense amplifiers
8KB

## Slide 30: DRAM Cell Operation
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline

## Slide 31: DRAM Cell Operation
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
0
½ VDD
0
1
1
VDD
raise wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell regains charge
Sense Amp
deviation in bitline voltage
½ VDD
0
bitline

## Slide 32: Triple-Row Activation: Majority Function
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
activate
all three rows
0
1
0
1

## Slide 33: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C

## Slide 34: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C
Output = AB + BC + CA
= C (A OR B) +
~C (A AND B)
Control the value of C to perform bitwise OR or bitwise AND of A and B
38X improvement in raw throughput
44X reduction in energy consumption
for bulk bitwise AND/OR operations

## Slide 35: Bulk Bitwise AND/OR in DRAM
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Result = row A AND/OR row B
Statically reserve three designated rows t1, t2, and t3
MICRO 2013
Notes: * each copy operation takes only 80ns

## Slide 36: Bulk Bitwise AND/OR in DRAM
Copy RowClone data of row A to row t1
Copy RowClone data of row B to row t2
Initialize RowClone data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy RowClone data of row t1/t2/t3 to Result row
Result = row A AND/OR row B
Use RowClone to perform copy and initialization operations completely in DRAM!
Statically reserve three designated rows t1, t2, and t3
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Notes: Replace copies with rowclone once it is mentioned
Tie back to the concerns.
Reiterate speedup numbers
strike copy and make it rowclone

## Slide 37: Negation Using the Sense Amplifier
Sense Amp
bitline
bitline
enable
Can we copy the negated value from bitline to a DRAM cell?
Notes: Mark the enable signal to the sense amplifier
Before introducing the dual contact cell, state the key idea

## Slide 38: Negation Using the Sense Amplifier
Sense Amp
Dual Contact Cell
Regular wordline
Negation wordline
bitline
bitline
enable
Notes: Mark the enable signal to the sense amplifier
Before introducing the dual contact cell, state the key idea

## Slide 39: Negation Using the Sense Amplifier
enable sense amp
Sense Amp
½ VDD + δ
½ VDD
VDD
½ VDD
0
activate source
activate
negation wordline
bitline
bitline
source
Notes: Provide the result for NOT
Present all the results after this slide?

## Slide 40: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X

## Slide 41: Integrating Ambit with the System
PCIe device
  Similar to other accelerators (e.g., GPU)
System memory bus
  Ambit uses the same DRAM command/address interface
Pros and cons discussed in paper
(Section 5.4)
Notes: Make it simpler
Two approaches.

## Slide 42: Real-world Applications
Methodology (Gem5 simulator)
  Processor: x86, 4 GHz, out-of-order, 64-entry instruction queue
  L1 cache: 32 KB D-cache and 32 KB I-cache, LRU policy
  L2 cache: 2 MB, LRU policy
  Memory controller: FR-FCFS, 8 KB row size
  Main memory: DDR4-2400, 1 channel, 1 rank, 8 bank
Workloads
  Database bitmap indices
  BitWeaving –column scans using bulk bitwise operations
  Set operations – comparing bitvectors with red-black trees
Notes: Add color
Fix workloads – add set operation workload as well

## Slide 43: Bitmap Indices: Performance
Consistent reduction in execution time. 6X on average
Chart: Execution Time of Query
| w = 2 | w = 3 | w = 4 | w = 2 | w = 3 | w = 4 | n = 8m | n = 16m
Baseline | 27.92 | 41.72 | 54.84 | 58 | 85.44 | 112.92
Ambit | 5.16 | 6.88 | 8.64 | 10.2 | 13.68 | 17.16
5.4X
6.1X
6.3X
5.7X
6.2X
6.6X
Notes: Add color
Remove “week” and “users”

## Slide 44: Speedup offered by Ambit for BitWeaving
Chart: Number of bits for each column value
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
1m | 1.8 | 2.7 | 3.5 | 4.1 | 9.6 | 10.6 | 11 | 11.6
2m | 1.8 | 2.8 | 7.6 | 9 | 9.8 | 10.8 | 11.2 | 11.7
4m | 1.8 | 6 | 7.8 | 9.2 | 9.9 | 10.9 | 11.3 | 11.8
8m | 3.9 | 6.1 | 7.9 | 9.2 | 10 | 11 | 11.4 | 11.9
Number of rows in the database table
select count(*) where c1 < field < c2
12X
Notes: Reference bitweaving again
Add color
Fix the tag

## Slide 45
ROW HAMMER
FLIPPING BITS IN MEMORY WITHOUT ACCESSING THEM ISCA 2014

## Slide 46: DRAM CHIP
WORDLINE
ROW
LOW VOLTAGE
HIGH VOLTAGE
VICTIM
VICTIM
AGGRESSOR
READ DATA FROM HERE, GET ERRORS OVER THERE

## Slide 47
GOOGLE’S EXPLOIT
http://googleprojectzero.blogspot.com
“We learned about rowhammer from Yoongu Kim et al.”

## Slide 48
GOOGLE’S EXPLOIT
PROPOSED SOLUTIONS
OUR PROOF-OF-CONCEPT
EMPIRICAL ANALYSIS

## Slide 49: REAL SYSTEM
x86
DRAM
1. CACHE HITS
2. ROW HITS
MANY READS TO SAME ADDRESS
OPEN/CLOSE SAME ROW
≠

## Slide 50
LOOP:
mov (X), %reg
mov (Y), %reg
clflush (X)
clflush (Y)
jmp LOOP
11111111111
11111111111
11111111111
11111111111
Y
X
11111111111
1111
1111
11011110010
10111010111
x86 CPU
DRAM
http://www.github.com/CMU-SAFARI/rowhammer
MANY ERRORS!

## Slide 51
WHY DO THE ERRORS OCCUR?

## Slide 52
DRAM CELLS ARE LEAKY
CHARGE
‘1’
‘0’
64ms
0ms
REFRESH
NORMAL CELL
TIME

## Slide 53
DRAM CELLS ARE LEAKY
CHARGE
‘1’
‘0’
64ms
0ms
REFRESH
VICTIM CELL
AGGRESSOR
TIME

## Slide 54: ROOT CAUSE?
COUPLING
Electromagnetic
Tunneling
⇝
⇝
⇝
⇝
⇝
⇝
⇝
⇝
ACCELERATES CHARGE LOSS

## Slide 55: AS DRAM SCALES …
CELLS BECOME SMALLER Less tolerance to coupling effects
CELLS BECOME PLACED CLOSER Stronger coupling effects
COUPLING ERRORS MORE LIKELY

## Slide 56
ERRORS ARE RECENT Not found in pre-2010 chips
ERRORS ARE WIDESPREAD >80% of chips have errors Up to one error per ~1K cells

## Slide 57
Test Engine
DRAM Ctrl
PCIe
FPGA
PC
DRAM

## Slide 58
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 59: MOST MODULES AT RISK
A VENDOR
B VENDOR
C VENDOR
86%
83%
88%
(37/43)
(45/54)
(28/32)

## Slide 60
MANUFACTURE DATE
ERRORS PER 109 CELLS
MODULES:  A  B  C

## Slide 61: DISTURBING FACTS
AFFECTS ALL VENDORS Not an isolated incident Deeper issue in DRAM scaling
UNADDRESSED FOR YEARS Could impact systems in the field

## Slide 62
HOW TO PREVENT COUPLING ERRORS?
Previous Approaches
1. Make Better Chips: Expensive
2. Rigorous Testing: Takes Too Long

## Slide 63
ROW
MORE ERRORS
ROW
MORE ERRORS
FASTER ACCESS
ROW
ROW
FEWER ERRORS
ROW
FEWER ERRORS
FREQUENT REFRESH
ROW

## Slide 64
Faster ⟶ Slower
ONE MODULE:  A  B  C
ACCESS INTERVAL (ns)
TOTAL ERRORS
55ns
500ns

## Slide 65
Often ⟵ Seldom
ONE MODULE:  A  B  C
REFRESH INTERVAL (ms)
TOTAL ERRORS
64ms
11ms

## Slide 66: TWO NAIVE SOLUTIONS
LIMIT ACCESSES TO ROW Access Interval > 500ns
REFRESH ALL ROWS OFTEN Refresh Interval < 11ms
LARGE OVERHEAD: PERF, ENERGY, COMPLEXITY

## Slide 67: OUR SOLUTION: PARR
Probabilistic Adjacent Row Refresh
Do nothing
Refresh (=Open) adjacent rows
After closing any row ...
0.1%
99.9%

## Slide 68: PARR: CHANCE OF ERROR
NO REFRESHES IN N TRIALS Probability: 0.999N
N=128K FOR ERROR (64ms) Probability: 0.999128K = 10–56
STRONG RELIABILITY GUARANTEE

## Slide 69
STRONG RELIABILITY
LOW PERF OVERHEAD
9.4×10–14 Errors/Year
0.20% Slowdown
NO STORAGE OVERHEAD
0 Bytes

## Slide 70: RELATED WORK
Security Exploit (Seaborn@Google 2015)
Industry Analysis (Kang@SK Hynix 2014) “... will be [more] severe as technology shrinks down.”
Targeted Row Refresh (JEDEC 2014)
DRAM Testing (e.g., Van de Goor+ 1999)
Disturbance in Flash & Hard Disk

## Slide 71: Emerging Memory Technologies

## Slide 72: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 73: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 74: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 75: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 76: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 77: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 78: PCM Resistance → Value
Cell resistance
1
0
Cell value:

## Slide 79: Multi-Level Cell PCM
Multi-level cell: more than 1 bit per cell
  Further increases density by 2 to 4x [Lee+,ISCA'09]
But MLC-PCM also has drawbacks
  Higher latency and energy than single-level cell PCM

## Slide 80: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Bit 1
Bit 0

## Slide 81: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Less margin between values
→ need more precise sensing/modification of cell contents
→ higher latency/energy (~2x for reads and 4x for writes)

## Slide 82: Phase Change Memory Properties
Surveyed prototypes from 2003-2008 (ITRS, IEDM, VLSI, ISSCC)
Derived PCM parameters for F=90nm
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
Lee et al., “Phase Change Technology and the Future of Main Memory,” IEEE Micro Top Picks 2010.

## Slide 83: Phase Change Memory Properties: Latency
Latency comparable to, but slower than DRAM
Read Latency
  50ns: 4x DRAM, 10-3x NAND Flash
Write Latency
  150ns: 12x DRAM
Write Bandwidth
  5-10 MB/s: 0.1x DRAM, 1x NAND Flash
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 84: Phase Change Memory Properties
Dynamic Energy
  40 uA Rd, 150 uA Wr
  2-43x DRAM, 1x NAND Flash
Endurance
  Writes induce phase change at 650C
  Contacts degrade from thermal expansion/contraction
  108 writes per cell
  10-8x DRAM, 103x NAND Flash
Cell Size
  9-12F2 using BJT, single-level cells
  1.5x DRAM, 2-3x NAND (will scale with feature size, MLC)

## Slide 85: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 86: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 87: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 88: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 89: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 90: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 91: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 92: PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 93: Review #5
Flipping Bits in Memory Without Accessing Them Yoongu Kim et al., ISCA 2014

## Slide 94: Review #3 Summary
(1) BDI only works for integer type of data
(2) There is no report on power/energy consumption
(3) The authors only explored the use of BDI compression algorithm in the context of L2 (L3) cache, but in fact other contexts (e.g. GPU registers) are also possible.

## Slide 95: Review #3 Results

## Slide 96: CSC 2224: Parallel Computer Architecture and Programming Advanced Memory
Prof. Gennady Pekhimenko
University of Toronto
Fall 2018
The content of this lecture is adapted from the slides of
Vivek Seshadri, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU