## Slide 1: Handout # 18 Network Security
Professor Yashar Ganjali
Department of Computer Science
University of Toronto
yganjali@cs.toronto.edu
http://www.cs.toronto.edu/~yganjali
CSC 458/2209 – Computer Networks

## Slide 2: Announcements
Programming Assignment 2
  To be completed individually.
  Due: Friday, Nov. 29th at 5pm
  Submit on MarkUs (pa2.tar.gz)
No tutorials this week
Next week’s tutorial: PS2 review + PA2 Q&A

## Slide 3: Announcements
Final Exam
  Time: Tue. December 10th, 2019; 14:00-16:00
  Location:
    A-KE: GB304
    KI-OM: MS2170
    OU-ZZ: WY119
    CSC2209 A-Z: WY119
Please check the location online a few days before the exam

## Slide 4: Connectivity: Good vs. Evil
Network have improved significantly: in terms of bandwidth and latency
  Good
    We can communicate
    Exchange information
    Transfer data
    …
  Evil
    It’s easier to do harm
    Harmful code can propagate faster
    Information collection, violating privacy
    …

## Slide 5: Life Just Before Slammer
Notes: Does anyone not know what a worm is?

## Slide 6: Life Just After Slammer

## Slide 7: A Lesson in Economy
Slammer exploited connectionless UDP service, rather than connection-oriented TCP.
Entire worm fit in a single packet! (376 bytes)
  When scanning, worm could “fire and forget”.
  Stateless!
Worm infected 75,000+ hosts in 10 minutes (despite broken random number generator).
  At its peak, doubled every 8.5 seconds.
Progress limited by the Internet’s carrying capacity (= 55 million scans/sec)

## Slide 8: Why Security?
First victim at 12:45 am
By 1:15 am, transcontinental links starting to fail
300,000 access points downed in Portugal
All cell and Internet in Korea failed (27 million people)
5 root name servers were knocked offline
911 didn’t respond (Seattle)
Flights canceled
Notes: Entire worm was 376 bytes (single packet)

## Slide 9: Witty Worm
Notes: Start with a bit of motivation
Describe what a worm is… search online for animation

## Slide 10: Witty Worm – Cont’d
Attacks firewalls and security products (ISS)
First to use vulnerabilities in security software
ISS announced a vulnerability
  buffer overflow problem
  Attack in just one day!
Attack started from a small number of compromised machines
In 30 minutes 12,000 infected machines
  90 Gb/s of UDP traffic

## Slide 11: Detecting Attacks
How can we identify and measure attacks like Witty and Slammer?

## Slide 12: Network Telescope
Large piece of globally announced IP addresses
No legitimate hosts (almost)
Inbound traffic is almost always anomalous
1/256th of the all IPv4 space
  One packet in every 256 packets if unbiased random generators used.
Provides global view of the spread of Internet worms.
Question. Can this system identify attacks in real time?

## Slide 13: Today
Network Security Goals
Security vs. Internet Design
Attacks
Defenses

## Slide 14: Network Security Goals
Availability
  Everyone can reach all network resources all the time
Protection
  Protect users from interactions they don’t want
Authenticity
  Know who you are speaking with
Data Integrity
  Protect data en-route
Privacy
  Protect private data

## Slide 15: Today
Network Security Goals
Security vs. Internet Design
Attacks
Defenses

## Slide 16: Internet Design
Destination routing
Packet based (statistical multiplexing)
Global addressing (IP addresses)
Simple to join (as infrastructure)
Power in end hosts (end-to-end argument)
“Ad hoc” naming system

## Slide 17: Internet Design vs. Security
Destination routing
  Keeps forwarding tables small
  Simple to maintain forwarding tables
  How do we know where packets are coming from?
    Probably simple fix to spoofing, why isn’t it in place?
Packet based (statistical multiplexing)
Global addressing (IP addresses)
Simple to join (as infrastructure)
Power in end hosts (end-to-end argument)
“Ad hoc” naming system

## Slide 18: Internet Design vs. Security
Destination Routing
Packet Based (statistical multiplexing)
  Simple + Efficient
  Difficult resource bound per-communication
    How to keep someone from hogging? (remember, we can’t rely on source addresses)
Global Addressing (IP addresses)
Simple to join (as infrastructure)
Power in End Hosts (end-to-end argument)
“Ad hoc” naming system

## Slide 19: Internet Design vs. Security
Destination routing
Packet based (statistical multiplexing)
Global Addressing (IP addresses)
  Very democratic
  Even people who don’t necessarily want to be talked to
    “every psychopath is your next door neighbor” – Dan Geer
Simple to join (as infrastructure)
Power in end hosts (end-to-end argument)
“Ad hoc” naming system

## Slide 20: Internet Design vs. Security
Destination routing
Packet based (statistical multiplexing)
Global addressing (IP addresses)
Simple to join (as infrastructure)
  Very democratic
  Misbehaving routers can do very bad things
    No model of trust between routers
Power in End Hosts (end-to-end argument)
“Ad hoc” naming system

## Slide 21: Internet Design vs. Security
Destination routing
Packet based (statistical multiplexing)
Global addressing (IP addresses)
Simple to join (as infrastructure)
Power in end-hosts (end-to-end argument)
  Decouple hosts and infrastructure = innovation at the edge!
  Giving power to least trusted actors
    How to guarantee good behavior?
“Ad hoc” naming system

## Slide 22: Internet Design vs. Security
Packet Based (statistical multiplexing)
Destination Routing
Global Addressing (IP addresses)
Simple to join (as infrastructure)
Power in End Hosts (end-to-end argument)
“Ad hoc” naming system
  Seems to work OK
  Fate sharing with hierarchical system
  Off route = more trusted elements

## Slide 23: Today
Network Security Goals
Security vs. Internet Design
Attacks
  How attacks leverage these weaknesses in practice
    Denial of service
    Indirection
    Reconnaissance
Defenses

## Slide 24: DoS: Via Resource Exhaustion
Downlink bandwidth
Uplink bandwidth
Memory (e.g. TCP TCB exhaustion)
CPU
User-time
Notes: Note to Martin. For DDoS have a computer and enumerate all the resources that can be exhausted for a DDoS

## Slide 25: DoS: Via Resource Exhaustion
Uplink bandwidth
  Saturate uplink bandwidth using legitimate requests (e.g. download large image)
  Solution: use a CDN (Akamai)
  Solution: admission control at the server (not a network problem??)
CPU time similar to above
Victim Memory
  TCP connections require state, can try to exhaust
  E.g. SYN Flood (next few slides)
Notes: Main argument is that the end-host has all the information it needs to
Distinguish between fair and unfair use. It should implement its own admission control policy. This stops being a network problem at this point and more of an OS issue.
E-protests
(Question, what is cheaper? Cpu or bandwidth?)

## Slide 26: Who Is Responsible?
Can we rely on the attack victim to stop DoS attacks?
If not, who can do this?
How?
Which resource is cheaper?
  Bandwidth, or
  CPU

## Slide 27: TCP Handshake
C
S
SYNC
SYNS, ACKC
ACKS
Listening
Store data
Wait
Connected
Notes: End-host stores all flow state.
For TCP this is done per connection using a TCB (transmission control block)

## Slide 28: Example: SYN Flooding
C
S
SYNC1
Listening
Store data
SYNC2
SYNC3
SYNC4
SYNC5

## Slide 29: Protection against SYN Attacks
SYN Cookies
  Client sends SYN
  Server responds to Client with SYN-ACK cookie
    sqn = f(src addr, src port, dest addr, dest port, rand)
    Server does not save state
  Honest client responds with ACK(sqn)
  Server checks response
    If matches SYN-ACK, establishes connection
Drop Random TCB in SYN_RCVD state (likely to be attackers)
[Bernstein, Schenk]

## Slide 30: Distributed DoS (DDoS)
Attacker compromises multiple hosts
Installs malicious program to do her biding (bots)
Bots flood (or otherwise attack) victims on command; Attack is coordinated
Bot-networks of 80k to 100k have been seen in the wild
  Aggregate bandwidth > 20Gbps (probably more)
E.g. Blue Frog (by Blue Security)
Notes: Important to note what aspects of the Internet design make this problem
So difficult to solve
* Mention blue security!

## Slide 31: Blue Frog
Anti-spam tool:
  Persuade spammers to remove community members’ addresses from their mailing list
Users register: Do Not Intrude Registry, Firefox, and IE plugins
Automatic reports: ISPs, law-enforcement, …
Spammers attacked
  Intimidating e-mails
  DDoS attack to “Blue Security” web page
  Redirected to blogs.com  Collapse
  Attackers identified
Blue Security ceased its anti-spam operation.

## Slide 32: What About Downlink? (Flooding)
Assume attacker generates enough traffic to saturate downlink bandwidth.
What can the server do?
What can the network do?
  Ideally want network to drop bad packets
  How to tell if a packet is part of a legitimate flow? (requires per flow state?)
  Even harder, how to tell if a SYN packet is part of a legitimate request?
Is the phone network immune to such attacks?
Notes: Important to note what aspects of the Internet design make this problem
So difficult to solve

## Slide 33: DoS Aplenty
Attacker guesses TCP seq. number for an existing connection:
  Attacker can send Reset packet to close connection. Results in DoS.
  Most systems allow for a large window of acceptable seq. #’s
  Only have to a land a packet in
  Attack is most effective against long lived connections, e.g. BGP.
Congestion control DoS attack
  Generate TCP flow to force target to repeatedly enter retransmission timeout state
  Difficult to detect because packet rate is low
RTO
2*RTO
Congestion
Congestion
Congestion
Notes: DDoD is a catch phrase for …. Limiting access.

## Slide 34: Indirection Attacks
Rely on connecting to “end-points” to get content/access services
Unfortunately network end-points (e.g. IPs, DNS names) are loosely bound
Long history of problems

## Slide 35: Example: Fetching a Web Page
DHCP Request
Client
ARP request (name server/gateway)
DNS request
HTTP Request

## Slide 36: DNS Vulnerability
Users/hosts typically trust the host-address mapping provided by DNS

## Slide 37: Bellovin/Mockapetris Attack
Trust relationships use symbolic addresses
  /etc/hosts.equiv contains friend.stanford.edu
Requests come with numeric source address
  Use reverse DNS to find symbolic name
  Decide access based on /etc/hosts.equiv, …
Attack
  Spoof reverse DNS to make host trust attacker

## Slide 38: Reverse DNS
Given numeric IP address, find symbolic addr
To find 222.33.44.3,
  Query 44.33.222.in-addr.arpa
  Get list of symbolic addresses, e.g.,
    1 IN PTR server.small.com
    2 IN PTR boss.small.com
    3 IN PTR ws1.small.com
    4 IN PTR ws2.small.com

## Slide 39: Attack
Gain control of DNS service for evil.org
Select target machine in good.net
Find trust relationships
  SNMP, finger can help find active sessions, etc.
  Example: target trusts host1.good.net
Connect
  Attempt rlogin from coyote.evil.org
  Target contacts reverse DNS server with IP addr
  Use modified reverse DNS to say “addr belongs to host1.good.net”
  Target allows rlogin

## Slide 40: DNS Rebinding Attacks
Modern browsers implement the same-origin policy.
  Isolate distinct origins.
To attack:
  Subvert the same-origin policy
  Confuse browser to aggregate network resources.
DNS Rebinding Attacks:
  register a domain, e.g. attacker.com
  Answer DNS queries for attacker.com with your IP, short TTL, serve malicious JavaScript
  Script requests IP address of attacker.com, feed the IP of private server
  Read private information
Protecting Browsers from DNS Rebinding Attacks, In Proceedings of ACM CCS 07

## Slide 41: Solution – DNS Pinning
Once a hostname is resolved to an IP address, cache the result for a while
  Regardless of TTL
Plug-ins can cause problems

## Slide 42: TCP Connection Spoofing
Each TCP connection has an associated state
  Client IP and port number; same for server
  Sequence numbers for client, server flows
Problem
  Easy to guess state
    Port numbers are standard
    Sequence numbers (used to be) chosen in predictable way

## Slide 43: IP Spoofing Attack
A, B trusted connection
  Send packets with predictable seq numbers
E impersonates B to A
  Opens connection to A to get initial seq number
  SYN-floods B’s queue
  Sends packets to A that resemble B’s transmission
  E cannot receive, but may execute commands on A
Other ways to spoof source IP?
Server A
B
E
Notes: A lot of Internet security is based on the assumption of unpredictable sequence numbers.
Not always a great assumption (see BGP denial of service nonsence)
Go home and break linux’s sequence generator

## Slide 44: Reconnaissance/Misc
To attack a victim, first discover available resources
Many commonly used reconnaissance techniques
  Port scanning
  Host/application fingerprinting
  Traceroute
  DNS (reverse DNS scanning, Zone transfer)
  SNMP
These are meant for use by admins to diagnose network problems!
  Trade-off between the ability to diagnose a network and reveal security sensitive information
Notes: For host/application fingerprinting, mention SYN fingerprinting

## Slide 45: Anecdotes …
Large bot networks exist that scan the Internet daily looking for vulnerable hosts
Old worms still endemic on Internet (e.g. Code Red)
  Seem to come and go in mass
  Surreptitious scanning effort?
Notes: Ssh trolling

## Slide 46: Today
Network Security Goals
Security vs. Internet Design
Attacks
Defenses

## Slide 47: Firewalls
Keep out unwanted traffic
Can be done in the network (e.g. network perimeter) or at the host
Many mechanisms
  Packet filters
  Stateful packet filters
  Proxies, gateways

## Slide 48: Packet Filters
Make a decision to drop a packet based on packet header
  Protocol type
  Transport ports
  Source/Dest IP address
  Etc.
Usually done on router at perimeter of network
And on virtually all end-hosts today

## Slide 49: Packet Filters: Problem
Assume firewall rule (allow from port 53 and port 80)
Easy for an attacker to send packets from port 53 or 80
Further attacker can forge source
Not very effective for stopping packets from unwanted senders

## Slide 50: Stateful Packet Filter
Idea: Only allow traffic initiated by client
  For each flow request (e.g. SYN or DNS req) keep a little state
  Ensure packets received from Internet belong to an existing flow
  To be effective must keep around sequence numbers per flow
Very common, used in all NAT boxes today
  Stateful NATs downside: failure  all connection state is lost!

## Slide 51: Proxies
Want to look “deeper” into packets
  Application type
  Content
Can do by reconstructing TCP flows and “peering” in, however this is really hard
  (Digression next slide)

## Slide 52: Passive Reconstruction of TCP Stream
Use passive network element to reconstruct TCP streams
“Peer” into stream to find harmful payload (e.g. virus signatures)
Why is this really hard?
Notes: Open up question to the class, can anyone tell me why this is really hard?

## Slide 53: Reconstructing Streams
Must know the client’s view of data
  Have to know if packet reaches destination (may not if TTL is too short)
  Have to know how end-host manages overlapping TCP sequence numbers
  Have to know how end-host manages overlapping fragments
End host
router
X
TTL = 0

## Slide 54: Proxies
Full TCP termination in the network
Often done transparently (e.g. HTTP proxies)
Allows access to objects passed over network
  E.g. files, streams etc.
Does not have same problems as stream reconstruction
Plus can do lots of other fun things
  E.g. content caching

## Slide 55: Proxy Discussion
Proxies duplicate per-flow state held by clients
How does this break end-to-end semantics of TCP?
  E.g. what if proxy crashes right after reading from client? (lost data!)
How to fix?
  Lots of work in this area

## Slide 56: Final Comments
Internet not designed for security
Many, many attacks
  Defense is very difficult
  Attackers are smart; Broken network aids them!
Retrofitting solutions often break original design principles
  Some of these solutions work, some of the time
  Some make the network inflexible, brittle
Time for new designs/principles?